## Slide 1: Doppler
Doppler Effect
  Vector Formulation
Doppler Simulation
  Doppler Simulation via Delay Lines
  Time-Varying Delay-Line Reads
  Variable Delay Line in Software
  Multiple Read Pointers
  Multiple Write Pointers
  Stereo Processing
  System Block Diagram

## Slide 2: Doppler Movie

## Slide 3: Stationary Sound Source
Sound waves produced at constant frequency f0
Wavefronts propagate symmetrically away from source at constant speed c
  speed of sound in the medium
Distance between wavefronts is wavelength
All observers hear same frequency
  Equal to actual frequency of source

## Slide 4: Source moving with vsource<c (Mach 0.7)
sound source radiating sound waves at a constant frequency
sound source moving to right with speed vs=0.7c (Mach 0.7)
source movingcenter of each new wavefront slightly displaced to right
wavefronts bunch up on right side (in front) of source
spread further apart on left side (behind) of source
observer in front of source hears higher frequency f ´ > f0
observer behind source hears lower frequency f ´ < f0

## Slide 5: Source moving with vsource=c
source moving at speed of sound in medium (vs =c, or Mach 1)
speed of sound in air at sea level ~ 340m/s or 750 mph
wavefronts in front of source now all bunched up at same point
observer in front of source will detect nothing until source arrives
pressure front will be quite intense (a shock wave), due to all wavefronts adding together
  not perceived as pitch but as thump of sound as pressure wall passes by

## Slide 6: Mach 1 - breaking the sound barrier
Jet pilots flying at Mach 1 report noticeable wall or barrier which must be penetrated before achieving supersonic speeds
wall due to intense pressure front
flying within this pressure front produces very turbulent and bouncy ride
Right combination of conditions and events can occur to create an unbelievable event
  F/A-18 Hornet passing through the sound barrier
   exact instant it goes supersonic
water vapor, density and temperature just right
Navy Ensign John Gay made this phenomenal photograph on July 7, 1999 while aboard carrier USS Constallation as Navy Lt. Ron Candiloro flew by.
plane in transonic flight
  normal shock waves emanating from behind the canopy and across wings and fuselage
condition will last for only an instant
once supersonic flow exists completely around the aircraft, sharp-angled sonic cones replace the normal shock waves
Credit: US Navy photo by John Gay, public domain

## Slide 7: Source moving with vsource>c: Mach 1.4 - supersonic
sound source broken sound speed barrier
traveling at 1.4 times the speed of sound (Mach 1.4)
source moving faster than sound waves it createsleads advancing wavefront
source will pass by observer before observer actually hears sound it creates
angle of Mach cone depends on ratio of source speed to sound speed
intense pressure front on Mach cone causes shock wave, sonic boom, as supersonic craft passes
shock wave advances at speed of sound c
it is built up from all of combined wave fronts
  sound heard by an observer will be quite intense
supersonic aircraft usually produces 2 sonic booms
  one from the aircraft's nose and other from its tail
  resulting in a double thump
bullet travelling at Mach 2.45
  Mach cone and shock wavefronts are very noticeable

## Slide 8: Doppler Effect
Doppler shift
  apparent change in acoustic frequency content of sound source due to motion of source relative to listener
  as sound-source moves toward you, pitch is raised
  as it moves away from you, pitch is lowered
Doppler effect
  causes pitch of sound source to appear to rise or fall due to motion of source and/or listener relative to each other
  enhance realism of simulated moving sound sources for compositional purposes
Doppler shift given by
  ws - frequency emitted by source at rest
  wl - frequency received by listener
  uls - listener speed relative to propagation medium in direction of source
  usl - source speed relative to propagation medium in direction of listener
  c - sound speed
all quantities are scalars
But this is an approximation!

## Slide 9: Moving source emits a sound at time t, which is heard by a moving listener at time t.
At time t, source located at xs(t), moving at velocity vs(t), emits a sound
At time t, listener located at xl(t), moving at velocity vl(t), hears this sound
xl(t)
xs(t)
vs(t)
vl(t)
vsl(t)
Vls(t)

## Slide 10: Vector Formulation
- 3D position
- time source emits sound
- time listener receives sound
- position of source at time t
- position of listener at time t
- sound-source velocity
- velocity of listener
Consider Fourier component of source at frequency ws
  Want shifted ws, wl, at listener
Doppler depends on velocity components along line connecting source & listener

## Slide 11: Useful vector properties
Unit vector in the direction of
Scalar projection of onto vector is
Derivative of the magnitude of a vector
  Dot product of velocity and unit length direction vector

## Slide 12: Derivation of Doppler
At time t, listener hears sound produced at some previous time t, so
Consider time derivative of this
  Note t depends on time t, since a small change in t must come from sound being produced at a different time t.
  has instantaneous phase f=wst and instantaneous angular frequency . We need to find the new instantaneous angular frequency

## Slide 13: Derivation of Doppler
Recall: derivative of magnitude of a vector
But
So
  Rearranging terms, and writing time dependence,

## Slide 14: Simplifications
Stationary listener:
Stationary source:
:
One dimensional:
<<

## Slide 15: Backwards Sound
Source moves in straight line towards listener at constant speed 2c. For frequency f emitted by the source, what does the listener hear?
Treat listener as fixed at 0, and source at a negative position (xs<0) with positive velocity. Doppler equation becomes
What does it mean to have negative frequency?
  Suppose at time 0 source at position –d.
  Sound emitted at time 0
    Arrives at listener at time t =d/c.
  2. Sound emitted at time T.
    Source first travels at speed 2c for time T, then emits sound which travels rest of the distance, d=2cT+c(t-T)=cT+ct
    Arrives at listener at time t= d/c-T.
   Thus a sound emitted T later will arrive at the listener T earlier.
    So listener hears the sound backwards

## Slide 16: Vector Formulation Example
Projected source velocity at t=0
  Perceived frequency ~ 1.013
Projected source velocity at t=1
  Perceived frequency ~ 1.010
Projected source velocity at t=2
  Perceived frequency ~ 1
Projected source velocity at t=3
  Perceived frequency ~ 0.9898
2D
Stationary listener
Source moves 5m/s
Closest distance is 5m
Away from listener

## Slide 17: Doppler Simulation
time-varying delay line results in frequency shift
  Use for precise Doppler simulation
Consider Doppler shift from physical point of view
  air analogous to magnetic tape which moves from source to listener at speed c
  source analogous to write-head of tape recorder
  listener corresponds to read-head.
  When source and listener fixed
    listener receives what source records
  When either moves
    Doppler shift observed by listener, according to

## Slide 18: Doppler Simulation via Delay Lines
works for delay-line based computational model
  magnetic tape is delay line
  tape read-head is read-pointer of delay line
  write-head is delay-line write-pointer
modulating delay by changing read-pointer increment from 1 to 1+vls
  requires interpolated reads
  corresponds to listener motion away from the source at speed uls
changing write-pointer increment from 1 to 1+vsl
  use interpolating writes (de-interpolation) into delay memory
  corresponds source motion toward listener at speed usl

## Slide 19: Time-Varying Delay-Line Reads I
If x(t) denotes input to time-varying delay,
  output written as y(t)= x(t-Dt)
Dt - time-varying delay in seconds
  In discrete-time, Dt not integer multiple of sampling interval
  y(t) approximated (in finite band) using bandlimited interpolation or other techniques for fractional delay
set x(t) to complex sinusoid at frequency ws:
output now
instantaneous phase of this signal is
differentiate for instantaneous frequency

## Slide 20: Time-Varying Delay-Line Reads II
delay growth-rate equals relative frequency downshift:
Recall
time-varying delay simulates Doppler shift with
Assume moving listener only
Delay growth-rate set to speed of listener away from source, normalized by sound speed

## Slide 21: Simple delay line
float *delayData; // circular delay buffer of audio samples
int delayBufLength; // Length of delay buffer in samples
int writePointer; // Write location in delay buffer
float readPointer; // Read location in delay buffer
// Set delay in number of samples, by finding read pointer relative to write pointer
void setDelay(float delayLength)
{
readPointer = writePointer - delayLength;
while(readPointer < 0) readPointer += delayBufLength;
}
//Process samples in channelData, put output in same buffer input came from
void process(float *channelData, int numSamples)
{
for (int i = 0; i < numSamples; ++i)
{
float in = channelData[i];
float out = delayData[readPointer];
// Store current sample in delay buffer
delayData[writePointer] = in;
// Increment pointers.
if (++writePointer >= delayBufLength) writePointer = 0;
if (++readPointer >= delayBufLength) readPointer = 0;
// Store output sample in buffer, replacing input
channelData[i] = out;
}
}

## Slide 22: Variable Delay Line in Software
delayBufLength Buffer of size
delayLength variable delay line in C
  Require delayLength <= delayBufLength.
use linear interpolation
out = delayData[readPointer];
replaced with
sampleBefore = floor(readPointer);
sampleAfter = (sampleBefore + 1);
Offset = readPointer - sampleBefore;
out = (1 - Offset) * delayData[sampleBefore] + Offset * delayData[sampleAfter];
Continuously varying delay
  add delay growth parameter D to delayline function
++readPointer;//pointer update
changed to
readPointer+= 1-D;//pointer update
  D=0, fixed delay line
  D>0, delay grows g samples per sample
    interpret as seconds per second, i.e.,
Need to simulate listener traveling toward source at speed

## Slide 23: Code example
// Variables used in this example whose values are set externally:
float *delayData; // Our own circular delay buffer of audio samples
int delayBufLength; // Length of our delay buffer in samples
int writePointer; // Write location in the delay buffer
float readPointer; // Read location in the delay buffer
// User-adjustable effect parameters:
float delta_; // Derivative of delay time
//Set delay in fractional number samples by finding read pointer relative to write pointer
void setDelay(float delayLength)
{
readPointer = (float)writePointer - delayLength;
while(readPointer < 0) readPointer += (float)delayBufLength;
}

## Slide 24: Code example
//Process group of samples in channelData, putting output in same buffer input came from
void process(float *channelData, int numSamples)
{
for (int i = 0; i < numSamples; ++i)
{
const float in = channelData[i];
float out = 0.0;
int sampleBefore = floor(readPointer);
int sampleAfter = (sampleBefore + 1) % delayBufLength;
float fractionalOffset = readPointer - (float)sampleBefore;
// Calculate output using linear interpolation between samples before and after
float out=(1 – fractionalOffset)*delayData[sampleBefore]
+ fractionalOffset *delayData[sampleAfter];
delayData[writePointer] = in; // Store current sample in delay buffer
//Increment pointers.Write pointer is integer so will wrap around strictly to 0
// read pointer is fractional so may wrap around to a fractional value
if(++writePointer >= delayBufLength) writePointer = 0;
readPointer += 1.0 - delta_;
if(readPointer >= delayBufLength) readPointer -= (float)delayBufLength;
// Store the output sample in the buffer, replacing the input
channelData[i] = out;
}
}

## Slide 25: Variable Delay Line in Software
Model of physical propagation-path geometry
   read- and write-pointers separated by predictable minimum & maximum delay intervals
    unnecessary to worry about read-pointers passing write-pointers
    unnecessary to worry about write-pointers passing read-pointers
Other cases
  Generic frequency shifters
    Time and pitch scale modification
  Doppler simulator not driven by changing geometry
  read- and write-pointers may get too close to each other
    read pointer will eventually ``catch up to'' or ``fall back into'' write pointer location
    discontinuity issues caused when read and write pointers cross
    pointer cross-fade scheme may be necessary

## Slide 26: Multiple Read Pointers
Used to simulate multiple listeners
Each read-pointer signal can be filtered to simulate
  propagation losses
  radiation characteristics
of source in direction of listener
Read-pointers can move independently to simulate different Doppler shifts associated with
  different listener motions
  relative source directions

## Slide 27: Multiple Write Pointers
If write pointers at fixed spacing
  equivalent to multiple read pointers
  provide basic multipath simulation
If write pointers moving independently
  induce independent Doppler shifts due to source motion
  each write-pointer represent signal from separate source to single listener
  each write-signal can be passed through its own filter
  implement all filtering on propagation path from source to listener
all write pointers have same input signal
  their filters can be implemented using series chain
  outputs of successive filters correspond to progressively longer propagation paths
    progressively more filtering
  reduce filter order required for propagation paths longer than shortest
  all but first write-pointer simply sum into shared delay line
  write-pointers may cross each other with no ill effects

## Slide 28: Multiple Write Pointers
single delay line simulates many moving listeners or many moving sources
many moving listeners and many moving sources
  different listeners do not see same Doppler shift for each moving source
  listener's read-pointer motion can be adjusted to correct for Doppler shift seen from any particular source
    cannot correct for more than 1 in general
   Not possible to share a single delay line
    need as many delay lines as there are sources or listeners, whichever is smaller
    N moving sources, M moving listeners  min(N,M) delay lines

## Slide 29: Delay line with multiple read and write pointers, corresponding to multiple sources and listeners.
Delay line
Listener1
Listener 2
Source1
Source2
Source3
Write pointers
Read pointers

## Slide 30: Stereo Processing
Stereo processing of many sources accomplished using 2 delay lines
  corresponding to left and right stereo channels
stereo mix may contain panned mixture of many sources, each with
  stereo placement
  path filtering
  Doppler shift
2 stereo outputs may correspond to
  ``left and right ears,'' or
  left- & right-channel microphones in studio recording set-up

## Slide 31: Sound Example I
stationary observer & moving sound source
  or stationary source & moving observer
source moving on straight line passing through observer
Initial distance from source to observer s=30 m
velocity of source v=6 m/s

## Slide 32: Sound Example I

## Slide 33: Sound Example II
stationary observer & moving sound source
source moves on straight line some minimum distance from observer
  Initial distance from source to observer s=30 m
  Velocity of source v=6 m/s
  Minimum distance d=5m

## Slide 34: Sound Example II

## Slide 35: Sound Example III
3 tone signal
stationary observer
moving sound source
source moves on line some minimum distance from observer
  Initial distance from source to observer s=30 m
  Velocity of source v=6 m/s
  Minimum distance d=5m

## Slide 36: Leslie speaker
Stationary
listener
Moving
loudspeaker
horn
Moving loudspeaker and stationary listener,