## Slide 1
Reverberation modelling – mechanical, physical and room models

## Slide 2: Reverb modeling
Physical
  Reverberation chambers
Mechanical & physical
  Reverberation chambers
  Spring reverb
  Plate reverb
Room modeling
  Ray tracing, Beam tracing, Finite boundaries
  Image source method

## Slide 3: Reverberation chambers
Studios use rooms to add reverb to recordings
Elevator shafts and stairwells work as highly reverberant environments
Reverb controlled by adding some absorptive materials
  Curtains can be drawn across more reflective surfaces

## Slide 4: Spring Reverbs
used in Hammand organs and many guitar amplifiers
Spring enclosed in metal box, reverb pan
  pan takes audio and produces reverberated version
  mixed with dry signal
transducer converts energy in one form to another
  Spring driven at one end by input audio signal
    Electrical energy converted to mechanical energy
  Pickup records vibrations on other end of spring
    Mechanical energy back to electrical energy
  other transducers are pickups on guitar, microphones, speakers..
Waves travel and reflect through spring
When wave arrives at end, part of wave energy reflected and stays in spring
  reflections create reverb characteristic sound

## Slide 5: Spring Reverb Implementation
Often several springs used together
Each spring different length or different tension to avoid uniform behavior in single spring
  reflections occur at different times
  increases 'randomness' of echoes
  spring lengths & tensions are usually fixed in design process, and not left to user to control
spring reverbs sensitive to motion
  If you drop amplifier, hear twangy, spring-like sound
  results when springs hitting case or other springs

## Slide 6: Plate Reverb
not used widely outside of studio
  expensive and bulky
similar to spring reverb
  instead of connected to springs, 2 or more transducers
connected to different points on metal plate.
  Transducers send vibration waves throughout plate
  Reflections occur each time wave reaches edge of plate
reverberation controlled by adjusting damping of plate
and location of transducers

## Slide 7: Other methods
many ways to create reverb effects
  not used often
tape based reverb units.
  inherently periodic behavior due to tape loop
  multiple playback heads used to disguise this
Other acoustical structures can be used
  pipes with microphones placed at various points
interesting to create and use
difficult competing against digitally based reverbs as far as simplicity and ease

## Slide 8: Modelling room reverberation
Inputs include
  Geometry of room
  Sound source location
  Listener location
Algorithms model specific room properties
  Ray tracing techniques
    follow paths of sound waves
  Beam tracing
    Trace beams (bundles of rays) from sources
  Boundary elements methods
    Solve wave equations over surfaces
  Image source method

## Slide 9: Image source method
Source
Microphone
Virtual source
A room with source sound and microphone, and its mirror image containing a virtual source

## Slide 10: Image source method
room with multiple mirror images in two dimensions
corresponding to reflections of sound source off of the walls

## Slide 11: Image source method
circle drawn to indicate virtual sources used for early reflections