## Slide 1
Reverb

## Slide 2: What is reverberation?
Series of delayed and attenuated sound waves
  Result of many reflections within a space
Multiple paths from a source to our ears
  Direct path
    Strongest and first
  Reflected paths, bouncing off walls or ceiling
    Weaker and arrive later
Creates spaciousness of a room
Source
Microphone

## Slide 3: Reverb, echo and delay
Reverb is not just a series of echoes
  Echo: distinct, delayed version of sound
    Delay more than 0.1-0.2 seconds
  Reverb: many closely-spaced copies of a sound
    Do not perceive reflections as echoes
    But overall effect is highly audible
Delay with feedback does not produce reverb
  Delay: reflections with fixed time interval
  Reverb: rate of reflections changes over time
    Greater spacing of initial reflections, closer spacing later

## Slide 4: Early reflections
Early reflections
  Short period after direct sound
  Set of well-defined and directional reflections
  Directly related to;
    size and shape of room
    position of source and listener
Late reflections
  Diffuse reverberation
    Density greatly increases
    More randomly spaced
  Follows early reflections
  Difficult to relate to physical characteristics of room
  Major factor establishing room size
    decays exponentially in good concert halls

## Slide 5: Late reflections
Diffuse reverberation
  Density greatly increases
  More randomly spaced
Follows early reflections
Difficult to relate to physical characteristics of room
Major factor establishing room size
  decays exponentially in good concert halls
Notes: After the early reflections, the rate of the arriving reflections increases greatly. These reflections are more random and difficult to relate to the physical characteristics of the room. This is called the diffuse reverberation, or the late reflections. It is believed that the diffuse reverberation is the primary factor establishing a room's 'size', and it decays exponentially in good concert halls. A simple delay with feedback will only simulate reflections with a fixed time interval between reflections.

## Slide 6: Impulse response
Series of scaled delta functions
Each vertical line marks when sound heard again
  represents delayed, attenuated copy of sound
Height of lines represents how loud sound is at that time
What would simple feedback delay look like?
Early
Reflections
Late
Reflections
Time

## Slide 7: Correlation
For stereo reverb, correlation of signals reaching each ear is important
Gives sense of spaciousness
low ceiling
  First reflections from ceiling (not walls)
  reach both ears at the same time
  Coherent reflections give sense of small space
high ceiling
  First reflections from walls
  Walls are different distances away
    path different for each ear
  Sound arriving at each ear is different (incoherent)
    Not strongly correlated

## Slide 8: Reverberation time
Characterises reverberation in room
  Important overall metric of reverb
Reverberation time (RT60)
  Time for sound pressure level to decay to 10-6 (60 dB) original value
  10-3 original amplitude
Long reverberation times
   sound energy stays in room longer before being absorbed
Associated with room size
  Concert hall reverberation time~ 1.5 - 2 seconds

## Slide 9: Reverberation time: factors
Room surfaces
  How much energy lost on each reflection
  Reflective materials increase reverberation time
    concrete, tiles, ...
  Absorptive materials reduce reverberation time
    curtains, carpet, people, ...
  Absorptivity varies with frequency
Room size
  Larger rooms have longer reverberation times
    Longer distance for waves to travel between reflections
Air in the room
  Air attenuates travelling sound waves, reducing reverb time
  Attenuation varies with humidity and temperature
    High frequencies affected most
    Many reverb units thus include lowpass filters

## Slide 10: Sound example
Reverb is omnipresent so we often ignore it
listen after short, impulsive sounds, while sound still bouncing around
  clap your hands
Sound without processing (dry sound), followed by same sound with reverb added Listen just after accented notes
Notes: Since we are so accustomed to hearing reverberation, we often have to specifically listen for it in order to notice it. Probably the best way to notice reverb is to listen after short, impulsive sounds, while the sound is still bouncing around. If you want to test out the reverb in various rooms of your house or apartment, clapping your hands works pretty well. Sound example 1 presents a dry sound (no reverb) and the same line with reverb added. Listen just after the accented notes.

## Slide 11: Sabine equation
Sabine equation can estimate reverberation time in a room:
  V = volume of room (m3)
  c = speed of sound in air (343 m/s)
  S = total surface area of room (m2)
  = average absorption coefficient for room
  Where ai are individual absorption coefficients for each surface Si

## Slide 12: Absorption and reverberation time
Example coefficients for various room surfaces:
Reverberation time differs by frequency band
  1000Hz band
    2.6 seconds for an empty room
    0.93 seconds for room with carpet
Frequency (Hz) | 125 | 250 | 500 | 1000 | 2000 | 4000
Concrete block, painted | 0.10 | 0.05 | 0.06 | 0.07 | 0.09 | 0.08
Concrete floor | 0.01 | 0.01 | 0.015 | 0.02 | 0.02 | 0.02
Carpet on concrete | 0.02 | 0.06 | 0.04 | 0.37 | 0.60 | 0.65
Carpet on foam rubber | 0.08 | 0.24 | 0.57 | 0.69 | 0.71 | 0.73

## Slide 13: Absorption and reverberation time
Composite photographs of an empty room:
Composite photograph of same room with carpet:
Hand Clap (room empty)
Hand Clap (with carpet)
Speech (room empty)
Speech (with carpet)

## Slide 14: Measured reverberation time
Hand clap samples
  Red shows empty room
  Black shows carpeted room
Based on 1000Hz plot
  RT60= 3.3s empty, 1.6s carpet
Measured > Sabine equation
  Cavities in ceiling trap sound
  Sabine assumes uniform distribution of absorption
1000Hz
2000Hz
500Hz

## Slide 15: Direct and reverberant sound fields
Direct field: source sound louder than reflections
Reverberant field: SPL from reflected sounds greater than direct sound
Depends on distance from source
Critical distance
  point where direct and reflected sounds are equal in volume
Reverberant fields are highly important
  Most listening situations are reverberant fields
  Reverb keeps sound energy localised in a room
    raising overall SPL and distributing sound
  Outdoors, reflective surfaces missing and energy lost

## Slide 16: Reverberant fields in music
Reverberant field distributes sound more evenly in space
  Helps hear all instruments in an ensemble
    Some instruments are farther away than others from audience
    Many instruments are highly directional in their radiation
    In direct field, violin sounds different as you move around
      Less true in a reverberant field which spreads energy around
  Large reverberation time makes it difficult to understand speech or follow musical lines
The ideal direct field: anechoic chamber
  Room designed to have no reflections

## Slide 17: Why use reverb?
Why add artificial reverb to recorded sound?
  Dry signals (e.g. close mic) sound unnatural
  Compensate for non-reverberant listening environment
    Headphones have no natural reverb
    Car or small room might not have sufficient reverberance to recreate sound of orchestra in concert hall
Can add natural reverb by recording in large room
  Distant microphones capture ambience as well as direct signal
  Impractical in many situations
   Add reverb synthetically

## Slide 18: Signal processing methods
Algorithmic reverb
  Early algorithms used two types of IIR filters
    Comb filter: regular notches in frequency response
    Allpass filter: change phase but pass frequencies equally
    Goal to mimic reflections within a room, especially gradual decay of later reflections
Convolutional reverb
  Convolve a signal with a known impulse response
  Many techniques using circular buffers and delay lines
Hybrid methods

## Slide 19: Schroeder’s reverberator
Early reverb work by Manfred Schroeder (1960s)
One Schroeder design:
  4 comb filters
  2 allpass filters
  Basic simulation, but lacks important features
    Increasing arrival of later reflections
    Not as effective as modern algorithms

## Slide 20: Schroeder’s reverberator
d
x[n]
y[n]
g
+
(b)
+
d
x[n]
y[n]
g
+
-g
1-g2
(a)
Schroeder’s comb filter
A Schroeder allpass section. Typical value for g is 0.7

## Slide 21: Moorer’s reverberator
J. A. Moorer. About this reverberation business. Computer Music Journal 3(2):13-18, 1979
  FIR filter simulates early room reflections
    Also consider as a tapped delay line (19 taps)
  In cascade with a bank of comb filters
  FIR filter coefficients from Moorer’s article
    Based on geometric simulation of Boston Symphony Hall
  Comb filters have unusual gain parameters
    Include a lowpass filter in the feedback loop
    Simulates absorption of high frequencies by the air
  All-pass filter with group delay 6ms at DC & gain 0.7

## Slide 22: Moorer’s reverberator
LP Comb
LP Comb
LP Comb
LP Comb
LP Comb
LP Comb
Allpass
+
z-d
+
Early reflections
Late reflections
X(z)
Y(z)
+
z-d1
c1
z-d2
c2
z-dn
cn
z-d3
c3
…
FIR filter to simulate early reflections
Parallel comb filters with low pass filtering to simulate the late reflections

## Slide 23: Moorer’s reverberator
6 parallel comb filters with different delay lengths
  Simulate modes of a room
  Sound reflecting between parallel walls
Allpass filter to increase the reflection density
  Avoid flutter echoes (rapid echo of even rate)
Lowpass filters in feedback loops
  Alter reverberation time as a function of frequency
  Different in each comb filter because their coefficients depend on delay line length
Last delay block
  Used to delay late reflections compared to early ones

## Slide 24: Flutter Echoes
Output of single comb filter has distinct periodicity
  distances between adjacent echoes decided by single delay parameter
Flutter echo - rapid multiple echo of even rate
Moorer’s Reverberator
  To avoid periodicity, several comb filters with co-prime delays in paralleled

## Slide 25: Examples
Concert hall simulation, RT60 = 3.0s
Concert hall simulation, RT60 = 0.4s
Some clicking, or something squishy can be heard during the word sitting
Amplitude
0
0.05
0.1
0.15
-0.6
-0.4
-0.2
0
0.2
0.4
0.6
0.8
1
Time (s)
Impulse Response for Moorer’s Reverberator,
RT60=0.4s
Notes: Some clicking, or something sounds decidedly “squishy” can be heard during the word “sitting”.
Examples:
Concert hall simulation, RT60 = 3.0s
Concert hall simulation, RT60 = 0.4s
The figure below shows the impulse response of Moorer’s reverberator. Note the discrete early reflection times in the first 50 ms, which are followed by the comb filter activity.

## Slide 26: Modelling room reverberation
Algorithms can model specific room properties
  Ray tracing techniques (follow paths of sound waves)
  Inputs include
    Geometry of room
    Sound source location
    Listener location
Filters used
  Finite impulse response (FIR) filter for early reflections
  Infinite impulse respond (IIR) filters for later, diffuse reverberation
  Low pass filters for modelling air absorption
  Can get complicated very quickly

## Slide 27: Convolution Reverb
Reverb completely characterised by impulse response
  It is a linear, time-invariant (LTI) effect
Suppose we have impulse response of a room
  Record impulse (like popping balloon) with microphone in one location, sound source in another location
Apply reverb by convolving signal with recorded impulse response
  Makes it sound as if it is in the space

## Slide 28: Convolution reverb
Naive convolution is very computationally expensive
Real impulses can be 3+ seconds long
  At 44.1kHz, 3 seconds = 132300 samples
  Like applying a 132300-coefficient FIR filter!
  Can’t be done in real time. So what do we do?
Implement convolution as multiplication in frequency domain
  Break the signal into blocks; take FFT of each block
  Blocks overlap; know as the overlap-add process
    Same as the phase vocoder
Problem: how long of an FFT to use?
  As long as the impulse?
  Latency will be at least 3 seconds. Not usable!
  Also, not very efficient
  Several possible solutions involving groups of smaller FFTs

## Slide 29: One block convolution
N N
h zeros
SkN:(k+1)N-1 zeros
FFT
FFT
X
IFFT
r
2N

## Slide 30: Partitioned convolution for real-time artificial reverberation.
r
h
s0:N-1*h
h
h
h
s0:N-1
sN:2N-1
s2N:3N-1
s3N:4N-1
sN:2N-1*h
s2N:3N-1*h
s3N:4N-1*h
…
…
…
…
…
…
…
Sum end of previous convolution and beginning of current convolution
{
Convolve impulse response and the current block
{
s

## Slide 31: Common parameters
Parameters vary by unit, type of implementation
Common parameter: reverb decay
  How quickly the reverberant sound fades
  Exact measurement varies by manufacturer
  Usually measured in milliseconds
  Like reverberation time for a room
Predelay = how long before first reflections sound
  Some units allow control of both early and late reflections
Predelay 1
Predelay 2
Time

## Slide 32: Gated reverb
Truncate impulse response of reverb unit
  Like changing IIR filters to FIR
  Alternately, only allow a finite number of reflections
  Commonly used on drums
Gate time
  Amount of time sound can reverberate
  Sometimes an abrupt silence
  Some units allow a gradual decay
Alternatively, gate threshold
  Similar to noise gate threshold
  Stop reverb when it falls below a certain level
Gate Time
Time

## Slide 33: Reverse reverb
Reverse reverb simulates reflections where sound gets louder over time, then cuts off
  Opposite of natural effect where reflections become quieter
  Reverse time or gate time = how long sound builds up
  Similar to gated reverb reversed in time
  May sound like slapback delay since it ends suddenly
  Sound example: dry, 50ms reverse time, then 150ms
Reverse Time
Time

## Slide 34: Software I
CoolEdit Pro
  Standard Reverb settings

## Slide 35: Software II
Renaissance Reverberator by Waves
  Highshelf and Lowshelf EQs for
    Damping(left)
    final output(right)
  upper middle display depicts
    Early Reflections placement and level
    Reverb portion start and fading
  Above this display is Reverb Type selector
    changes placement & level of Early Reflections
    Size slider has influence on Early Reflections as well