## Slide 1
Graphic EQ

## Slide 2: Tone controls
Most common equalisation is the tone control
  Controls: bass and treble
  Adjust sound to suit your taste, or the room
  Bass control = lowpass shelving filter
  Treble control = highpass shelving filter
  Control centred = unity gain = flat response
Boost
Cut
Boost
Cut

## Slide 3: Tone controls
Compare shelving filters to standard lowpass and highpass filters
  Most filters try to completely remove low or high frequencies
  Here, just want to boost or cut a portion
0
p
wc
|H|2
1
Low-pass
|H|2
0
p
1
wc
High-pass
0
p
wc
|H|2
1
G
Low Shelving Filter
|H|2
0
p
1
wc
G
High Shelving Filter
Cutoff frequency
  Where response changes between 2 levels
  Can design adjustable cutoff as well as level

## Slide 4: Tone controls - Midrange
In addition to bass and treble, midrange control
Affects frequencies between highs and lows
boost or cut portion of spectrum without affecting the rest
Does not attempt to isolate particular frequencies
Rarely, adjustable center frequency
  Where gain is at maximum (or minimum)
Boost
Cut

## Slide 5: (a) Bass and treble tone controls implemented as a low shelving filter and high shelving filter placed in series. (b) Three tone controls, including a peaking/notch filter to adjust the midrange.
Bass
Treble
x[n]
High shelf
Low shelf
y[n]
Bass
Mids
x[n]
Peaking/ notch
Low shelf
y[n]
Treble
High shelf
y[n]
(a)
(b)

## Slide 6: Tone controls - Summary
2 or 3 controls: bass, mid, treble
Implemented with shelving and peaking filters
Filters connected in series
Able to adjust level of each section
Sometimes but rarely, adjustable cutoff frequencies
Q is usually fixed

## Slide 7: Presence and loudness
Some amplifiers have a presence knob as part of tone controls
  Boosts mid-to-high frequencies, 2-6kHz
  Alter recorded instrument’s sound to give sense of presence in the room with listener
  Can help an instrument stand out more in a mix
Many amplifiers also have a loudness control
  Louder? Isn’t this the volume knob?

## Slide 8: Loudness
Human hearing is nonlinear
  Perceived loudness depends on frequency as well as SPL
Loudness control designed for listening at low volume
  Boost bass and treble to simulate higher-volume listening
90 phon- top curve
10 phon- bottom curve
Each curve represents Sound Pressure Level (SPL) required for listener to perceive constant loudness when presented with pure tones across frequency range

## Slide 9: Speakers and crossovers
Hard to design speaker/cabinet with flat response over the whole audio range
  Need more than one speaker to cover whole range
Send specific frequencies to each speaker
  Tweeters can be damaged by low frequencies
  Woofers sound terrible at high frequencies
Use a crossover to separate frequencies
Tweeter (high freq.)
Midrange (mid freq.)
Woofer (low freq.)

## Slide 10: Speakers and crossovers
Crossover - network of filters that splits audio into components for each speaker
In 2-way (woofer and tweeter) system
  Lowpass for woofer
  Highpass for tweeter
  Same cutoff frequency for both
  Often use Butterworth filters (maximally flat freq. resp.)
  Not shelving type filters
In 3-way system
  Lowpass, bandpass, and highpass
    Can be implemented with lowpass, then lowpass and highpass
  Two relevant cutoff frequencies

## Slide 11: A loudspeaker crossover
Low pass filter
x[n]
yLP[n]
Woofer
Tweeter
yHP[n]
High pass filter
Low pass filter
x[n]
yLP[n]
Woofer
Tweeter
yHP[n]
High pass filter
Low pass filter
High pass filter
Midrange
yBP[n]
(a)
(b)
Separates the signal into different frequency bands that the various speakers can handle
2-way (a) and 3-way (b) loudspeaker crossovers are depicted

## Slide 12: Equalisation
Definition
  Boosting or cutting certain frequency components in a signal
Equalisation (EQ) is a form of filtering
  Filters are class of systems that change magnitudes and phases of input signal in a frequency-dependent manner
  Usually linear and time-invariant
Origin
  Trying to obtain flat frequency response
  No colouration
Example
  Transmitting analogue voice signal over long distance
  Transmission line attenuates high frequencies
  Apply equalisation filters to correct loss, resulting in more natural sound on the other end

## Slide 13: Introduction
Graphic equalisers let user set gains for fixed frequency bands
  Gain of each band generally controlled with slider
Band distribution is logarithmic in frequency
  Matches human perception
  Common designs include 1-octave and 1/3-octave bands
In live performance, delay can be a concern
  Every audio device needs lowest possible latency
  Use recursive (IIR) filters instead of FIR
  General IIR filter design is computationally expensive
  Equaliser implemented as collection of sub-filters, each of which affects one band only

## Slide 14: More on graphic EQ
More flexible than tone control
  More frequency bands available
    6 to 40 bands is typical range
  Like tone controls, centre frequencies are fixed
Boost or cut controlled with sliders
  slider positions represent samples of magnitude response at different frequencies
  Give ‘graphic’ representation of frequency response
Use in sound reinforcement and tuning rooms
  Achieve flat frequency response for sound system
    Resonances of room/speakers can colour sound
    Counteract coloration with graphic equaliser
  At instrument level, stomp-box equalisers provide both volume boost and tone change for soloing

## Slide 15: Graphic Equalisers and sliders
Manipulate each frequency band independently by inserting gain control
sliders on front of equaliser are gain controls in each band

## Slide 16: Graphic EQ and octaves
Centre frequencies usually equally spaced in octaves
  Logarithmic, not linear, in frequency
  octave is factor of 2 (or 21)
  1/3 octave spacing based on factor of 21/3 ~ 1.26
Examples
  1 octave spacing starting at 100Hz would have...
    200Hz, 400Hz, 800Hz, 1.6kHz, ...
  1/3 octave spacing starting at 100Hz would have...
    126Hz, 159Hz, 200Hz, 252Hz, 318Hz, 400Hz, ...
  ISO standard for preferred frequencies to use

## Slide 17: Parallel implementation
Consider as bank of bandpass filters
  Completely isolate individual frequency bands
  Real bandpass filters may have ripple in passband and don’t have a perfectly sharp cutoff
Arrange filters in parallel
  Each has same input
  Outputs summed (mixed) after band gains adjusted
x[n]
y[n]
Bandpass
Filter
+
Bandpass
Filter
Bandpass
Filter
...
...
|H|2
0
p
wc
1
B
Band-pass

## Slide 18: Series implementation
Consider cascade of peaking or shelving filters
Add a boost or notch to a specific frequency band
  Top and bottom bands may be shelving filters which extend to edge of spectrum
Each filter has gain of 1 outside the band
Arrange filters in series
Each takes its input from the previous filter
x[n]
Peak/Notch
100Hz
Peak/Notch
200Hz
Peak/Notch
6.4kHz
Shelving HP
12.8kHz
Peak/Notch
50Hz
...
y[n]
Boost/Cut
Level
Boost/Cut
Level
Boost/Cut
Level
Boost/Cut
Level
Boost/Cut
Level
Shelving LP
50Hz
Peak/Notch
12.8kHz
(variation)
(variation)
Gain of 1 (0dB)

## Slide 19: Design using shelving filters
Specify frequencies for ith band
  Let normalised lower cutoff be wl,i and upper cutoff wu,i
  Bandwidth Bi= wu,i -wl,i
  Centre frequency is approx. geometric mean
  Require frequency bands to be adjacent: wu,i =wl,i +1
Logarithmic distribution specified as follows
  By cutoff frequencies wl,i+1=R wl, i
  Equivalently, by centre frequencies wc,i+1=R wc, i
  Implies Bi+1=R Bi
  Notice: constant Qi =wc,i /Bi
  For octave equaliser, R=2
  For 1/3 octave equaliser, R=

## Slide 20: Design Using Shelving Filters
Parameters in terms of band centre frequencies
Subfilters ideally have magnitude of Gi inside band and unity gain outside that band
In practice, subfilters have transitional regions around band edges

## Slide 21: Design using shelving filters
When same gain used in adjacent bands, want flat magnitude response
  Requires filters to have complementary band-edges
  In general, we have
  So when Gi =Gi+1 =G , need:
When different gain used in adjacent bands
  Need filter edges to be sharp to minimise interband influence
  Requires higher-order filters

## Slide 22: Design using shelving filters
Start with lowpass filter prototype
  Use high-order Butterworth with cutoff wu,i -wl,i
  Use lowpass to bandpass transformation formula
  Then convert bandpass filter to shelving filter
  Shelving filters placed in series
Are these shelving
or bandpass filters?
From M. Holters and U. Zölzer, "Graphic Equalizer Design Using Higher-Order Recursive Filters," 9th Digital Audio Effects Conf. (DAFx) , 2006.
Notes: Note: plot is shelving filters since y axis is in db

## Slide 23: Octave equaliser
For 10-band octave equaliser
  Magnitude response with 8th-order band-shelving filters, equal (12dB) gain [dotted = individual, solid = sum]:
From M. Holters and U. Zölzer, "Graphic Equalizer Design Using Higher-Order Recursive Filters," 9th Digital Audio Effects Conf. (DAFx) , 2006.

## Slide 24: 1/3-octave equaliser
For 30-band 1/3-octave equaliser
  Magnitude response with 8th-order band-shelving filters, equal (12dB) gain [dotted = individual, solid = sum]:
From M. Holters and U. Zölzer, "Graphic Equalizer Design Using Higher-Order Recursive Filters," 9th Digital Audio Effects Conf. (DAFx) , 2006.