## Slide 1
Wah-wah

## Slide 2: Background
Origins
  Originally developed by jazz trumpeters using mutes
  Guitar effect since Jimi Hendrix popularised the Vox Crybaby pedal in the late 1960s
Wah-wah pedal
  Resonant (high-Q) filter with variable centre frequency
  Pedal controls the frequency
  Separate knob controls mix between original and filtered signal
  The Original GCB95 Cry Baby Wah
  Creative commons image from Wikipedia

## Slide 3: Resemblance to voice
“Wah-wah” resembles human vocalisation
Spectral characteristics of phonemes [u] & [a]:
  Vocal folds are harmonic source filtered by formants depending on shape of mouth
    [u] vowel: first formant is around 350 Hz
    [a] vowel: first formant is around 700 Hz
    [u] to [a] articulation produces modulated sound
    Trajectory of 1st formant moves up in frequency
  [a] ‘ah’ first formant in range 700-1200Hz
    Matches range of resonant peak in wah-wah circuit
    Pedal range covers frequencies where first 2 formants overlap
  But missing the second formant
    Only one resonant peak in wah-wah circuit
    Electro-Harmonix “Talking Pedal” uses two peaks
Resonant lowpass filter

## Slide 4: Block diagram
Variable Mixing
Bandpass or peaking filter with variable center frequency
x[n]
+
y[n]
1-Mix
Mix

## Slide 5: Varieties of wah-wah effects
Resonant (bandpass or peaking) filter
  Variable centre frequency
  Small bandwidth (i.e. high Q)
Standard wah-wah
  Centre frequency controlled by pedal (manual control)
Auto-wah (2 effects)
  Centre frequency controlled by LFO
  Frequency of LFO usually around 1-2 Hz
  OR, could depend on envelope of input signal
Tremolo-wah: also amplitude variations
Centre frequency can vary from near 0 to fs/2
  In practice, varies across the midrange frequencies only

## Slide 6: Magnitude response of a resonant low pass filter
magnitude 12 dB (Gc ~ 20) at wc=p/2

## Slide 7: Auto-wah [part 1]
One auto-wah effect uses a low-frequency oscillator
  LFO controls the centre frequency of the filter
  Parameters are similar to other LFO effects:
    Sweep rate
    Sweep width
    Minimum frequency
Time
fc
fmin
W

## Slide 8: Auto-wah [part 2]
Auto-wah can also refer to an envelope follower wah effect
  The centre frequency scales with the signal envelope
    Envelope is essentially the local average level of the signal
  Envelope is characterised by attack and decay times
    How fast does it respond to increasing and decreasing signal?
    Generally, attack time is much faster than decay time

## Slide 9: Auto-wah [part 3]
Auto-wah can also refer to an envelope follower wah effect
  The centre frequency scales with the signal envelope
    Envelope is essentially the local average level of the signal
  Envelope is characterised by attack and decay times
    How fast does it respond to increasing and decreasing signal?
    Generally, attack time is much faster than decay time
Other parameters:
  Minimum frequency
  Sensitivity S

## Slide 10: M-fold wah-wah
Replacing the unit delay in the resonant bandpass filter by an M tap delay leads to M-fold wah-wah filter
M bandpass filters are spread over entire spectrum and simultaneously change their center frequency.

## Slide 11: M-fold wah-wah
White noise input applied to M-fold wah-wah filter
Periodic enhancement of the output spectrum