## Slide 1
Phasing

## Slide 2: Background
Phaser (or phase shifter) creates 1 or more notches in frequency domain that eliminate sounds at notch frequencies
  Sometimes called phase shifter
Filter signal to shift phases of different frequencies
  Mix filter output with original signal
  Some frequencies add constructively, some destructively
Design filters to independently control
  Location of each notch
  Number of notches
  Width of notches
Sound example:
  plucked chord sequence
  dry, then with phaser

## Slide 3: Phaser, Wah-Wah, Flanger
Wah-wah
  Based on filters
  Varies centre frequency of a bandpass filter
Phaser
  Based on filters
  Set of allpass filters process the input signal
    Arbitrarily spaced notches
    Alternatively, implemented with notch filters
Flanger
  Relies on delay line
  Equally spaced notches
  Sound similar to phasing
    Can be considered simple type of phasing

## Slide 4: How phasing works
Notches implemented using allpass filters
  Allpass filter passes all frequencies equally
  No amplification or attenuation:
Add filtered output to original
  Amount of filtered output controlled by depth or mix control
Where do the notches come from?
It’s all about the phase
+
Allpass
Filter
x[n]
y[n]
Depth

## Slide 5: Phase response
Consider “black box” LTI system
  Don’t know what’s inside, but linear time-invariant
Observe important characteristics
  Magnitude response
    Relative amplitude of input and output at each frequency
    For allpass filter, these amplitudes are equal
    Magnitude response is 1 for all frequencies.
  Phase response (or phase lag)
    Relative alignment of two signals in time
    Allpass filters shift the phase of an input signal

## Slide 6: Phase response
Time and phase are inherently related
  Phase shift = altering relationship between input and output phases
  For a sine wave, phase shift is equivalent to delay
when original sine wave and 1800 phase lag are added together, result is complete cancellation
sine wave
with 900 phase lag
1800 phase lag
2700 phase lag
3600 phase lag (one cycle)

## Slide 7: Phase response
Practical filters have phase response that changes with frequency
Linear phase (special case)
  Phase lag is a linear function of frequency
  Could be pure delay
    Doubling frequency will double the phase response
    No phase distortion (different frequencies arriving at different times)
  Symmetric FIR filters are linear phase
Corollary: pure delay is a type of allpass filter

## Slide 8: Notches
To create notches, mix allpass filter output with input
  At some frequencies, phase lag will be 180o
    equivalent to taking negative of input.
  frequencies (notches) with 180o phase lag cancel frequency components in input
Frequencies near notch also attenuated
Filter with nonlinear phase response delays signal
  not all frequencies delayed by same amount
Linear phase case - pure delay
  phase response hits values of -180o minus multiples of 360o (-180, -540...) at equally spaced frequencies
  when mix delayed copy of signal with original, notches at equally spaced frequencies
  exactly how flanger operates
    flanger is type of phase shifter

## Slide 9: Allpass filters
Use allpass filters that do not have linear phase characteristic
  distort phase response to produce notch at any frequency
  # notches determined by filter complexity
chain additional filters to create more notches
  series combination of allpass filters is allpass filter
  phase response for chain of filters is sum of each filter's phase response
  MXR Phase 90 pedal contains 4 stages to create its sound
    each stage doesn't necessarily produce a notch
    phase response of first order allpass approaches 180o at very high frequencies
    multiple stages needed to create notch
  unlike flanger, can control width of notches if we want to
    parameter often determined in design stage of product
    can't be adjusted by user

## Slide 10: First order allpass filter
Feedforward and feedback loop gains are negatives of each other
flow diagram for first order digital allpass filter
+
z-1
x[n]
y[n]
g
+
-g

## Slide 11: Allpass filtering
Consider a 2nd-order IIR filter
We want
  This requires
  Which in turn gives:
  Notice: and
    0°/360° phase shift at DC and Nyquist

## Slide 12: Allpass filtering
Consider the phase
Frequency (0 to π)
Phase (-360° to 0°)
Here showing transition
frequencies:
π/8, π/4, π/2, 3π/4, 7π/8
Frequencies with ~= 0°/360°
phase shift will add constructively
Frequencies with ~= 180°
phase shift will add destructively

## Slide 13: Allpass filtering
IIR allpass filters have nonlinear phase response
Continuous-time and discrete-time IIR filters have different phase response
  Discrete-time warping effects
  Implications for digital simulation of analogue phasers
Discrete Time (w = 0 to π)
Continuous Time (log(f) scale)

## Slide 14: Allpass and notches
Can cascade multiple allpass filters to create more notches
  Phase response is sum of individual filters
  MXR Phase 90 and Small Stone Phaser include 4 allpass stages
  Unlike flanger, phaser can control width of notches
    Not commonly user-controllable
Dashed lines show
location of notches
(180° + k*360°)

## Slide 15: Allpass filter phase and phaser notch locations. Center frequency 1kHz, sampling frequency 44.1kHz. a, b, c and d represent 1, 2, 3 and 4 second order sections
(a)
(b)
(c)
(d)

## Slide 16: Notch spacing
4 1st-order sections = 2 second-order sections
  720° of total phase shift
  Where are the notches?
    -180° and -540°

## Slide 17: Notch spacing

## Slide 18: Notch spacing
Notice: not evenly spaced

## Slide 19: Notch spacing
Adding more sections moves all the notches

## Slide 20: Notch spacing
At 3kHz, start to see an effect from the discrete-time warping
Highest notch off by -2.5 semitones

## Slide 21: Notch spacing
Warp even more pronounced at 10kHz
Highest notch off by -12.8 semitones!

## Slide 22: Sweeping notches
Chorus and flanger
  LFO controls delay time
Phaser
  Notch frequencies change exponentially
    e.g. double notch frequency for each unit time going up, halve notch frequency at each step to return to low point
  Most commercial products
    limited or no control over how notches sweep
    Except overall rate at which they sweep
Sound example: exponential and linear sweep
2 segments of phase shift applied to distorted guitar
  notches sweep exponentially along frequency axis
  notch sweep is linear
Listen to notches at beginning (low point)
  In 1, notches move more slowly at first compared to 2d clip

## Slide 23: Common parameters
Depth (mix level)
  Amount of filter output added to sound
  Name comes from its relation to depth of notches
  When depth = 1, notches reach to 0
  In some multi-effects processors, depth control may be only in mixer section
Sweep width (sometimes “sweep depth”)
  Frequency range notches traverse
  Sometimes able to select actual frequency values
  Or set deviation from a given base frequency
  Compare all this to similar controls on flanger
Distorted guitar sound, processed by phaser with 1 octave sweep depth, then 2 octave sweep depth. rate is same in both cases

## Slide 24: Common parameters
Speed or rate:
  How quickly notches sweep over frequency range
    Oscillations per second
  How fast notches move in frequency domain is controlled by
    Speed control
    Sweep width
    Sweep pattern

## Slide 25: Feedback / regeneration
Feedback produces more intense sound
  Works by adding part of output back to input
Some units allow negative feedback gains
  Subtract output from input
For multistage allpass filters:
  Can use feedback on individual stages or overall
strummed guitar using phaser with mild feedback, followed by higher feedback setting
+
Allpass
Filter
x[n]
y[n]
Depth
gFB
+
Phaser with feedback. Feedback gain can be positive or negative, but must have a magnitude strictly less than 1

## Slide 26: Alternate implementations (1)
Standard implementation: 2nd order allpass filters
  Time-varying centre frequencies
  Multiple allpass filters in cascade
  Time-varying phase shifts
Feedforward and feedback configurations
x[n]
Allpass
filter
Allpass
filter
...
gFB
g
+
+
y[n]
Allpass
filter

## Slide 27: Alternate implementations (2)
Cascade of 2nd order IIR notch filters
  Combine notch outputs and direct sound
  Notch frequencies slowly varied (LFO)
Notch filters also produce phase shift
  Combines with input phase to create cancellations
Notch
filter
...
g
+
x[n]
y[n]
Notch
filter
Notch
filter

## Slide 28: Stereo phasing
Like stereo flanger and chorus
  2 filters with notches at different frequencies
  Selectively mix output of each filter to create new sounds (additional notches)
Spatial phaser
  Feed-across gains set to 0
  Each output fed to different speaker
  Notches exist only in air (acoustic cancellation) and heard by moving about room
x [n]
y1[n]
y2[n]
Allpass
Allpass

## Slide 29: Phaser C++ code
int numSamples; // Indicates how many audio samples to process
float *channelData; // Array of audio samples, length numSamples
float ph; // Current phase of the LFO (0-1)
float lastFilterOutput; // Output of the filter last sample, for implementing feedback
OnePoleAllpassFilter **allpassFilters; // Objects handling a first order allpass filter
float inverseSampleRate; // Defined as 1.0/(sample rate)
int sc; // Sample count, used to decide when to update the coefficients
float depth_; // Depth of the phaser effect (0-1)
float feedback_; // Amount of feedback (>= 0, < 1)
float lfoFrequency_; // Frequency of the LFO
float baseFrequency_; // Lowest point in the sweep of the allpass center frequency
float sweepWidth_; // Width of the LFO (in Hz)
int waveform_; // Identifier of what type of waveform to use (sine, triangle, ...)
int filtersPerChannel_; // How many allpass filters are used
int filterUpdateInterval_; // How often to update the allpass coefficients
for (int sample = 0; sample < numSamples; ++sample)
{
float out = channelData[sample];
…[SEE NEXT SLIDE]
}

## Slide 30: Phaser C++ code
//If feedback on, feedback last sample to input of allpass filter chain
If (feedback_) out += feedback_ * lastFilterOutput;
for(int j = 0; j < filtersPerChannel_; ++j)
{
// Update current allpass filter coefficients depending on parameter
// settings & LFO phase. Only update coefficients at fraction of sample
// rate; since LFO is slow, difference won't generally be audible.
if(sc % filterUpdateInterval_ == 0) allpassFilters[j]->makeAllpass(
inverseSampleRate, baseFrequency_ + sweepWidth_* lfo(ph, waveform_));
out = allpassFilters[j]->processSingleSampleRaw(out);
}
lastFilterOutput = out;
// Add allpass signal to output, maintaining constant level
// depth = 0 --> input only ; depth = 1 --> evenly balanced input and output
channelData[sample] = (1-0.5*depth_)*channelData[sample] + 0.5*depth_*out;
// Update LFO phase, keeping it in range 0-1
ph += lfoFrequency_*inverseSampleRate;
if(ph >= 1.0) ph -= 1.0;
sc++;

## Slide 31: Allpass filter code
The expression allpassFilters[j]->processSingleSampleRaw(out) runs the following code for each allpass filter object:
float OnePoleAllpassFilter::processSingleSampleRaw(float sampleToProcess)
{
// Process one sample, storing the last input and output
y1 = (b0 * sampleToProcess) + (b1 * x1) + (a1 * y1);
x1 = sampleToProcess;
return y1;
}
Here, x1 and y1 keep track of the last input and output x[n-1] and y[n-1] respectively. b0, b1 and a1 are coefficients of the filter, as calculated by the makeAllpass() function in the previous code block.