## Slide 1
Graphic equalizer design with the Web Audio API

## Slide 2: Equalisation
Filters change magnitudes & phases of a signal’s frequency content
Can use audio nodes in the Web Audio API to create filters
  BiquadFilterNode – standard second order filters
  IIRFilterNode – arbitrary fixed design filters
  ConvolverNode – create a Finite Impulse Response (FIR) filter
  Audio Worklet – create your own filters
Equalisation (EQ) is a form of filtering
  Boosting or cutting certain frequency components in a signal
Origin
  Trying to obtain flat frequency response
  No colouration
A simple tool is the tone control

## Slide 3: Tone controls
Most common equalisation is the tone control
  Controls: bass and treble
  Adjust sound to suit your taste
  Bass control = low shelving filter
  Treble control = high shelving filter
  Control centred = unity gain = flat response
Boost
Cut
Boost
Cut

## Slide 4: Tone controls - Midrange
In addition to bass and treble, midrange control
Peaking filter affects frequencies between highs and lows
Boost or cut portion of spectrum without affecting the rest
Does not attempt to isolate particular frequencies
Boost
Cut

## Slide 5: Three tone controls, including peaking filter to adjust the midrange
Bass
Treble
Input audio
High shelf
Low shelf
Output audio
Bass
Mids
Peaking/ notch
Low shelf
Treble
High shelf
Input audio
Output audio
Bass and treble tone controls implemented as low and high shelf filters in series

## Slide 6: Graphic equaliser
Lets user set gains for fixed frequency bands
  Gain of each band generally controlled with slider
More flexible than tone control
  More frequency bands available
    6 to 40 bands is typical range
  Like tone controls, centre frequencies are fixed
Boost or cut controlled with sliders
  slider positions represent samples of magnitude response at different frequencies
  Gives ‘graphic’ representation of frequency response
Band distribution is logarithmic in frequency
  Matches human perception

## Slide 7: Graphic Equalisers and sliders
Manipulate each frequency band independently by inserting gain control
sliders on front of equaliser are gain controls in each band

## Slide 8: Graphic EQ and octaves
Centre frequencies usually equally spaced in octaves
  Logarithmic, not linear, in frequency
  Octave is factor of 2
  1/3 octave spacing based on factor of 21/3 ~ 1.26
Examples
  1 octave spacing starting at 100Hz would have...
    200Hz, 400Hz, 800Hz, 1.6kHz, ...
  1/3 octave spacing starting at 100Hz would have...
    126Hz, 159Hz, 200Hz, 252Hz, 318Hz, 400Hz, ...
Q kept roughly constant for each frequency band
Gains are given in decibels

## Slide 9: Series implementation
Consider cascade of peaking or shelving filters
Add boost or notch to a specific frequency band
  First and last bands can be shelving filters
Each filter has gain of 1 outside the band
Arrange filters in series
Each takes its input from the previous filter
Input
Peaking
100Hz
Peaking
200Hz
Peaking
6.4kHz
High shelf
12.8kHz
...
Output
Boost/Cut
Level
Boost/Cut
Level
Boost/Cut
Level
Boost/Cut
Level
Boost/Cut
Level
Low shelf
50Hz
Gain of 1 (0dB)

## Slide 10: Octave equaliser
When same gain used in adjacent bands, want flat magnitude response
Real bandpass filters may have ripple in passband and don’t have a perfectly sharp cutoff
For 10-band octave equaliser
Magnitude response

## Slide 11: Parallel implementation
Consider lowpass, bandpass and highpass filters
  Completely isolate individual frequency bands
Input
Output
Bandpass
+
Lowpass
Highpass
...
...
|H|2
0
p
wc
1
B
Bandpass
Gains:
Filters:
Arrange filters in parallel
  Each has same input
  Outputs summed (mixed) after band gains adjusted
Q=wc/B