## Slide 1
Delay-Based Effects

## Slide 2: Basic delay
From digital system perspective, delay is simple:
  Difference equation adding the current input sample to one N samples prior
  y[n]=x[n]+ax[n-N] | a|<1 (usually)
For audio:
  Delay ranges from milliseconds to several seconds
  What values of N does this imply for sampling rate= 44.1kHz?
    1 second =
    1 ms =
    = 1 sample
    44100 samples
    ~ 44 samples
    22.6µS
+
Delay (N)
x[n]
y[n]
g

## Slide 3: Basic delay: aesthetics
Takes audio and plays it back after delay time
  One of the simplest audio effects
Use delay to:
  Bring to life dull mixes
  Widen an instrument’s sound
  Solo over yourself
Delay is building block for other effects
  Echo
  Reverb
  Chorus
  Flanging
  ...

## Slide 4: Delay with feedback
Most delays have feedback control (regeneration)
  takes delay output, sends it back to input
  repeat sound over and over
Quieter each time it plays back
  assuming feedback gain is less than one
    Most delay devices restrict gain to less than one for stability
  after some point, drops below noise floor  inaudible
Basic delay unit with feedback
+
Delay N
x[n]
y[n]
gFB
+
To derive y[n] in terms of x[n]:
d[n]=x[n-N]+gFBd[n-N] , y[n]=x[n]+d[n]
d[n-N]=y[n-N]-x[n-N]
y[n]=x[n]+ x[n-N]+gFBd[n-N]
=x[n]+x[n-N]+gFB(y[n-N]-x[n-N])
=x[n]+ (1-gFB)x[n-N]+gFBy[n-N]

## Slide 5: Delay on an instrument
Playing through delay unit with short echo, say 50 to 100 milliseconds, creates doubling effect
  Useful for filling out an instrument's sound
  Like two instruments being played in unison
  Several delays together with feedback can create reverb-like sound
simple guitar riff, followed by the same riff, but with added delay 40 ms., doubling the sound

## Slide 6: Long delays
Delay times above 100ms no longer a subtle effect
  Can match delay time to tempo of song
    Delayed copies of sound fall on a beat
Extending to very long delays: 1 second or more
  Can play over yourself
  develop harmonies even though you may only play one note at a time
See A Study of The Edge’s (U2) Guitar Delay by Tim Darling
  http://www.amnesta.net/edge_delay/
can use long delay to layer notes
delay time used here is 1.5 seconds

## Slide 7: Looping and sampling
Record only a segment of playing and loop it
  e.g. a chord progression
  Play recorded audio over and over
  Solo over yourself, without rhythm player
Some delay pedals include sampling capability
  Length of sample often limited to 2 seconds or less
For serious looping, need longer recording time
  Memory depends on duration, sample rate, bit depth
Popular units offer additional capabilities
  Recording additional sounds onto sample
  Playing loop backwards
  Recording several different loops

## Slide 8: Delay and mixing
Important when mixing for stereo
  Enhance stereo placement of instruments
  Make mix sound “bigger”
Small delay can be more effective than panning for spreading tracks out in stereo field
  Simple delay ca. 20ms can make big difference
We discuss this when covering spatial effects
riff initially mixed to center of stereo mix.
followed by same riff with 20 ms delay between 2 channels.
NO panning involved - just pure delay with no feedback.

## Slide 9: Slapback and echo
Slapback delay is not new algorithm
  same as basic delay without feedback
Delay is called slapback delay if delay time fairly short
  between 40 and 120 milliseconds.
Longer delay called echo

## Slide 10: Typical effect delay times
(We’ll see these
other effects soon!)

## Slide 11: Multi-tap delay
Simple delay: outputs taken after total delay time
Multi-tap delay is more flexible
  Take outputs after only portion of delay time
  Known as tapping the delay line
    Like tap in water pipe allows you to get water at various points
Units labeled with number of available taps
  3-tap delay has 3 taps to use, a 4-tap has 4, etc.
  Unwanted taps removed by setting output level to 0
  Amount of delay between taps can be different
4-tap delay in action
z-N1
x[n]
y[n]
+
z-N2
z-N3
z-N4
+
+
+

## Slide 12: Multi-tap delay
General case of basic delay design
  Set all but one tap gain to 0, place remaining tap at delay line end  results in basic delay line
Multi-tap delay can be generalised further
  Allow feedback from each delay output to beginning
  Easy to create unstable system!
Looking only at single tap
  Sound repeats according to total delay time
  Input appears at tap output before total delay time (except last, rightmost tap)
sound produced with 4-tap delay
same sound with fourth tap moved 80 ms. closer to input
sound with increased total delay time increased by 200 ms. (i.e., Delay 5 in the diagram increased by 200 ms.).

## Slide 13: Delay in the recording process
Suppose we record instrument with two microphones
  Sound travels at 340.3m/s
  If mics are 2m apart, sound arrives 5.9ms later to the distant mic
Adding closely timed similar signals creates phase problems
  Selective cancellation of certain frequencies
  Can be used deliberately as musical effect (more on this soon)
Solution: delay the close mic to compensate
2m = 5.9ms
Delay
5.9ms

## Slide 14: Digital delay implementation
Operation
  Read an input recorded previously
  Store current input in another memory location
    Or may be same location that was just read
    This is why value read before writing
  Next sampling period
    Read & write next location in memory
    When end of memory, loop around to first memory location
    This is a circular buffer, and it is quite efficient
Programming delays
  Read and write pointers keep track of where to read/write in memory
  Pointers increment each sample
  Multi-tap delays created using additional read pointers

## Slide 15: Delay on a circular buffer
Buffer is a contiguous block of memory
  Read and write pointers point to specific locations within this block
  Difference in read/write pointer location determines delay
  This is equivalent to difference equation representations
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
x[13]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
write pointer
read pointer

## Slide 16: Delay code
Our Delay effect will be simple VST plugin
  Start with HelloWorld UI from Getting Started
  Use the first, generic version
Define variables in pluginprocessor.h
Set up the variables in prepareToPlay
Edit processBlock so that it implements delay
  Use read and write pointers on circular buffer
  Make sure that incrementing pointer on one channel does not affect other channels

## Slide 17: Define and initialise
Add private parameters in pluginProcessor.h
Add parameters to generic user interface in pluginProcessor.cpp
private:
juce::AudioParameterFloat* delayTimeParam;
juce::AudioParameterFloat* feedbackParam;
juce::AudioParameterFloat* dryWetMixParam;
juce::AudioSampleBuffer delayBuffer;
int delayBufferLength;
int delayReadPosition, delayWritePosition = 0;
Parameters on interface
Circular buffer variables for implementing delay
DelayAudioProcessor::DelayAudioProcessor() …
{
addParameter(delayTimeParam = new juce::AudioParameterFloat(
"delayTime", "Delay time", 0.0f, 2.0f, 0.0f));
addParameter(feedbackParam = new juce::AudioParameterFloat(
"feedback", "Feedback", 0.0f, 0.999f, 0.0f));
addParameter(dryWetMixParam = new juce::AudioParameterFloat(
"dryWetMix", "Dry/wet mix", 0.0f, 1.0, 0.0f));
}
Notes: juce::AudioParameterFloat* delayTimeParam;
juce::AudioParameterFloat* feedbackParam;
juce::AudioParameterFloat* dryWetMixParam;
float inputPhase = 0.0, lfoPhase = 0.0;
// Circular buffer variables for implementing delay
juce::AudioSampleBuffer delayBuffer;
int delayBufferLength;
int delayReadPosition = 0, delayWritePosition = 0;

## Slide 18: Define and initialise
Set up delay buffer in prepareToPlay on pluginProcessor.cpp
void NewProjectAudioProcessor::prepareToPlay (double sampleRate, int samplesPerBlock) {
auto delayTime = delayTimeParam->get();
delayBufferLength = (int)(2.0 * sampleRate);
delayBuffer.setSize(2, delayBufferLength);
delayBuffer.clear();
delayReadPosition = (int)(delayWritePosition - (delayTime * getSampleRate())
+ delayBufferLength) % delayBufferLength;
}
Allocate delay buffer, size depends on sample rate
determine delay position offset in samples
Notes: juce::AudioParameterFloat* delayTimeParam;
juce::AudioParameterFloat* feedbackParam;
juce::AudioParameterFloat* dryWetMixParam;
float inputPhase = 0.0, lfoPhase = 0.0;
// Circular buffer variables for implementing delay
juce::AudioSampleBuffer delayBuffer;
int delayBufferLength;
int delayReadPosition = 0, delayWritePosition = 0;

## Slide 19: processBlock 1 - Define variables
Set up the basics in the processBlock method on pluginProcessor.cpp
const int numInputChannels = getTotalNumInputChannels();
const int numOutputChannels = getTotalNumOutputChannels();
const int numSamples = buffer.getNumSamples();
float sampleRate = (float)juce::AudioProcessor::getSampleRate();
auto dryWetMix = dryWetMixParam->get();
auto feedback = feedbackParam->get();
auto delayTime = delayTimeParam->get();
delayReadPosition = (int)(delayWritePosition - (delayTime * getSampleRate())
+ delayBufferLength) % delayBufferLength;
Information about these samples
Update read position based on current delay time
Notes: must pass MidiKeyboardState object to initialise MidiKeyboardComponent object

## Slide 20: processBlock 2 – apply delay
for (int i = 0; i < numSamples; ++i) {
for (int j = 0; j < numInputChannels; ++j) {
const float in = buffer.getWritePointer(j)[i];
float* delayData = delayBuffer.getWritePointer(j);
delayData[delayWritePosition] = in + delayData[delayReadPosition] * feedback;
float out = (1 - dryWetMix) * in + dryWetMix * delayData[delayReadPosition];
buffer.getWritePointer(j)[i] = out;
}
if (++delayReadPosition >= delayBufferLength) delayReadPosition = 0;
if (++delayWritePosition >= delayBufferLength) delayWritePosition = 0;
}
Go through each audio channel
delayData is circular buffer for finding delay on this channel
get current input value for this channel, this sample
write to buffer. delayData[delayReadPosition] is last delay sample that we read
set current output for this channel, this sample, replacing input
increment pointers; once per sample, not once per channel!
Read from buffer. Output is input + delay buffer content, weighted by dryWetMix
Notes: must pass MidiKeyboardState object to initialise MidiKeyboardComponent object

## Slide 21: Ping-pong delay
For stereo audio systems
Creates bouncing effect
  Sound typically jumps between left and right channels
2 delay lines with 2 inputs, 2 outputs
  Can use same signal for each input
  Typically pan outputs hard left and hard right
Feedback from each delay line goes to opposite line
ping-pong delay
1st sequence generated with symmetric setup (delays same length, same feedback gain) panned hard left and right
2nd sequence breaks symmetry and panning
x1[n]
y1[n]
z-N
z-N
y2[n]
x2[n]

## Slide 22: Lets work out the transfer functions
x1[n]
y1[n]
z-N
z-N
y2[n]
x2[n]

## Slide 23
W1 (z)=[b1W2 (z)+a1X1 (z)] z-N
W2 (z)=[b2W1 (z)+a2X2 (z)] z-N
Solve these equations for W1
b1 b2W1z-2N + b1 a2X2 z-2N+a1X1z-N =W1
W1=[a2 b1 X2 z-2N+a1X1 z-N]/[1-b1 b2 z-2N ]
Now plug into
Y1 (z) = c1W1 (z)+X1 (z)
...and similar for the other channel
X1(z)
Y1(z)
z-N
z-N
Y2(z)
X2(z)
W1(z)
W2(z)
a1
a2
c1
c2
b2
b1

## Slide 24: Define and initialise
Start with delay plugin
Add private parameters to pluginProcessor.h
Set up delay buffer in prepareToPlay on pluginProcessor.cpp
auto delayTime = delayTimeParam->get(); …
delayReadPosition = (int)(delayWritePosition - (delayTime * getSampleRate())
+ delayBufferLength) % delayBufferLength;
auto leftRightDelayTime = leftRightDelayTimeParam->get();
auto rightLeftDelayTime = rightLeftDelayTimeParam->get();
delayReadPositionLeft = (int)(delayWritePosition - (leftRightDelayTime * sampleRate)
+ delayBufferLength) % delayBufferLength;
delayReadPositionRight = (int)(delayWritePosition - (rightLeftDelayTime * sampleRate)
+ delayBufferLength) % delayBufferLength;
juce::AudioParameterFloat* delayTimeParam;
juce::AudioParameterFloat* leftRightDelayTimeParam, rightLeftDelayTimeParam;
juce::AudioParameterBool* linkDelaysParam;
juce::AudioParameterBool* reverseChannelsParam;
…
int delayReadPosition
int delayReadPositionLeft, delayReadPositionRight;

## Slide 25: processBlock 1 - Define variables
Set up the basics in the processBlock method on pluginProcessor.cpp
…
auto delayTime = delayTimeParam->get();
auto leftRightDelayTime = leftRightDelayTimeParam->get();
auto rightLeftDelayTime = rightLeftDelayTimeParam->get();
auto reverseChannels = reverseChannelsParam->get();
// these are arrays of length numSamples which contain a chnnel’ audio
float* channelDataL = buffer.getWritePointer(0);
float* channelDataR = buffer.getWritePointer(1);
// these are the circular buffers for implementing delay
float* delayDataL = delayBuffer.getWritePointer(0);
float* delayDataR = delayBuffer.getWritePointer(1);
for (int i = 0; i < numSamples; ++i) {
…
}
Notes: must pass MidiKeyboardState object to initialise MidiKeyboardComponent object

## Slide 26: processBlock 2, loop over samples
//const float inL = channelDataL[i], inR = channelDataR[i];
float outL, outR;
if (reverseChannels) {
outL = (inL + dryWetMix * delayDataR[delayReadPositionLeft]);
outR = (inR + dryWetMix * delayDataL[delayReadPositionRight]);
} else {
outL = (inL + dryWetMix * delayDataL[delayReadPositionLeft]);
outR = (inR + dryWetMix * delayDataR[delayReadPositionRight]);
}
// Store output of one delay buffer into other, producing ping-pong effect
delayDataR[delayWritePosition] = inR + (delayDataL[delayReadPositionLeft] * feedback);
delayDataL[delayWritePosition] = inL + (delayDataR[delayReadPositionRight] * feedback);
if (++delayReadPositionLeft >= delayBufferLength) delayReadPositionLeft = 0;
if (++delayReadPositionRight >= delayBufferLength) delayReadPositionRight = 0;
if (++delayWritePosition >= delayBufferLength) delayWritePosition = 0;
// Store the output samples in the buffer, replacing the input
channelDataL[i] = outL;
channelDataR[i] = outR;