## Slide 1: Ping-pong delay
For stereo audio systems
Creates bouncing effect
  Sound typically jumps between left and right channels
2 delay lines with 2 inputs, 2 outputs
  Can use same signal for each input
  Typically pan outputs hard left and hard right
Feedback from each delay line goes to opposite line
ping-pong delay
1st sequence generated with symmetric setup (delays same length, same feedback gain) panned hard left and right
2nd sequence breaks symmetry and panning
x1[n]
y1[n]
z-N
z-N
y2[n]
x2[n]

## Slide 2: Lets work out the transfer functions
x1[n]
y1[n]
z-N
z-N
y2[n]
x2[n]

## Slide 3
W1 (z)=[b1W2 (z)+a1X1 (z)] z-N
W2 (z)=[b2W1 (z)+a2X2 (z)] z-N
Solve these equations for W1
b1 b2W1z-2N + b1 a2X2 z-2N+a1X1z-N =W1
W1=[a2 b1 X2 z-2N+a1X1 z-N]/[1-b1 b2 z-2N ]
Now plug into
Y1 (z) = c1W1 (z)+X1 (z)
...and similar for the other channel
X1(z)
Y1(z)
z-N
z-N
Y2(z)
X2(z)
W1(z)
W2(z)
a1
a2
c1
c2
b2
b1

## Slide 4: Define and initialise
Start with delay plugin
Add private parameters to pluginProcessor.h
Set up delay buffer in prepareToPlay on pluginProcessor.cpp
auto delayTime = delayTimeParam->get(); …
delayReadPosition = (int)(delayWritePosition - (delayTime * getSampleRate())
+ delayBufferLength) % delayBufferLength;
auto leftRightDelayTime = leftRightDelayTimeParam->get();
auto rightLeftDelayTime = rightLeftDelayTimeParam->get();
delayReadPositionLeft = (int)(delayWritePosition - (leftRightDelayTime * sampleRate)
+ delayBufferLength) % delayBufferLength;
delayReadPositionRight = (int)(delayWritePosition - (rightLeftDelayTime * sampleRate)
+ delayBufferLength) % delayBufferLength;
juce::AudioParameterFloat* delayTimeParam;
juce::AudioParameterFloat* leftRightDelayTimeParam, rightLeftDelayTimeParam;
juce::AudioParameterBool* linkDelaysParam;
juce::AudioParameterBool* reverseChannelsParam;
…
int delayReadPosition
int delayReadPositionLeft, delayReadPositionRight;

## Slide 5: processBlock 1 - Define variables
Set up the basics in the processBlock method on pluginProcessor.cpp
…
auto delayTime = delayTimeParam->get();
auto leftRightDelayTime = leftRightDelayTimeParam->get();
auto rightLeftDelayTime = rightLeftDelayTimeParam->get();
auto reverseChannels = reverseChannelsParam->get();
// these are arrays of length numSamples which contain a chnnel’ audio
float* channelDataL = buffer.getWritePointer(0);
float* channelDataR = buffer.getWritePointer(1);
// these are the circular buffers for implementing delay
float* delayDataL = delayBuffer.getWritePointer(0);
float* delayDataR = delayBuffer.getWritePointer(1);
for (int i = 0; i < numSamples; ++i) {
…
}
Notes: must pass MidiKeyboardState object to initialise MidiKeyboardComponent object

## Slide 6: processBlock 2, loop over samples
//const float inL = channelDataL[i], inR = channelDataR[i];
float outL, outR;
if (reverseChannels) {
outL = (inL + dryWetMix * delayDataR[delayReadPositionLeft]);
outR = (inR + dryWetMix * delayDataL[delayReadPositionRight]);
} else {
outL = (inL + dryWetMix * delayDataL[delayReadPositionLeft]);
outR = (inR + dryWetMix * delayDataR[delayReadPositionRight]);
}
// Store output of one delay buffer into other, producing ping-pong effect
delayDataR[delayWritePosition] = inR + (delayDataL[delayReadPositionLeft] * feedback);
delayDataL[delayWritePosition] = inL + (delayDataR[delayReadPositionRight] * feedback);
if (++delayReadPositionLeft >= delayBufferLength) delayReadPositionLeft = 0;
if (++delayReadPositionRight >= delayBufferLength) delayReadPositionRight = 0;
if (++delayWritePosition >= delayBufferLength) delayWritePosition = 0;
// Store the output samples in the buffer, replacing the input
channelDataL[i] = outL;
channelDataR[i] = outR;