## Slide 1: Introduction: FFT
Fast Fourier Transform
Method to compute Discrete Fourier Transform (DFT) for evenly-spaced frequency samples
DFT is sampling of Discrete-Time Fourier Transform (DTFT)
  DTFT:
  DFT:
  FFT:
(continuous frequency)
(discrete frequency)
Same as DFT: just a specific implementation

## Slide 2: Introduction: FFT
Reconstructing signal from DFT/FFT
  Inverse Discrete Fourier Transform (IDFT/IFFT)
    DFT:
    IDFT:
Notice: N time samples N frequency samples
  Two different perspectives on same signal
  Given signal length M, can exactly reconstruct from FFT of length N ≥ M
    What happens with an FFT of length N < M?
Aliasing

## Slide 3: The Fast Fourier Transform
Most common use of block-based processing: the Fast Fourier Transform (FFT)
  Efficient computational algorithm for calculating the Discrete Fourier Transform (DFT)
  The DFT is a mathematical formula for calculating the frequency content of a signal
Any discrete-time signal of N points can be expressed as the sum of N sinusoids:
x[n] (time domain)
Frequency
Amplitude
Phase
(other components are 0 or redundant)
0
4.00
0
π/8
1.64
-.875*π
3π/8
0.20
-.625*π
5π/8
0.09
-.375*π
7π/8
0.65
-.125*π
Xk (frequency domain)
The DFT calculates the amplitudes and
phases of each frequency component

## Slide 4: The Discrete Fourier Transform
DFT calculates amplitudes and phases of each sinusoidal component
  Frequencies are linearly spaced between 0 and 2π:
  Each amplitude/phase measurement is called a bin
  Collectively, the N bins are called the frequency domain representation of the signal
for
Frequency
Amplitude
Phase
(other components are 0 or redundant)
0
4.00
0
π/8
1.64
-.875*π
3π/8
0.20
-.625*π
5π/8
0.09
-.375*π
7π/8
0.65
-.125*π
Xk (frequency domain)

## Slide 5: The Discrete Fourier Transform
Key point: N time samples «︎ N frequency samples
  Two different mathematical perspectives on the same signal
  Inverse Discrete Fourier Transform (IDFT) converts from frequency domain to time domain
  The DFT+IDFT is an exact reconstruction as long as signal length M ≤ DFT length N
Xk (frequency domain)
x[n] (time domain)
DFT
IDFT

## Slide 6: The Discrete Fourier Transform
sum, for all values of n between 0 and N-1...
...of signal x[n] multiplied by...
...complex exponential of frequency
...where k is the bin number
The mathematical basis of the Discrete Fourier Transform:
N is the size of the DFT
  For the FFT, N is almost always a power of 2 (the Cooley-Tukey algorithm)
Each time sample x[n] is a real number
Each frequency bin Xk is a complex number:
  Magnitude of the bin is given by:
    We usually use magnitude to plot a spectrum or spectrogram of a signal
  Phase of the bin is given by:
DFT (FFT)
time domain → frequency domain
IDFT (IFFT)
frequency domain → time domain
where

## Slide 7: DFT magnitude and phase
Each frequency bin Xk is a complex number:
  Magnitude of the bin is given by:
    We usually use magnitude to plot a spectrum or spectrogram of a signal
  Phase of the bin is given by:
Can also turn the calculation around:
  Given magnitude M and a phase 𝜙, calculate real and imaginary components
  Real component: Imaginary component:
Remember, frequency resolution depends on DFT size
  Bin frequencies are spaced 2π/N apart, where 2π corresponds to the sample rate
  For example, N=1024, fs = 44.1kHz: bin spacing is 43.1Hz
where

## Slide 8: DFT frequency spacing
Discrete Fourier Transform bins are spaced linearly in frequency
  By contrast, musical intervals are defined as ratios in frequency (e.g. 1 octave = 2x)
  This means that pitch resolution of the DFT is better for higher bins
    This can be a headache for many musical applications
FFT bin frequencies
(linear spacing)
f
2f
1 octave
1 octave
1 octave
8f
16f
32f
ECS7012P Music and Audio Programming • Week 10b

## Slide 9: Short-Time Fourier Transform
Short-Time Fourier Transform (STFT) is DTFT of windowed signal
  Similarly, can take DFT/FFT for discrete samples of windowed signals
Can break signal into windowed segments
  ...then (in right circumstances) put it back together

## Slide 10: Window spectra
Hann-windowed
spectrum
(frequency smearing)
Windowing lets us isolate segment of signal
Cost is smearing of energy in frequency domain
  Energy appears at frequencies where it doesn’t exist in original signal
Each frequency component of signal appears as series of lobes
  Main lobe: broad peak centred around actual frequency
  Side lobes: secondary peaks at other frequencies
Typically want to minimise:
  Main lobe width
  Side lobe height
ideal signal
(all energy at one
frequency)
Main lobe width
(expressed in
frequency)
Side lobe height
(expressed in dB)

## Slide 11: Window spectra
Main lobe width: 8π/N
Side lobe height: -26.5dB
Rectangular
Triangular (Bartlett)
Hann
Hamming
Main lobe width: 4π/N
Side lobe height: -13dB
Main lobe width: 8π/N
Side lobe height: -31.5dB
Main lobe width: 8π/N
Side lobe height: -42.8dB
→ When in doubt: use a Hann window

## Slide 12: Applications
Many possibilities between DFT and IDFT
  Efficient FIR convolution
    FIR filter of length N needs N multiplies per sample
    Convolution in time = multiplication in frequency
H(z)
X(z)
Y(z)

## Slide 13: Phase vocoder, part 3
Learn
  Modifying signals in frequency domain
  Converting frequency to phase
  Analysis and synthesis windows
Finally, create phase vocoder effects:
  Robotisation (phase zeroing)
  Whisperisation (phase randomisation)
  Pitch shifting
FFT
effect
IFFT

## Slide 14: Phase vocoder: more ideas
Ways to improve the quality of the effects:
  When mixing components into an FFT bin, use RMS amplitude rather than linear addition
  When mixing components into an FFT bin, find the weighted average of the frequencies
  Implement peak tracking to reduce some of the effects of window lobes
Other effects using phase vocoder:
  Combine frequency detector with pitch shift to implement auto-tuning
  Cross-synthesis: combine frequencies from one signal with magnitudes from another
  Noise reduction: suppress frequency components below threshold or matching known profile
As effects become more complex, CPU becomes a limitation
  Try larger hop sizes (which may also require larger FFTs)
  Pre-calculate frequently used constants (e.g. bin frequencies)
  Look for other optimisations to reduce number of multiplies per hop