## Slide 1
Phase Vocoder Effects
Mutation, Robotisaton, Whisperisation, Pitch shifting, Time scaling

## Slide 2: Phase vocoder, part 1
What you’ll learn:
Segmenting a real-time signal into windows
Working with overlapping windows (overlap-add)
What you’ll make:
A phase vocoder framework

## Slide 3: Block-based processing
Sometimes audio calculations need to run on block of samples
  For example: wait until 512 samples arrive, then do something with all of them at once
Compare this to filters, where we calculate new output every sample
  With block-based processing, usally run calculation periodically, not every sample
run calculation

## Slide 4: Block-based input
input
buffer
Start with fixed size buffer
  Fill it up sample by sample
  When full, apply window function and pass it to block-based process (like FFT)
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
write
pointer
current
sample
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
x[n]
Block-based
processing
Apply
window
Block-based
processing
Apply
window
Block-based
processing
Apply
window
S12
S13
S14
S15
S16
S17

## Slide 5: Block-based input and output
After dividing signal into windows, often want to reconstruct it
  Process each block
  Stitch processed blocks together into
  new signal
  If we don’t process each block,
  should reconstruct signal exactly
Application: phase vocoder
  FFT on each block
  Do processing in frequency domain
  IFFT on each block

## Slide 6: Block-based input and output
input
buffer
Ideal block-based processing system might work something like this:
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
write
pointer
current
sample
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
x[n]
Block-based
processing
Apply
window
Block-based
processing
Apply
window
Block-based
processing
Apply
window
S12
S13
S14
S15
S16
S17
...
y[n]
output
buffer
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
Y9
Y10
Y11
Y12
Y13
Y14
Y15
Y16
Y17
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
Y9
Y10
Y11
Y12
Y13
Y14
Y15
Y16
Y17
read
pointer
Problem: not causal!

## Slide 7: Block-based output: causality
For causal system, output cannot depend on future inputs
Partial solution: add 1-window latency to output
  As we gather input samples for next FFT, copy samples from last FFT into output
...
Block 0
Block 1
Block 2
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
...
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
...
Block-based
processing
Block-based
processing
Block-based
processing
Block-based
processing
x[n]
y[n]
Problem: y[0] depends on x[5]. System is not causal!

## Slide 8: Overlapping blocks
Useful to have overlapping blocks
# samples between consecutive blocks is hop size
  Often fraction of block size (or window size)
  For example, FFT size 1024, hop size 512
Might apply window before calculating FFT
Window size = M
Hop size = M/2

## Slide 9: Overview of Overlap and Add Process
FFT
IFFT
Frequency Domain
Processing
...
...
+
+
+
+
+
+
x[n]
y[n]
Break input signal into windows
Add results of each IFFT to output
Hop Size
Window Size
for each window:
...
...
Take mth segment of length M using windowing function
Take FFT of length N ≥ M of segment
  If N > M, zero-pad the segment (add zeros to end)
  Extract amplitudes and phases
Do something to frequency data
Take IFFT to get new time domain segment
Add result to output buffer containing prior segments
Advance by hop size to (m+1)th frame and repeat

## Slide 10: Review: overlapping blocks (input side)
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
...
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
Goal is to work with overlapping blocks in real time
  This means block k shares some samples with block k-1
  How do we adapt our windowing code to handle this?
Easiest approach: keep running history of input samples
  i.e. buffer which always has last M samples
  What kind of structure does this?
  At each hop, pass M samples from circular buffer to FFT
x[n]
y[n]
Circular buffer

## Slide 11: Review: overlap-add with a circular buffer
Use circular buffer to keep track of input
Necessary characteristics:
  Buffer always holds (at least) last M input samples (where M is the window size)
  If using multiple channels, one buffer per channel
Using circular buffer:
  Each iteration of for() loop:
    store input in buffer
    increment write pointer (wrapping as necessary)
    increment total count of samples stored
  When count reaches hop size:
    take one window from buffer, unwrap it, and pass it to FFT
    i.e, copy it to new buffer such that oldest sample appears at index 0 of new buffer
x[24]
x[12]
x[18]
x[6]
x[3]
x[25]
x[26]
x[4]
x[5]
x[7]
x[8]
x[9]
x[10]
x[11]
x[15]
x[14]
x[13]
x[16]
x[17]
x[19]
x[20]
x[21]
x[22]
x[23]
write pointer
(next sample to
be replaced)
latest
window
(M = 8 in this
example)
Not same as when write
pointer wraps around!

## Slide 12: Review: unwrapping the circular buffer
x[24]
x[12]
x[18]
x[6]
x[3]
x[25]
x[26]
x[4]
x[5]
x[7]
x[8]
x[9]
x[10]
x[11]
x[15]
x[14]
x[13]
x[16]
x[17]
x[19]
x[20]
x[21]
x[22]
x[23]
write pointer
(next sample to
be replaced)
latest
window
(M = 8 in this
example)
x[24]
x[25]
x[26]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
x[13]
x[14]
x[15]
x[16]
x[17]
x[18]
x[19]
x[20]
x[21]
x[22]
x[23]
How circular buffer stored in memory:
What we need to calculate FFT (latest 8 samples):
x[19]
x[20]
x[21]
x[22]
x[23]
x[24]
x[25]
x[26]
In other words: having assembled samples into circular buffer, on each hop it is helpful to copy them into linear (standard) buffer to pass to FFT library

## Slide 13: Block-based output: overlap
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
Need intermediate output buffer (different from system audio output) to hold results of block-based calculation
  Each window, new output should be added into that buffer
  Sample can be sent from there to system output as soon as all blocks it depends on have been calculated (implies latency of at least 1 window)
x[n]
Block-based
processing
Block-based
processing
Block-based
processing
Block-based
processing
Block-based
processing
output
buffer
These output
samples are sum of parts of two different blocks

## Slide 14: Output circular buffer
Circular buffer to get output from overlap-add
  Different from input circular buffer
Keep track of 2 pointers in circular output buffer
  Write pointer: where does next block get written?
    moves in jumps of hop size
  Read pointer: where to get next sample for output?
    moves continuously frame by frame
  Write pointer must remain ahead of read pointer
Necessary characteristics of the output buffer:
  Hold at least W+H samples, for W window size, H hop size
  One buffer per channel of signal
  Need array, write pointer from FFT & read pointer to system output
Using output buffer:
  After inverse FFT, add result to output buffer, starting at write pointer
  In processBlock, copy from output buffer to audio output at read pointer
  Then set sample you just copied to 0
  Finally, increment read pointer
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
read
pointer
write
pointer
Output
circular buffer:

## Slide 15: The full signal chain
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
x[n]
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
...
y[n]
write
pointer
input
buffer
Block-based
processing
Apply
window
output
buffer
add
result
at write
pointer
most
recent W
samples
read pointer
these processes
happen every frame
happens once per hop (every H samples)

## Slide 16: The full signal chain: added latency
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
x[n]
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
...
y[n]
write
pointer
input
buffer
Block-based
processing
Apply
window
output
buffer
add
result
at write
pointer
most
recent W
samples
read pointer
We have 1 full hop to
finish FFT calculations