## Slide 1
Fundamentals
Notes: We assume some knowledge of DSP as a prerequisite, but these concepts will get us started with or without it.

## Slide 2: But first…

## Slide 3: Continuous and discrete time
t is a continuous variable
(any real value)
n is a discrete variable
(only defined for integers)
The physical world is continuous in space and time
  Audio signals are (continuous) pressure waves
  In analogue audio equipment, audio is represent by continuous voltage and current
Computers are discrete systems
  Limited temporal and spatial/amplitude resolution

## Slide 4: Sampling
Discrete sequences do not have to represent any continuous or physical quantity
  In the audio world, we often work with sampled audio
Sampling = converting continuous time to discrete
Reconstruction = discrete to continuous
T is called the sampling period
  1/T is the sampling frequency or sample rate (fs)

## Slide 5: Sampling 2
Reconstruction is harder than sampling
  Sampling inherently loses information
  How do we distinguish between these two cases?
Need a band-limited input signal
  Limited frequency range
Nyquist Sampling Theorem
  Need to sample a signal at twice its highest frequency to be able to uniquely reconstruct it
  This frequency is called the Nyquist frequency

## Slide 6: Aliasing
Two sinusoids, one with frequency 0.3fs and the other with frequency 0.7 fs. They appear identical when sampled at frequency fs.

## Slide 7: Sampling and audio
What is a good sample rate for audio signals?
  What’s the range of human hearing?
    20Hz - 20kHz (approximately)
  Suggests fs > 40kHz to accurately sample audio
What do we do if our signal isn’t band-limited?
  Filter it: lowpass filter removes high frequencies
  Every audio ADC (*analogue-to-digital converter) has an analogue front-end to prepare the signal before it is digitised
  Similarly, every audio DAC has analogue post-filtering to remove digital artefacts
Sample rates in practice:
  44.1kHz, 48kHz, 96kHz, 192kHz (why?)
    Analogue filters not ideal: need extra margin
    Some digital processing better done at higher sample rate
Notes: ADC / DAC design is a fascinating topic, but unfortunately beyond the scope of this text. We will assume digital signals as a basis, but we should know where they come from.

## Slide 8: Sampling and audio 2
Digital systems are limited in precision as well as sample rate
  Each sample stored with a fixed number of bits (bit depth)
  Bit depth determines number of discrete levels that can be represented
    8 bits = 28 = 256 levels
    16 bits = 216 = 65536 levels
    24 bits = 224 = 16777216 levels
Bit depth determines maximum dynamic range
  Ratio of loudest to softest signal
  Human hearing: 140dB dynamic range
decibel scale
for N bits
Notes: How many bits are theoretically required to represent the dynamic range of human hearing? Why can’t we represent the whole range in practice?

## Slide 9: Sampling and audio 3
Other reasons we care about bit depth
  Why not use as many bits as possible?
    Memory, computational complexity
  Quantisation noise
    Error left over from digitising a signal
    Purely digital effects can also generate quantisation noise
    Rounding error on calculations, etc.
Sampling bit depth ≠ processing bit depth
  High-end ADCs sample at 24 bits
  Audio processing done at 32 or 64 bits, floating point
    Single or double precision (contrasts with fixed point)
IEEE 754 single-precision floating point (Wikipedia)
Notes: On computers, it’s common to process audio at a higher bit depth than it is sampled at. This minimises numerical errors during calculations and potentially even prevents instability in certain effects. Most of the time, calculations are done in floating point, where some of the bits are reserved to hold information on the scale of the number. Floating point can represent a greater range of values than fixed point, but it is more computationally expensive. Many low-power DSP systems are fixed point, which is computationally equivalent to working with integers and thus much easier. A greater burden is placed on the programmer to understand the proper scale of each variable in this case.

## Slide 10: Useful digital sequences
Impulse
  for n = 0; 0 otherwise
  For LTI systems, we’ll often talk about impulse response
Step
  for n >= 0; 0 otherwise
Exponentials
  Right-sided exponential:
Convolution of two signals

## Slide 11: Properties of digital systems
Linearity:
Time invariance:
  Linear, Time-Invariant (LTI) systems are a common useful case
Stability:
  x[n] bounded y[n] bounded
Causality:
  x[n] = 0 for n < 0 y[n] = 0 for n < 0
  f doesn’t depend on any future sample (i.e. greater n)
Memorylessness:
  y[n] only depends on the current value of x[n]
f
x[n]
y[n] = f(x[n])
Notes: Useful properties to know. Which audio effects satisfy or break these properties?

## Slide 12: Complex number a+jb=rejq depicted in the complex plane. Unit circle, cosq+j sinq =ejq is also depicted.
q
Imaginary axis
Real axis
r
a
b

## Slide 13: Time domain block diagram of a digital linear filter
Delay
Delay
...
Sum
Delay
Delay
...
x[n]
y[n]
-a1
-aN
b1
bN
b0

## Slide 14: Z-domain block diagram of a digital linear filter
z-1
z-1
...
z-1
z-1
...
X(z)
Y(z)
-a1
-aN
b1
bN
b0
+

## Slide 15: Pole zero plot (a), impulse response (b), magnitude response (c) and phase response (d) of a digital linear filter
(a)
(c)
(b)
(d)

## Slide 16: Buffering
How do we implement an effect in practice?
Two memory buffers
  One contains the input signal, the other starts empty
  Go through sample-by-sample, run a function on the input to calculate an output sample
    The function could depend on the current sample, or any combination of previous samples (see casuality and memorylessness)
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
y[0]
y[1]
y[2]
y[3]
y[4]
y[5]
y[6]
y[7]
y[8]
y[9]
y[10]
y[11]
y[12]
. . .
. . .
. . .
. . .

## Slide 17: Buffering
Audio signals could be of any length
  For real-time signals, we don’t know the length
  We can’t hold all this in memory at once
  Fortunately, once we’ve played back a sample or recorded it to disk, we can usually forget about it
Moving audio samples in memory is wasteful
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
x[13]
NO (don’t move 11 samples to add 1)

## Slide 18: Buffering FIX
Some pseudocode...
x=zeros(100,1);
X[1]=1; % unit impulse signal of length 100
g=0.5;
Delayline=zeros(10,1); % memory allocation for length 10
for n=1:length(x);
y[n]=x[n]+g*Delayline[10];
Delayline=[x(n);Delayline(1:10-1)];
end;
Inefficient
(though it’s fine to demonstrate the concept)
Useful C/C++ points:
Arrays / buffers are indexed starting at 0 in C/C++ (versus 1 for matlab)
Use brackets to access elements of an array (like our [] notation)
Semicolon ends a line

## Slide 19: Circular buffering
Circular buffer acts like a loop
  Write from beginning to end, then go back to the beginning again
  Always holds the most recent samples without moving them
  Keep track of the write pointer to know where you are
  Implemented with modulo arithmetic
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
YES (samples stay in place)
x[12]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
x[13]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
write pointer

## Slide 20: Buffering in real-time
Another reason to buffer audio samples
  44.1kHz audio has a sampling period of 22.6µs
  Modern multitasking OSes put many demands on the CPU
    Processor won’t be available for audio every 22.6µs
  Solution: collect multiple samples into a buffer to process
  Typical buffer sizes: 32 to 1024 samples
    Usually a power of 2 for computational efficiency
What’s the tradeoff?
  Latency
    Delay from input to output
  Can be a big problem for DAFX
    Musicians can detect latencies as low as 2ms
  Keep buffer as small as possible before dropouts

## Slide 21: Time and frequency domain
Any digital signal can be represented as a sequence of samples (known as the time domain)
  ..., x[-2], x[-1], x[0], x[1], x[2], ...
It can also be represented as a sum of sinusoids
  Again, true of any signal! (not just periodic ones)
=

## Slide 22: Time and frequency domain
So any x[n] can also be represented as a sum of sinusoids...
  So let’s do that then!
Our time domain signal is...
the sum
of weighted
sinusoids
*with a scaling factor we’ll talk about in a bit
means add up the function f(k) for every
(integer) value of k between 0 and N-1
is a complex exponential (ex when x is complex produces a complex cosine/sine wave)

## Slide 23: Time and frequency domain
So any x[n] can also be represented as a sum of sinusoids...
  So let’s do that then!
  The second version is called the frequency domain representation of x
    * or at least discrete samples of the frequency domain...
  What frequencies are present, with what amplitude and what phase? From this we can exactly determine x[n].
We will use both time domain and frequency domain to understand digital audio effects

## Slide 24: Fourier transforms
This equation:
  ...is known as the Inverse Discrete Fourier Transform (IDFT)
The Fourier Transform is a mathematical formula which converts from time to frequency domain
  The traditional Fourier Transform is for continuous-time signals
  The Discrete Fourier Transform (DFT) is the same idea for discrete-time sequences (and discrete frequencies)
The DFT: time frequency
The IDFT: frequency time
*and the scaling factor makes DFT IDFT balance out

## Slide 25: The FFT
The DFT finds the frequency content of a discrete-time (finite length) signal
So what’s the FFT?
  Fast Fourier Transform
  It’s just a fast algorithm for calculating the DFT!
Whenever we see a spectrum in digital audio, it has been calculated with the FFT
Time
Frequency (post-FFT)

## Slide 26: DTFT and z-transform
Discrete-Time Fourier Transform of a digital sequence
  Samples of x[n] referred to as time domain
  Values of known as frequency domain
    Notice that this function is continuous
    represents frequency: ranges from 0 to 2π
    Contrast this to continuous-time frequency
z-transform is an abstraction of the DTFT
  Useful for assessing behaviour of discrete time systems
  DTFT is a special case
Notes: This takes a bit of maths to justify, and we will assume it’s familiar from a previous DSP module. See any DSP text for the derivation and significance

## Slide 27: The time domain waveform (a), frequency domain power spectrum (b) and spectrogram of a 3 second excerpt of solo guitar performance.
(c)
(b)
(a)