## Slide 1: Overdrive, Distortion and Fuzz

## Slide 2: Terminology
Overdrive, distortion and fuzz used primarily by guitar players
  Sometimes used interchangeably, but sometimes a distinction
Overdrive
  Becomes nonlinear when driven with signal above operating range
    Operation linear for softer signals, nonlinear for louder signals
  Characteristic sound comes from nonlinear region
    Warm, smooth sound in nonlinear region
Distortion
  Operates in nonlinear region
  Signal reaches point of clipping where output fixed to maximum level
  Used for metal and grunge sounds
Fuzz
  Completely nonlinear effect
    Harder, harsher sound than distortion
  “Buzzy” sound with long sustain

## Slide 3: Grunge

## Slide 4: Clipping
Simplest form of distortion: clip the waveform
  Apply an input gain and hold the output to a fixed max value
  Known as hard clipping (abrupt transition)
  Aggressive, bright sound
Input
Output
Transfer function (G = 5)
Example (G = 1.2)
Time
Input
Example (G = 5)
Output
  Sound examples: original, G = 10, G = 100
  Music example: Beatles Revolution

## Slide 5: Soft clipping (overdrive)
Most analogue systems have smooth transition from linear to nonlinear
  Rounded tops of waveforms known as soft clipping
Notice: G = 2
Characteristic input/output curve for a quadratic distortion.

## Slide 6: Effect of soft clipping on a decaying sinusoid

## Slide 7: Soft clipping of a sine wave with four different input gains.

## Slide 8: Comparison of hard and soft clipping.

## Slide 9: Spectrum after distortion has been applied for sinusoidal input
Varying distortion level, soft clipping soft and hard clipping

## Slide 10: Soft clipping
Another implementation of soft clipping
  Exponential function grows gradually more nonlinear as input gain increases
  Asymptotically approaches clipping point
  Sound examples: hard, soft (G = 10)
Input
Output
Transfer function (G = 5)
Time
Output
Hard vs. Soft clipping (sine input)

## Slide 11: Distortion in the frequency domain
Distortion is a nonlinear effect (why?)
  Nonlinearity introduces new frequency components that weren’t present in original signal
Bin #
Magnitude (dB)
Fourier Transform: Sine input
Bin #
Magnitude (dB)
Fourier Transform: Hard clipping (G = 5)

## Slide 12: Distortion in the frequency domain
Spectrum depends on amount and type of distortion
What’s special about the location of the new components?
  Harmonics (multiples) of the original, and specifically...
  Odd harmonics
Bin #
Magnitude (dB)
Hard clipping: G = 1.2, 5, 1000
Bin #
Magnitude (dB)
Soft clipping: G = 1.2, 5

## Slide 13: Waveshapers and harmonics
Waveshaper: any function mapping current input sample to current output sample
  No memory dependence
Three questions
  Do waveshapers produce only harmonic distortion for sinusoidal input?
  Do waveshapers produce inharmonic distortion for nonsinusoidal input?
  What distortion results when the waveshaper is an odd or an even function?

## Slide 14: 1. harmonic distortion
Do waveshapers produce only harmonic distortion for sinusoidal input?
Any function can be approximated as a polynomial series expansion
Assume the input is a complex sinusoid
So
 only harmonics (multiples) of the input frequency

## Slide 15: 2. inharmonic distortion
Do waveshapers produce inharmonic distortion for nonsinusoidal input?
Any function can be approximated as a polynomial series expansion
Assume the input is a sum of complex sinusoids
So
Yes! Sum of input frequencies, not just multiples

## Slide 16: 3. Symmetry and harmonics
What distortion results when the waveshaper is an odd or even function?
Odd function:
  Examples: Most op-amp, transistor, digital systems
Even function:
  Examples
Important property
  Sum of odd functions is odd
  Sum of even functions is even
  Sum of odd and even functions is neither (unless one of them is 0)

## Slide 17: 3. Symmetry and harmonics
What distortion results when input is odd or even function?
  Sum of odd functions is odd
  Sum of even functions is even
  Sum of odd and even functions is neither
So
  So if f is odd
  If f is even
  For complex sinusoid
Odd functions produce odd harmonics
Even functions produce even harmonics

## Slide 18: Waveshapers and harmonics
Waveshaper: any function mapping current input sample to current output sample
  No memory dependence
Answers to three questions
  Waveshapers produce only harmonic distortion for sinusoidal input
  Waveshapers produce inharmonic distortion for nonsinusoidal input
  Even functions give even harmonics, odd functions give odd harmonics, for sinusoidal input

## Slide 19: Analogue and digital
Why soft clipping is a good simulation
Most fuzz boxes (overdrive units, distortion pedals) use diodes to clip the signal
  Could theoretically simulate the characteristics of the particular diode

## Slide 20: Tube distortion
Many guitarists still prefer vacuum tube amps
  Tube distortion has warmer, “bluesier” sound than transistor distortion (hard or soft)
  original information about what input wave used to be not lost, just compressed
  Form of soft clipping, with two major differences:
  Sound examples: clean and tube-like distortion
  Simulating a real tube amplifier is hard!
    Most emulations are not perfect replicas
1. More rounded edges
2. Asymmetrical

## Slide 21: Spectrum of a single sine wave before and after asymmetric distortion has been applied

## Slide 22: Tube distortion
Tube distortion produces even harmonics
  Often a combination of even and odd

## Slide 23: Rectification
Another form of asymmetrical distortion
  Full-wave rectification flips the negative half of the signal
    Equivalent to absolute value function
  Half-wave rectification passes only the positive half
  Both forms produce strong octave harmonic (2x frequency)
    Full-wave rectification eliminates the fundamental frequency
  Used in many fuzz pedals:
    Tycho Brahe Octavia, UniVox SuperFuzz,
    Foxx Fuzz-Wah, and Foxx Tone Machine

## Slide 24: Rectification
Spectrum shows even harmonics
  Notice component at DC (f = 0)
  Half-wave = full-wave + original (mathematical identity)
  Sound examples: clean, half-wave, full-wave
Bin #
Magnitude (dB)
Spectrum: full wave rectification
Bin #
Spectrum: half wave rectification

## Slide 25: Intermodulation distortion
The bane of fuzzbox technology
Trig. identity:
  Sum and difference frequencies are products of intermodulation between inputs
  When we apply nonlinear distortion, intermodulation products will show up in the spectrum
  If two tones are harmonically-related
    Intermodulation products will be harmonically-related as well
  If two tones are not harmonically-related
    Intermodulation produces will be harsh and dissonant
    Exact guitar tuning is especially important when using distortion!
  Goal: maximise harmonic distortion, minimise intermodulation distortion

## Slide 26: Spectrum of two sinusoids before and after distortion applied

## Slide 27: Aliasing
Products of distortion are not band-limited
  Harmonics that exceed Nyquist frequency are folded back into spectrum
Bin #
Magnitude (dB)
Exponential (soft clipping) distortion: aliasing
8192-point FFT
(4096 = fs/2)

## Slide 28: Aliasing
One possible solution
  Operate at higher sampling rate, filter & downsample
Bin #
Magnitude (dB)
Same distortion at 4x sampling rate
Original frequency range (now 0-fs/8)
Bin #

## Slide 29: Output spectrum with aliasing due to distortion, and output spectrum after oversampling, lowpass filtering and downsampling.

## Slide 30: Memory and analogue simulation
Nonlinearities discussed earlier are memoryless
  Current output depends only on current input
  Real fuzz boxes don’t work this way
The nonlinearity depends on diodes and RC filter
  RC (lowpass) filter in particular has a memory effect
Simple approach: lowpass filter, then nonlinearity
  Nonlinearity can be calculated by lookup table
But the two components aren’t truly independent!
  Current through diode affects the operation of the RC filter.
D. Yeh, J. Abel , J. Smith. Simulation of the diode limiter in guitar distortion circuits by numerical solution of ordinary differential equations. Proc. Digital Audio Effects (DAFX) 2007.

## Slide 31: Analogue modelling references
D. Yeh, J. Abel and J. O. Smith. Simulation of the diode limiter in guitar distortion circuits by numerical solution of ordinary differential equations. In Proc. Digital Audio Effects (DAFX) 2007.
D. Yeh, J. Abel, A. Vladimirescu and J. O. Smith. Numerical methods for simulation of guitar distortion circuits. Computer Music Journal 32(2), pp. 23-42, 2008.
J. Pakarinen and D. Yeh. A review of digital techniques for modeling vacuum-tube guitar amplifiers. Computer Music Journal 33(2), pp. 85-100, 2009.
J. Pakarinen and M. Karjalainen. Enhanced wave digital triode model for real-time tube amplifier emulation. IEEE Transactions on Audio, Speech, and Language Processing 18(4), pp. 738-746, 2010.

## Slide 32: Distortion code
int numSamples; // Indicates how many audio samples to process
float *channelData; // Array of audio samples, length numSamples
float inputGain; // Input gain (linear scale), before distortion
float inputGainDecibels_; // Gain in decibels, from the user control
int distortionType_; // Index containing the type of distortion
// Calculate input gain once to save calculations
inputGain = powf(10, inputGainDecibels_ / 20);
for (int i = 0; i < numSamples; ++i) {
const float in = channelData[i] * inputGain;
float out;
…[SEE NEXT SLIDE]
// Put output back in buffer
channelData[i] = out;
}

## Slide 33: Distortion code- Apply distortion based on type
if (distortionType_ == kTypeHardClipping) {
float threshold = 1;
if(in > threshold) out = threshold;
else if(in < -threshold) out = -threshold;
else out = in;
}
else if (distortionType_ == kTypeSoftClipping) {
float threshold1 = 1/3, threshold2 = 2/3;
if(in > threshold2) out = 1;
else if(in > threshold1) out = (3-(2-3*in) * (2-3*in))/3;
else if(in < -threshold2) out = -1;
else if(in < -threshold1) out = -(3-(2+3*in) * (2+3*in))/3;
else out = 2* in;
}
else if (distortionType_ == kTypeSoftClippingExponential) {
if(in > 0) out = 1 - expf(-in);
else out = -1 + expf(in);
}
else if (distortionType_ == kTypeHalfWaveRectifier) {
if(in > 0) out = in;
else out = 0;
}
else if (distortionType_ == kTypeFullWaveRectifier) out = fabsf(in);