## Slide 1: Mixing Consoles

## Slide 3: Mixing console overview
Mixing console/mixing desk/audio mixer
  Device for combining, routing, and modifying audio signals
  Analog or digital signals, depending on type
  Modified signals summed to produce output
Main functions
  Summing: combining audio signals
    Many channels summed to stereo or mono via mix bus
  Processing: modifying audio signal properties
    Consoles often have on-board equalisers and dynamics processors
  Routing: grouping, sending and receiving signals
    Enable use of external processors and effects
    Insert points, auxiliary sends and receives

## Slide 4
What’s going on here??

## Slide 5: Two main sections
Channel section
  Collection of channels organised in physical strips
  Each channel corresponds to individual track on multitrack recorder
  Most channels support mono input; some support stereo
  Some channels will have different types of equalisation, etc.
Master section
  Central control over console (global functionality)
  Includes master aux sends, effect returns, control room level, ...

## Slide 6
Channel
Master

## Slide 7: A simple channel strip having only a cut control, a panning knob and a level fader, and corresponding signal flow diagram.
Cut
Panning
Fader
Fader
Panning
Input
yL[n]
G
GL
GR
yR[n]
x[n]
Output
Cut

## Slide 8: Channel strip and associated block diagram, with additional controls
Compressor
Cut
f
Clipping
Indicators
Panning
Fader
Gain
Parametric EQ
Inserts
Polarity
Gain
Freq
Q
Gain
Freq
Gain
Freq
Low shelf
High shelf
Low-mids
Gain
Freq
Q
Mid-highs
Thresh.
Ratio
Attack
Release
Peak/RMS
Clipping
Indicator
EQ
Compressor
Fader
Panning
yL[n]
G
GL
GR
yR[n]
Input
x[n]
Output
Cut
Gain
+/-1
Phase
Insert
dynamics (compressor) and frequency (parametric equalizer) processing

## Slide 9: Signal flow diagram and user interface for simple mixing console with 4 channels and a master section.
Channel strip
Channel strip
Channel strip
Channel strip
yL[n]
G
yR[n]
x1[n]
x2[n]
x3[n]
x4[n]
Master
Fader
G
Summing
amplifier
1 2 3 4
Master
Fader
Channel Section
Master Section
Cut
Cut
Cut
Cut
Meter

## Slide 10: About our simple console
Each channel has its own controls; fader, pan pot, cut (mute) switch…
  Line gain: boost or attenuate level before signal enters channel path
  Phase invert: flips sign (polarity) of signal
  Clip indicators: show when signal exceeds a threshold (red)

## Slide 11: Busses
Buss or bus
  common signal path to which many signals can be mixed
  Summing amplifier used to combine multiple sources
On typical large console:
  Mix buss
  Group busses
  Auxiliary busses
  Solo buss

## Slide 12: On-board processors
Most consoles offer some on-board processing for each channel
  Basic tone controls
  Filter section
  Dynamics section
For example:
  Processors in signal path between phase and cut stages
    High pass filter, equaliser, basic compressor

## Slide 13: Insert points
Signal flow
Insert
return
engaged
Insert
Insert
send
Insert
return
Insert
Insert
send
External processor
External processor
Insert external device into signal path
  Breaks signal path
  Diverts existing signal to external device
  Return allows externally processed signal to replace original
Most consoles send signal to insert send socket
  Insert button determines whether return replaces original

## Slide 14: Auxiliary sends
Aux send: Copy signal and route to internal auxiliary buss
  Buss routs to output socket
  Can feed external effect unit
Each channel strip has set of controls related to aux send
  Level control
  Pre/post fader switch
  Pan control
  On/off switch
Can send each channel to same aux buss
  Insert sends: 1 ch. per effects unit
  Aux sends: share effects between ch.
Cut
Aux 1 Bus
Channel
fader
Channel
fader
Local aux
send level
Master aux
send level
Local aux
send level
Aux 1
Send output
Signal flow for auxiliary sends

## Slide 15: FX returns
Sometimes called aux returns
Stereo inputs that can be routed to mix buss
Often with dedicated mute and level controls
When there are free channels
  Can bring back effect into channel rather than FX return
  Channels offer more processing options

## Slide 16: Control groups
Two types of groups: control and audio
Control groups
  Allocate a set of channels to control simultaneously
  Moving one fader moves all others automatically
  Audio signals are still separate (no alteration of signal path)
Audio groups
  Subgrouping
    Sum group of audio signals to group buss
    Acts as submix that can be processed and routed to main mix buss
    Used to handle many audio signals collectively
  Group busses are mono
    Often used together in stereo pairs
  Consoles can be described by the format channels : groups : mix-busses

## Slide 17: Audio groups
Routing matrix on channel strip assigns channel to groups
  Located vertically next to fader or separate collection of buttons
Routing matrices come in two formats
  Independent button for each group buss or
  Button for each (stereo) pair of groups
1
3
5
2
4
6
L/R
5-6
3-4
1-2
L/R

## Slide 18: Terminology: effects and processors
Distinction made by audio recording engineers
Effects are
  Added to original signal
  Encompass dry and wet sounds that can be mixed
    Dry: original sound
    Wet: processed sound
  Often delay-based
    Reverb, echo, chorus, flanging
Processors
  Change whole of a signal
  Generally do not mix with original
    Compressors, gates, equalisers
Distinction often blurred
  We treat them all as digital audio effects
Dry
Wet
75%
Notes: This is a distinction made by audio recording engineers, but not generally made by the audio signal processing community.

## Slide 19: Effects and processors
Connection methods are generally different
  Processors: connect using an insertion point
  Effects: connect using an auxiliary send
  However, there are exceptions
Effect
Notice dry/wet mix
Processor
Dry/wet mix not relevant
Effect
Processor
(a)
(b)

## Slide 20: DAWs, software mixers and sequencers

## Slide 21: DAW – Digital Audio Workstation
Computer for editing, processing digital audio professionally
  high-quality audio hardware
    Multiple ADC/DAC
    High-end Soundcard
  Multitrack audio software
freely manipulate recorded sound
  like word processor manipulates typed words
from 2-channel editor to complete digital recording studio
Computer-based DAWs
  computer
    host for sound card and software
    provides processing power for audio editing
  ADC-DAC sound card
    audio interface
    Convert analog into digital audio
    assist in processing audio
  digital audio editor software
    controls hardware components
    user interface to allow for recording & editing
Integrated DAWs
  Mixing Console
  Control Surface
  Digital interface

## Slide 22: Screenshot of Audacity, a popular open source DAW

## Slide 23: Computer DAW Functionality
Standard layout
  Transport controls
    Play, Rewind, Record, ...
  Track controls
  Mixer
  Waveform display
Multitrack DAWs
  Can operate on multiple tracks at once
  Adjust overall volume, balance of all waveforms in track
    Pan control adjusts balance between speakers
  Plugins can be placed on a track to process the sound
Automation
  Commonly performed through envelope points
  Create and adjust multiple points along waveform
    Specify parameters of sound over time
Each dot
represents
one envelope
point

## Slide 24: MIDI
Musical Instrument Digital Interface
  Industry-standard electronic communication protocol (since 1983)
  Serial interface (3.9 kBps) with defined set of messages
  Defines each musical note in an electronic instrument
    Allow instruments and computers to exchange data
MIDI does not transmit audio
  Transmits digital symbolic information about a performance

## Slide 25: MIDI
Example MIDI messages
Note On / Note Off
Note #, Velocity
Control Change
Control #, Value
e.g. Modulation, Pan, Effect Levels
Pitch Wheel
Pitch value (up / down)

## Slide 26: Sequencers
Program in computer or stand-alone keyboard
  Record & edit musical performance without audio input
  Performance recorded as MIDI events
    What (virtual) instruments played
    What note played, when, and how loud
      How hard key was pressed (velocity)
    When did sustain pedal (or other controls) get pressed
  Data played back into MIDI synth or sound module
Can change sound without re-recording
  e.g. select piano, later decide to change to organ
Multiple modules can use different MIDI channels
  Layer sounds / instruments to create orchestra

## Slide 27: Sequencers
Most modern sequencers now feature audio editing and processing capabilities
  Sequencers DAWs
Sequencer
in Cubase

## Slide 28: Sequencers
Some sequencers used for live performance as well as composing / arranging
  Also precision mixing by DJs
Ableton
Live

## Slide 29: Tracks and mixer strips
No separation between multitrack and the mixer
Multitrack represented as sequence window
  Also known as arrangement, edit or project window
  Shows tracks and audio regions
Lose the channels, just tracks and mixer strips
  New track in sequence window creates a new mixer strip in mixer window
Mixer strips
  Similar to channel strips on consoles
    Have input
    Signal flows through specific path
    Routed to output

## Slide 30: Tracks and mixer strips
Multitrack represented as sequence window
  Shows tracks and audio regions
  New track in sequence window creates a new mixer strip in mixer window
Sequence / Audio Editor Window
Mixer Window

## Slide 31: Tracks
Audio: raw tracks and their audio regions
Aux
  Audio grouping and to accommodate effects as part of an aux send
  Sometimes called FX channel or group channel
Master: most commonly main stereo buss
  In sequence window, these tracks only display automation data
MIDI: record, edit and output symbolic information
  Sometimes used during mixing to automate external digital units or store/recall their state and presets
  Might be used for drum triggering
Instrument: contain MIDI data
  Converted to audio by virtual instrument
  Look and behave like audio tracks
...

## Slide 32: Mixer strips
Similar to channel strips on consoles
  Have input
  Signal flows through specific path
  Routed to output
Cut
…
…

## Slide 33: Mixer strips
Signal flow
Single line can denote mono or stereo path throughout

## Slide 34: Mixer strips
Input selection
  What signal feeds strip
  Either busses or physical audio inputs
  Audio strips fed from audio regions in sequence window
Output selection
  Routes strip to buss or physical audio output
Inserts
  Load plug-ins in series to signal path
  Add effects and processors
Sends
  Feed either pre-fader or post-fader signal to buss
  Each send can be routed to different buss

## Slide 35: Control grouping
Each track can be assigned to 1 or more groups
  Can select which properties to group
  Much more functionality than mixing consoles

## Slide 36: Audio grouping
Software mixers do not provide routing matrices
  Set output of each included track to bus
  Feed bus into auxiliary track
Process each track individually using inserts
Process audio group using inserts on aux track

## Slide 37: Sends and effects
Effects added using send
  Tracks sent to buss
  Buss fed to aux track
  Effect plug-in loaded as insert on aux track
  Aux track has output set to stereo mix

## Slide 38: Recommended text
See Roey Izhaki’s Mixing Audio for an excellent discussion of mixing consoles and DAWs, their architecture and their use.