## Slide 1: Choosing an FFT size
Previous formulas gave us one frequency component for each bin
  FFT of size N has (N/2+1) unique bins after accounting for symmetry
  Tells us maximum number of frequency components we can represent
N time-domain samples ↔︎ N frequency-domain bins
Larger FFT  greater frequency resolution
  Bins spaced more closely together in frequency: 2πk/N
  Easier to resolve two closely-spaced frequency components of signal
Trade off:
  Fundamental mathematical limitations
  Resolving short transient events within long time window is difficult
Poor time resolution, long latency

## Slide 2: Choosing a hop size
How often should we take FFT?
  If we want to reconstruct signal, hop size H must be no more than FFT size N
Advantages of smaller hop sizes
  More frequent time snapshots of signal
  Phase of each bin advances less from one hop to next,
  improving frequency estimation
  Some types of window need a hop size of N/2, N/3 or even less to reconstruct the signal
  Lower latency for phase vocoder effects
Disadvantages of smaller hop sizes
  More computationally expensive
  Hop sizes that aren’t integer division of FFT size can lead to reconstruction artifacts
H = N
H = N/2
H = N/4

## Slide 3: Windowing
Overlap-Add process segments signal into finite-length windows
  These segments can have discontinuities at the edges (assuming 0 outside the window)
  Might not notice this if we just reconstruct the signal with no frequency-domain processing
  If we modify signal, these sharp edges can lead to crackling or buzzing sounds
Can use window function to taper the edges
  Pre-calculated shape that we multiply the segment by before FFT
H = N/4
sharp edges
Hann window

## Slide 4: Types of window function
Rectangular
Triangular (Bartlett)
Hann
Hamming
for

## Slide 5: Effect of rectangular window and Hann window applied to signal

## Slide 6: Window spectra
Hann-windowed
spectrum
(frequency smearing)
Windowing lets us isolate segment of signal
Cost is smearing of energy in frequency domain
  Energy appears at frequencies where it doesn’t exist in original signal
Each frequency component of signal appears as series of lobes
  Main lobe: broad peak centred around actual frequency
  Side lobes: secondary peaks at other frequencies
Typically want to minimise:
  Main lobe width
  Side lobe height
ideal signal
(all energy at one
frequency)
Main lobe width
(expressed in
frequency)
Side lobe height
(expressed in dB)

## Slide 7: Coding a window
Most efficient to pre-calculate window when program starts
  Then recalculate when settings change: window size, window type etc.
Store window in an array (typically a global variable)
  Array length equal to window size
To calculate, use for() loop to iterate over each sample of window
To apply, multiply signal by window buffer frame-by-frame
  Could do this while unwrapping circular buffer
for(unsigned int n = 0; n < windowSize; n++) {
windowedSignal[n] = originalSignal[n] * windowBuffer[n];
}
const int windowSize = 1024;
float windowBuffer[gWindowSize];
for (n = 0; n < windowSize; n++)
windowBuffer[n] =
equation for window