## Slide 1: Mutation
DFT bins have magnitude and phase
Suppose we have DFTs of two signals
  Combine magnitudes and phases in interesting combinations
  Sometimes known as cross-synthesis or morphing
  For example, magnitude from one, phase from other

## Slide 2: Mutation
Example operations on magnitude only
  Multiplication: r = r1 * r2
    Multiplication in linear terms = addition in dB scale
    Similar to spectral AND operation, keeping zones where energy is located in both signals
    For fixed r2 (and zero phase z2), equivalent to FIR filtering
  Addition: r = r1 + r2
    Similar to spectral OR operation
    Not simple mixing: only operating on magnitudes, not phases
  Masking: r = (r2 > threshold ? r1 : 0)
    Keep magnitude of one sound only if the other is above a threshold
    (A ? B : C) syntax means “if A, then B, otherwise C”

## Slide 3: Mutation
Phase is critical to time-frequency representations
  Explains how signals evolve from frame to frame
  Has an important influence on output quality
Example operations on phase of two inputs
  Keep phase of only one sound, change magnitude
    Phase is a strong cue for pitch of sound (why?)
    Result: pitch influenced by the phase you keep
  Add phases
    Strong alteration: phase moves at double speed on average
    Or double the reconstruction hop size: n2 = 2 * n1
  Arbitrary combination or variation on phases

## Slide 4: Denoising
Removal of unwanted low level sounds not intended to be in signal
  Reduce unwanted low level sound on musical recording usually 'hiss' or 'hums'
  Remove artefacts produced by nonlinear operations
  Minimize unwanted low level (generally high) frequencies
Noise from any number of sources
  usually appears as high frequency 'hiss', or low level 'hum'
Goals
  achieve clean crisp signal by reducing overall noise
  Don’t disrupt wanted signal
Denoising performed using analysis and synthesis
  extract magnitude and phase information
  Phase unchanged
  Low magnitudes attenuated

## Slide 5: Denoising
Two basic nonlinear algorithms:
  and
  x is input signal, c is noise reduction coefficient
  Another example implementation:
Similar to applying noise gate
  However, operates on each frequency component
  Only magnitude modified; phase remains as it was
function ft = denoise(f,r,coef)
if abs(f) >= 0.001
ft = f.*(r./(r+coef));
else
ft = f.*(r./(r+sqrt(coef)));
end

## Slide 6: Denoising
Example spectra for windowed FFT of flute sound
  Left: input signal
  Right: output according to with c = 0.01

## Slide 7: Denoising example
Denoising reduces amplitudes of each bin
  Need to boost overall signal level to maintain loudness
    Similar to dynamic range compressor
  In this example, gain of 4.75 to restore level

## Slide 8: Denoising variations
Analyse noise content first
  Apply different nonlinear function to each bin
  For example, reducing ventilation noise in a room
Time-varying noise estimation
  Estimate noise threshold as function of spectrum
  Often involves LPC or cepstral techniques
Use noise estimation to decrease pumping effects
Denoising is nonlinear and can produce artefacts
  Small grains (spurious components) that jump out
  Noise can also be a useful component of a sound