## Slide 1
Low Frequency Oscillators

## Slide 2: Commonly used low frequency oscillator (LFO) waveforms
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 3: Get LFO sample
Function for calculating ‘biased’ LFO waveforms with output range [0, 1]
Phase range [0, 1], output also [0, 1]
  not [-1, +1] as for ordinary Sine function
float PluginAudioProcessor::getLfoSample(float phase, int waveform) {
switch (waveform) {
case 0://Triangle:
if (phase < 0.25f) return 0.5f + 2.0f*phase;
else if (phase < 0.75f) return 1.0f - 2.0f*(phase - 0.25f);
else return 2.0f*(phase - 0.75f);
case 1://square
if (phase < 0.5f) return 1.0f;
else return 0.0f;
case 2://Sawtooth:
if (phase < 0.5f) return 0.5f + phase;
else return phase - 0.5f;
case 3://Sine:
return 0.5f + 0.5f*sinf(juce::MathConstants<float>::twoPi * phase);
}
}
Notes: case 0://Triangle:
if (phase < 0.25f) return 0.5f + 2.0f*phase; // .5 to 1
else if (phase < 0.75f) return 1.0f - 2.0f*(phase - 0.25f);// 1 to 0
else return 2.0f*(phase - 0.75f); // 0 to .5
case 1://square
if (phase < 0.5f) return 1.0f;
else return 0.0f;
case 2://Sawtooth:
if (phase < 0.5f) return 0.5f + phase;// .5 to 1
else return phase - 0.5f; // 0 to .5
case 3://Sine:
default:
return 0.5f + 0.5f*sinf(juce::MathConstants<float>::twoPi * phase);

## Slide 4: Update LFO
In processBlock
float LfoValue = getLfoSample(lfoPhase, lfoType);
…
// Update the LFO phase, keeping it in the range 0-1
lfoPhase += float(lfoFrequency * inverseSampleRate);
while (lfoPhase >= 1.0f) lfoPhase -= 1.0f;
Add private parameters to pluginProcessor.h
float lfoPhase; // Phase of the LFO
float getLfoSample(float phase, int waveform);
Notes: must pass MidiKeyboardState object to initialise MidiKeyboardComponent object

## Slide 5: Keeping track of LFO phase
for n = 0 to (number of samples):
{
m[n] = 1 + alpha*cos(2*pi*f*n/fs);
y[n] = m[n]*x[n];
}
Change of f causes phase discontinuity. Instead,
phase = 0;
for n = 0 to (number of samples):
{
m[n] = 1 + alpha*cos(phase);
y[n] = m[n]*x[n];
phase = phase + 2*pi*f/fs;
}

## Slide 6: LFO code example
float lfo(float phase, int waveform)
{
switch(waveform)
{
case kWaveformTriangle:
if(phase < 0.25) return 0.5 + 2*phase;
else if(phase < 0.75) return 1 - 2*(phase - 0.25);
else return 2*(phase-0.75);
case kWaveformSquare:
if(phase < 0.5) return 1.0;
else return 0.0;
case kWaveformSquareSlopedEdges:
if(phase < 0.48) return 1;
else if(phase < 0.5f) return 1 - 50*(phase - 0.48);
else if(phase < 0.98f) return 0;
else return 50*(phase - 0.98f);
case kWaveformSine:
default:
return 0.5f + 0.5f*sinf(2.0 * M_PI * phase);
}
}