## Slide 1
Flanging

## Slide 2: Story of the flanger
Artificial Double Tracking (ADT)
  Recorded vocal track re-recorded onto second machine
  Second machine has variable (oscillating) tape speed
    Alternatively, change speed with finger on rim (flange) of wheel
  Combine (mix) original and modulated signals
  Irregularities mimic natural variations in human voice when overdubbed
“They often liked to double-track their vocals, but it's quite a laborious process and they soon got fed up with it. So, after one particularly trying night-time session doing just that, I was driving home and suddenly had an idea."
Ken Townsend, Beatles Studio Technician
“I knew he'd never understand it, so I said, 'Now listen, it's very simple. We take the original image and split it through a double vibrocated sploshing flange with double negative feedback...' He said, 'You're pulling my leg, aren't you?' I replied, 'Well, let's flange it again and see.' From that moment on, whenever he wanted ADT he would ask for his voice to be 'flanged,' or call out for 'Ken's flanger.' George Martin, Beatles Producer

## Slide 3: Flanging introduction
First: 2 tape machines playing same tape
  Outputs mixed equally
  Flange of supply reel touched to make it play slower
  Delay develops between machines
Then: flange released, flange of other machine touched
  Delay gradually disappears, grows in opposite direction
  Total delay kept below echo perception threshold
    A few milliseconds in each direction
Repeat as desired, alternating flanges
Flange
y[n]

## Slide 4: Flanging introduction
Characteristic sound referred to as whooshing
  Like jet plane flying overhead
Rapid flanging introduces Doppler effect
  Like Leslie speaker on electric organs
Creates equally-spaced notches in audio spectrum
Later: compare to phaser
  Also based on notches
  Spacing can be arbitrary
  Phaser uses all-pass filters instead of delay
Leslie speaker
Drum loop dry, followed by same loop with flanging applied

## Slide 5: Flanging: how it works
Mix signal with slightly delayed copy of itself
  Length of delay constantly changing
Depth control
  How much delayed signal added to original
Not an echo effect
  Typical delays are 1-10ms
  Human ear perceives echo starts at 50-70ms
+
Delay M[n]
x[n]
y[n]
g

## Slide 6: Flanging: how it works
Feedforward comb filter
Input-output relation: y[n]=x[n]+gx[n- M(n)]
  x[n] - input signal
  y[n] - output signal
  g - depth of flanging effect
  M(n) - length of delay line at sample n
M(n) must vary smoothly over time
  Interpolated (fractional) delay line allows noninteger M
+
Delay M[n]
x[n]
y[n]
g

## Slide 7: Delay and interference
Consider two related signals:
Constructive interference:
  for integer k
Destructive interference:
  for integer k
Interference depends on delay with respect to frequency of the signal

## Slide 8: Delay and interference
(Usually undesired) destructive interference, known as comb filtering, is common in mixing
  Multiple microphones to record single source
  Mixing electric instrument direct signal with acoustic amplified signal
  Parallel signal paths with different latency times
+
Constructive
Destructive
+
(2k+1)π/w

## Slide 9: Frequency response
Delay & add has filtering effect on signal
  Creates series of notches in frequency response
  Eliminates periodically spaced set of frequencies
  Other frequencies passed with amplitude change
Comb filter - notches resemble teeth on comb
Frequency response for two flangers with depth 1.
Which one has smaller delay, and why?

## Slide 10: Frequency response of simple flanger
depth set to 1
delay values are 1, 2, 3 and 4 samples

## Slide 11: Frequency response of a simple flanger
Peaks
Notches
six sample delay, depth set to 1. Locations of 6 peaks & 6 notches over whole frequency range 0 to 2p is shown
Six notches at p/6, 3p/6, 5p/6, 7p/6, 9p/6, 11p/6.
Peaks at 0, 2p/6, 4p/6, 6p/6, 8p/6, 10p/6.

## Slide 12: z-transform and delay theorem
Recall the z-transform
When can find frequency response
  Normalised units, frequency ranges from 0 to 2π
Suppose we know z-transform of a sequence
  Then we have
  and in general

## Slide 13: Amplitude Response
Delay equation:
Z-Transform:
Transfer function:
Frequency response:
Amplitude response:
M peaks in response
Here M = 6, 6 peaks
Peaks move slowly over time by changing M
Peaks
Notches

## Slide 14: Amplitude response
Peaks located at:
When depth g = 1:
  Peaks maximally pronounced
  M notches
    Elimination of sound at single frequency or narrow freq. interval
Notches (or minima) located at:
  g < 1 will produce less-than-complete attenuation
Peak / notch spacing at intervals of fs/M Hz
  fs is sample rate
Time variation of delay-line length M[n]
  Flanging created by moving notches in spectrum
  Notch motion essential for flanging effect
    Static row of notches sounds like being in an acoustic tube
    Isolated notch may be inaudible

## Slide 15: Sound of a flanger
Characteristic sound results when these notches sweep up and down frequency axis over time
Sweeping action of notches achieved by continuously changing amount of delay used
As delay increases, notches go ...
  Lower in the spectrum
Delay change set by low frequency oscillator (LFO)
  For example, sine wave at < 5 Hz
Flanging.mov

## Slide 16: Pitch modulation
Changing M(n) over time
  What does this mean in practice?
  Read faster or slower from delayed signal
  dM/dt (or M[n] - M[n-1]) indicates difference in playback speed of delayed signal
Classic analogue tape example
  Pitch changes as tape speeds up or slows down
Only delayed copy has pitch change
  Mixed with original signal
  Perceived pitch warbles

## Slide 17: Depth control g
Determines how deep notches go
  How pronounced the effect is
When depth is 0
  frequency response is flat
  No flanging
Increase depth notches appear and extend downward
When depth=1
  notches extend down to 0
  Peaks maximally pronounced
Even if notches<<1, they have audible effect
  In multieffects units, g may only be controllable in mixer section, not flanging processor itself

## Slide 18: Delay parameter
Minimum delay used on copy of signal
  Determines how high the first notch will go
  Increasing delay drops the first notch downward
If minimum delay = 0 ...
  Notches sweep to uppermost frequency range, momentarily disappear
drum loop flanged with a delay of 1ms, and then 4 ms. Listen to notches sweep downward, then upward before returning to initial location.

## Slide 19: Sweep width
Range of delay times (min to max delay)
  Width (amplitude) of LFO
Sweep width is maximum additional delay
  In addition to delay parameter (determines minimum)
  Maximum delay = delay parameter + sweep width
Determines how low the first notch will go
Small width keeps variance in delay time small
Large width causes notches to sweep larger area
Sometimes called “sweep depth”
  Not to be confused with depth g!
Total
delay
Delay
parameter
Sweep
Width
(LFO amplitude)
Time
LFO Period
The maximum delay is the sum of the delay and sweep width parameters. The delay changes over time according to the sweep rate

## Slide 20: Sweep width
Increased width  increased pitch modulation
  Why?
  dM/dt will grow
    Flanger needs to read faster and slower to change delay in same amount of time
Using sweep parameters:
  Set delay to determine high frequency of sweep
    Delay changes both upper and lower points of first notch
  Adjust width to determine low frequency of sweep
    Width only changes lower limit
plucked electric guitar string, first flanged with depth of 2 ms, then with 6 ms
Latter varies more in pitch

## Slide 21: LFO settings
Delay M(n) modulated by low frequency oscillator (LFO)
  For sinusoidal case: M[n]=M0(1+Asin(2pfnT))
    f - speed (or rate) of flanger in cycles per second
    A - excursion or sweep (maximum delay swing)
    M0 - average delay length (controls notch density)
      Either A or M0 often not user-controllable
    T - sampling period
  Triangular LFO common in most flangers
Speed control
  How many times per second notches oscillate
  Also affects amount of pitch modulation (why?)
    Derivative of sin term above:
    Delay has to travel the same distance in less time

## Slide 22: Feedback / regeneration
Take portion of flanger output, feed back to input
  Regeneration control sets level of feedback
  Feedback comb filter in addition to previous feedforward comb filter
  Add or subtract feedback
  Feedback usually in small amounts
    Large feedback creates intense or “metallic” sound
    Too large and it becomes unstable
+
Delay M(n)
x[n]
y[n]
gFF
gFB
+
LFO
Sound example: flanging with heavy feedback on strummed chord

## Slide 23: Impulse responses for comb filter with 5 samples delay
gain g= 0.8 and no feedback
gFF= 0.8 and gFB= 0.5

## Slide 24: Feedback / regeneration
As feedback goes to 1, can become unstable
  Just as in other feedback delay cases
  Result: overflow or clipping
Control options
  Add or subtract feedback signal
  Feedback from any subset of allpass sections
    Usually in small amounts
Combined feedback/feedforward comb filter

## Slide 25: Flanger inverted mode
Different type of maximum depth obtained for g = -1
  Peaks and notches trade places relative to g = 1
  First notch at DC (f = 0)
  Results in weak bass response
    Unless minimum delay M >> 0
Depth control g usually constrained to [0, 1] interval
  Sign inversion controlled with separate switch
  Sounds high-pass filtered relative to g > 0
As M shrinks (and notch spacing grows):
  Amplitude response approaches first-order difference
  y[n]=x[n]-x[n-1]
  Approximates (continuous) differentiator
  Behaviour of ideal differentiator:
    Eliminates DC
    Progressive high-frequency boost (6dB/octave)
    Amplitude response is |H(w)|=|w|

## Slide 26: Digital implementation
Use delay lines (generally circular buffers)
  Contiguous block of memory to store samples
  Continuously read and write this space
Changing delay creates challenges
  Samples are one sampling period apart
  Delay line has to be an integer value
Solution: interpolation (fractional delay)
  Estimate value between 2 samples
  Zeroeth order: choose closest point to read from
    Zipper noise: clicking in output as delay length changes
  Linear interpolation: read value from line between points
    Okay but still noisy
  Quadratic interpolation
    Better, but more computation

## Slide 27: Notch spacing issues
Only uniformly spaced notches
non-ideal because:
  Ear uses logarithmic frequency scale
    Flanger notches spaced linearly
    Exponentially spaced notches sound more perceptually uniform
  Uniform peaks/notches impose discernible resonant pitch
    Impression of being inside resonant tube

## Slide 28: Disappearing instruments
If instrument harmonics land on notches
  instrument may be eliminated from output
Exact alignment unlikely, but...
  Loudness can be modulated as notches move through spectrum
  Flanging best used with percussive, noisy or inharmonic sounds
    Works well with drums
  For harmonic sounds, need non-uniform notches
Flanging often used on entire mix, rather than specific instrument within mix

## Slide 29: Stereo flangers
2 monophonic flangers in quadrature phase
  Same depth, width, delay, etc.
  LFO in each monophonic flanger differs in phase by 90 degrees (1/4 wavelength)
Creates ‘wider’ sound
  Sound arriving at each ear is different
Sound examples
  Dry, then monophonic flanger
  Then stereo flanger