## Slide 1
Chorus

## Slide 2: The chorus effect
Chorus = a group of singers
Two people playing instruments in unison:
  Won’t be precisely synchronised
    Some delay between sounds they produce
  Instrument pitches deviate, despite careful tuning
Chorus effect
  Make one instrument sound like many played together
  Add thickness to sound
  Described as ‘lush’ or ‘rich’
  Reproduce irregularities using delay line
    Slight delay
    Variable delay, like flanger and vibrato
      Detuning
Dry chord progression, then chorused version
Notes: Just as a chorus is a group of singers, the chorus effect can make a single instrument sound like there are actually several instruments being played. It adds some thickness to the sound, and is often described as 'lush' or 'rich'. This is an example of the chorus effect in action.
The algorithm behind the chorus effect isn't a spectacular or amazing trick - it's actually fairly simple. What happens when two people play instruments in unison? Well they are not always playing in precise synchronization, so there is some delay between the sounds they produce. In addition, the pitch of the two instruments can deviate somewhat, despite careful tuning. These are the functions that your chorus effect is reproducing.
This slight delay can be easily implemented with a delay line. Creating the detuning effect may not seem very simple at first, but it can be achieved by transforming the simple delay line into a variable length delay line. The 'variable length' part just means that the delay time changes over time, though it's effect on the pitch may not be very clear at first.

## Slide 3: Chorus and flanger
Mix original signal with delayed and pitch modulated copy
Similar to flanger, except
  Delay times in chorus are larger than in flanger
    Chorus delay between 20-30ms
    Flanger delay usually 1-10ms
    Long delay doesn't produce sweeping sound of flanger
  For chorus, generally no feedback used
+
Delay M(n)
x[n]
y[n]
g
LFO

## Slide 4: Chorus and LFO
Delay time changes with low frequency oscillator
  Periodic waveform (e.g. sine, triangle)
  Waveform changes slowly (3 Hz and below)
  LFO controls:
    Frequency
    Amplitude
    Shape (waveform)
Can randomly change delay instead of LFO
  Arguably, better models musicians playing in unison
Multiple players in unison show loudness differences
  Can vary amplitude of delayed signal
  Amplitude parameter could be controlled by another LFO
+
Delay M(n)
x[n]
y[n]
g
LFO

## Slide 5: Common parameters
Delay
  Controls minimum delay time that is used
  For very small delay, chorus acts as flanger
  Typical delay times between 20 and 30ms.
Sweep width (or depth)
  Amplitude of LFO, in milliseconds
  Controls how much total delay time changes over time
  Have to read faster/slower to cover total change in time
  Increased sweep widths increase pitch modulation
  Large sweep depths create a ‘warble’
LFO settings
  Waveform describes how delay changes over time
  Max of waveform = max delay time
  Increasing LFO value = lower pitch (reading slower)
  Pitch modulation related to speed of LFO (as before)
    Steepest portions on waveform produce large pitch modulation
    Increase speed compress waveform steeper pitch altered more
Total delay
= sweep width
+ delay
Delay
parameter
Sweep
Width
(LFO amplitude)
Time
LFO Period
Sustained note- processed with chorus with 3 ms sweep width, then with6 ms sweep width
Notes: The sweep depth also increases the pitch modulation introduced by the time-varying delay line. This happens because you have to read even faster and slower to cover the total change in time. Large sweep depths will create a 'warble.' The sound example demonstrates this effect.
The LFO waveform shows how the delay changes over time. When the waveform reaches a maximum, then the delay is at its largest value. When the waveform (and total delay time) is increasing, the pitch becomes lower. The amount of pitch modulation introduced by the chorus is related to how quickly the LFO waveform changes - the steepest portions on the waveform produce a large amount of pitch modulation, while the relatively flat portions have very little or no effect on the pitch. We can use this view to understand how the sweep depth varies the pitch. If you increase the sweep depth, you are effectively stretching the waveform vertically, which makes it steeper, and thus, the pitch is altered more.

## Slide 6: LFO waveform
Sine
  Smooth
  Continuously changing, both pitch and delay
Triangle
  Only 2 pitches because only 2 slopes (positive and negative)
  Sudden change between pitches
Log (exponential)
  Smooth over cycle, but jump at end of each cycle
  Slope at beginning and end of waveform differ
    Causes abrupt change in pitch
  Large sweep width stresses LFO effect
Sustained note processed with chorus using sine, triangle, and logarithm curve

## Slide 7: More parameters
Number of voices
  Multiple copies of sound
    Model more than 2 instruments being played
  Multi-voice chorus uses single LFO waveform for all voices
  Each voice has different phase
    At any point in time, each voice is at different point in waveform
    Different delay times
    If all in phase, same effect as single voice chorus with increased level
+
x[n]
y[n]
Delay M1(n)
g1
LFO
Delay M2(n)
g2
LFO

## Slide 8: Stereo chorus
Run 2 monophonic choruses in quadrature phase
  Same delay, width, etc.
  Each LFO differs in phase by 90° (1/4 wavelength)
Sound arriving at each ear is different
  Creates wider sound
  Same principle as stereo flanger
For multi-voice chorus
  Create stereo chorus simply by panning voices away from centre of mix
Mono source file processed first by a monophonic chorus, and then a stereo chorus
Notes: A stereo chorus is generally constructed by running two monophonic chorus run in quadrature phase. This simply means that the LFO in each monophonic flanger differ in phase by ninety degrees (or one-quarter of a wavelength). This technique creates a 'wider' sound because the sound arriving at each of your ears is different. Sound Set 4 presents a mono source file processed first by a monophonic chorus, and then a stereo chorus. (If you are having trouble hearing any difference, make sure your computer is generating a stereo output, and use a pair of headphones.)
Note that in a multi-voice chorus (where each voice is monophonic), you can effectively create a stereo chorus simply by panning the voices away from the center of the mix.

## Slide 9: Aside: building real-time effects
Delay, Vibrato, Flanger, Chorus all use buffers to hold delayed audio samples
  How long does buffer need to be?
    As long as maximum delay (for any point in the LFO cycle)
  But how does audio get into the buffer?
Real-time audio systems break stream into discrete buffers
  Can usually set buffer size for audio device
    How much data at a time comes from the device?
  But this is different than the size of the delay buffer!
Audio Samples
Audio device buffer size

## Slide 10: Aside: building real-time effects
Audio hardware, not your program, controls when sound processed
  You create callback function to process audio
    System “calls you back” whenever there’s work to be done
  System tells you buffer size
    i.e. how many audio samples are there to process right now?
  Your job now is to process only those samples that just came in. Run your effect and return when finished.
    But you might need to remember what happened previously!
...
audio device buffer size
callback function

## Slide 11: Aside: building real-time effects
What if we need delay longer than audio buffer size?
  Never have enough samples in audio buffer
What if delay is shorter than the audio buffer size?
  Might need sample from last time callback function was run
Allocate separate delay buffer
  Delay buffer holds past M samples, regardless of how audio device chooses to deliver them
Audio Samples
Audio device buffer size
+