## Slide 1
Delay-Based Effects

## Slide 2: Basic delay
From a digital system perspective, delay is simple:
  Difference equation adding the current input sample to one D samples prior
  y[n]=x[n]+ax[n-D] | a|<1 (usually)
For audio:
  Delay ranges from milliseconds to several seconds
  What values of D does this imply for sampling rate= 44.1kHz?
    1 second =
    1 ms =
    = 1 sample
    44100 samples
    ~ 44 samples
    22.6µS
+
Delay (D)
x[n]
y[n]
g

## Slide 3: Basic delay: aesthetics
Takes audio and plays it back after delay time
  One of the simplest audio effects
Use delay to:
  Bring to life dull mixes
  Widen an instrument’s sound
  Solo over yourself
Delay is building block for other effects
  Echo
  Reverb
  Chorus
  Flanging
  ...

## Slide 4: Delay with feedback
Most delays have feedback control (regeneration)
  takes delay output, sends it back to input
  repeat sound over and over
Quieter each time it plays back
  assuming feedback gain is less than one
    Most delay devices restrict gain to less than one for stability
  after some point, drops below noise floor  inaudible
Basic delay unit with feedback
+
Delay N
x[n]
y[n]
gFF
gFB
+

## Slide 5: Delay with feedback
To derive y[n] in terms of x[n]:
d[n]=gFF{x[n-N]+gFBd[n-N]} , y[n]=x[n]+d[n]

d[n-N]=y[n-N]-x[n-N]
d[n]=gFF{x[n-N]+gFBd[n-N]}
y[n]=x[n]+gFF{x[n-N]+gFBd[n-N]}
=x[n]+gFF{x[n-N]+gFB(y[n-N]-x[n-N])}
=x[n]+gFF(1-gFB)x[n-N]+gFFgFBy[n-N]
+
Delay N
x[n]
y[n]
gFF
gFB
+
d[n]

## Slide 6: Delay with feedback C++ code
int numSamples; // how many audio samples to process
float *channelData;// Array of audio samples, length numSamples
float *delayData; // Our circular delay buffer of audio samples
int delayBufLength;// Length of delay buffer in samples
int dpr, dpw; // Read and write pointers into the delay buffer
// User-adjustable effect parameters:
float dryMix_; // Level of dry (undelayed) signal
float wetMix_; // Level of wet (delayed) signal
float feedback_; // Feedback level for the delay (0 if no feedback used)
for (int i=0;i<numSamples;++i)
{
    const float in = channelData[i];
    // Output is input + weighted content of delay buffer
    float out = dryMix_*in + wetMix_*delayData[dpr];
    //Store current info in delay buffer. delayData[dpr] is delay sample we
    //read (out of buffer). Write delayData[dpw] to buffer (goes in)
    delayData[dpw] = in + (delayData[dpr] * feedback_);
    if (++dpr >= delayBufLength) dpr = 0;
    if (++dpw >= delayBufLength) dpw = 0;
    channelData[i] = out; // Store output sample in buffer, replacing input
}

## Slide 7: Sound samples
Delays applied to a pulse-like sound
  Original pulse
  Processed with 60 ms delay (no feedback)
  100 ms delay
  150 ms delay
  250 ms delay
  250 ms delay with feedback
  250 ms delay with higher feedback gain

## Slide 8: Delay on an instrument
Playing through delay unit with short echo, say 50 to 100 milliseconds, creates doubling effect
  Useful for filling out an instrument's sound
  Like two instruments being played in unison
  Several delays together with feedback can create reverb-like sound
simple guitar riff, followed by the same riff, but with added delay 40 ms., doubling the sound

## Slide 9: Long delays
Delay times above 100ms no longer a subtle effect
  Can match delay time to tempo of song
    Delayed copies of sound fall on a beat
Extending to very long delays: 1 second or more
  Can play over yourself
  develop harmonies even though you may only play one note at a time
See A Study of The Edge’s (U2) Guitar Delay by Tim Darling
  http://www.amnesta.net/edge_delay/
can use long delay to layer notes
delay time used here is 1.5 seconds

## Slide 10: Looping and sampling
Record only a segment of playing and loop it
  e.g. a chord progression
  Play recorded audio over and over
  Solo over yourself, without rhythm player
Some delay pedals include sampling capability
  Length of sample often limited to 2 seconds or less
For serious looping, need longer recording time
  Memory depends on duration, sample rate, bit depth
Popular units offer additional capabilities
  Recording additional sounds onto sample
  Playing loop backwards
  Recording several different loops

## Slide 11: Delay and mixing
Important when mixing for stereo
  Enhance stereo placement of instruments
  Make mix sound “bigger”
Small delay can be more effective than panning for spreading tracks out in stereo field
  Simple delay ca. 20ms can make big difference
We discuss this when covering spatial effects
riff initially mixed to center of stereo mix.
followed by same riff with 20 ms delay between 2 channels.
NO panning involved - just pure delay with no feedback.

## Slide 12: Slapback and echo
Slapback delay is not new algorithm
  same as basic delay without feedback
Delay is called slapback delay if delay time fairly short
  between 40 and 120 milliseconds.
Longer delay called echo

## Slide 13: Typical effect delay times
(We’ll see these
other effects soon!)

## Slide 14: Multi-tap delay
Simple delay: outputs taken after total delay time
Multi-tap delay is more flexible
  Take outputs after only portion of delay time
  Known as tapping the delay line
    Like tap in water pipe allows you to get water at various points
Units labeled with number of available taps
  3-tap delay has 3 taps to use, a 4-tap has 4, etc.
  Unwanted taps removed by setting output level to 0
  Amount of delay between taps can be different
4-tap delay in action
z-N1
x[n]
y[n]
+
z-N2
z-N3
z-N4
+
+
+

## Slide 15: Multi-tap delay
General case of basic delay design
  Set all but one tap gain to 0, place remaining tap at delay line end  results in basic delay line
Multi-tap delay can be generalised further
  Allow feedback from each delay output to beginning
  Easy to create unstable system!
Looking only at single tap
  Sound repeats according to total delay time
  Input sound will appear at tap output before total delay time (except last, rightmost tap)
sound produced with 4-tap delay
same sound with fourth tap moved 80 ms. closer to input
sound with increased total delay time increased by 200 ms. (i.e., Delay 5 in the diagram increased by 200 ms.).

## Slide 16: Ping-pong delay
For stereo audio systems
Creates bouncing effect
  Sound typically jumps between left and right channels
2 delay lines with 2 inputs, 2 outputs
  Can use same signal for each input
  Typically pan outputs hard left and hard right
Feedback from each delay line goes to opposite line
ping-pong delay
1st sequence generated with symmetric setup (delays same length, same feedback gain) panned hard left and right
2nd sequence breaks symmetry and panning
x1[n]
y1[n]
z-N
z-N
y2[n]
x2[n]

## Slide 17: Lets work out the transfer functions
x1[n]
y1[n]
z-N
z-N
y2[n]
x2[n]

## Slide 18
W1 (z)=[b1W2 (z)+a1X1 (z)] z-N
W2 (z)=[b2W1 (z)+a2X2 (z)] z-N
Solve these equations for W1
b1 b2W1z-2N + b1 a2X2 z-2N+a1X1z-N =W1
W1=[a2 b1 X2 z-2N+a1X1 z-N]/[1-b1 b2 z-2N ]
Now plug into
Y1 (z) = c1W1 (z)+X1 (z)
...and similar for the other channel
X1(z)
Y1(z)
z-N
z-N
Y2(z)
X2(z)
W1(z)
W2(z)
a1
a2
c1
c2
b2
b1

## Slide 19: Delay in the recording process
Suppose we record an instrument with a close microphone and a distant microphone
  Sound travels at 340.3m/s
  If mics are 2m apart, sound arrives 5.9ms later to the distant mic
Adding closely timed but not identical signals creates phase problems
  Selective cancellation of certain frequencies
  This can be used deliberately as a musical effect (more on this soon)
Solution: delay the close mic to compensate
2m = 5.9ms
Delay
5.9ms

## Slide 20: Digital delay implementation
Operation
  Read an input recorded previously
  Store current input in another memory location
    Or may be same location that was just read
    This is why value read before writing
  Next sampling period
    Read & write next location in memory
    When end of memory, loop around to first memory location
    This is a circular buffer, and it is quite efficient
Programming delays
  Read and write pointers keep track of where to read/write in memory
  Pointers increment each sample
  Multi-tap delays created using additional read pointers

## Slide 21: Delay on a circular buffer
Buffer is a contiguous block of memory
  Read and write pointers point to specific locations within this block
  Difference in read/write pointer location determines delay
  This is equivalent to difference equation representations
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
x[13]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
write pointer
read pointer

## Slide 22: Fractional delay
What happens when we want non-integer D?
  x[n] undefined if n is not an integer
Consider this discrete/continuous system:
D / C
Delay
C / D
48kHz
48kHz
dT = 10.4µs
(0.5 samples)
+
Delay (D)
x[n]
y[n]
g

## Slide 23: Fractional delay
Ideal discrete-to-continuous converter
  “sinc reconstruction”
Delay of D samples corresponds to a convolution:
  Not causal
  Infinitely long convolution
https://ccrma.stanford.edu/~jos/st/Introduction_Sampling.html
where
Full derivation: Oppenheim, Schafer and Buck, Discrete-Time Signal Processing, 2nd ed., Sec 4.5

## Slide 24: Fractional delay in practice
Use interpolation between samples
  Linear (fast), second order or cubic (better quality)
Pseudocode (next slide...)
  Input:
    An input signal x[n] at sampling rate R
    Required delay line size D
    Starting delay for read pointer initialdelay
    Read pointer update rate updateread (write pointer update rate=1)
  Output:
    N samples of signal y[n] at sampling rate R (output of read pointer)

## Slide 25: Fractional delay in practice
Allocate buffer delayline of size D for storing samples
writepos=0; // write pointer position, start at beginning of buffer
readpos=(writepos+D-initdelay)%D;// read pointer position, modulo keeps indexing correct
for (n=0; n<=N-1; n++)
{
prev=floor(readpos); // get previous integer index
next=(prev+1)%D; // get next integer index; because of wraparound, need modulo for safety
t=readpos – prev; // get fractional position of read pointer
y[n]=(1-t)*delayline[prev]+t*delayline[next]; // Linear interpolation
readpos=(readpos+updateread)%D; // update read pointer for next time, modulo wraps
delayline[writepos]=x[n]; // write current sample to delay line
writepos=(writepos+1)%D; // update write pointer for next time, modulo wraps
}
Code doesn’t check whether pointers cross
  won’t happen when moving at same speed
  pointers moving at different speeds here
Read always happens before write to delays of full buffer length
  Should work properly