## Slide 1: Aside: building real-time effects
Delay, Vibrato, Flanger, Chorus all use buffers to hold delayed audio samples
  How long does buffer need to be?
    As long as maximum delay (for any point in the LFO cycle)
  But how does audio get into the buffer?
Real-time audio systems break stream into discrete buffers
  Can usually set buffer size for audio device
    How much data at a time comes from the device?
  But this is different than the size of the delay buffer!
Audio Samples
Audio device buffer size

## Slide 2: Aside: building real-time effects
Audio hardware, not your program, controls when sound processed
  You create callback function to process audio
    System “calls you back” whenever there’s work to be done
  System tells you buffer size
    i.e. how many audio samples are there to process right now?
  Your job now is to process only those samples that just came in. Run your effect and return when finished.
    But you might need to remember what happened previously!
...
audio device buffer size
callback function

## Slide 3: Aside: building real-time effects
What if we need delay longer than audio buffer size?
  Never have enough samples in audio buffer
What if delay is shorter than the audio buffer size?
  Might need sample from last time callback function was run
Allocate separate delay buffer
  Delay buffer holds past M samples, regardless of how audio device chooses to deliver them
Audio Samples
Audio device buffer size
+