## Slide 1
Fractional delay

## Slide 2: Fractional delay
What happens when we want non-integer D?
  x[n] undefined if n is not an integer
Need to do interpolation
  Estimate the value at some location based on values at other locations
+
Delay (D)
x[n]
y[n]
a

## Slide 3: Zeroth order interpolation
Just pick the nearest known value
  x[m]= x[⌊m+0.5⌋]
  Example: x[2.3] = x[⌊2.3+0.5⌋] = x[⌊2.8⌋] = x[2]
0
1
x0
x1

## Slide 4: First order interpolation
Weighted sum of two nearest points
Find given known samples and
We fit the points to a line,

0
1
x0
x1

## Slide 5: Quadratic interpolation
2nd order polynomial from three nearby points
Find given known samples and
We fit the points to a line,

-1
0
x0
x1
2
Notes: Check:
Suppose x_t = 2t^2 –t +1
X0=1
X1=2
X2=7
X_0.5 = 2t^2 + -1 t +1

## Slide 6: Fractional delay in practice
Use interpolation between samples
  Linear (fast), second order or cubic (better quality)
Pseudocode (next slide...)
  Input:
    An input signal x[n] at sampling rate R
    Required delay line size D
    Starting delay for read pointer initialdelay
    Read pointer update rate updateread (write pointer update rate=1)
  Output:
    N samples of signal y[n] at sampling rate R (output of read pointer)

## Slide 7: Fractional delay in practice
Allocate buffer delayline of size D for storing samples
writePosition=0; // write pointer position, start at beginning of buffer
readPosition =(writePosition +D-initdelay)%D;// read pointer position, modulo keeps indexing correct
for (n=0; n<=N-1; n++) {
prev=floor(readPosition); // get previous integer index
next=(prev+1)%D; // get next integer index; because of wraparound, need modulo for safety
t= readPosition – prev; // get fractional position of read pointer
y[n]=(1-t)*delayline[prev]+t*delayline[next]; // Linear interpolation
delayline[writePosition]=x[n]; // write current sample to delay line
readpos=(readPosition+updateread)%D; // update read pointer for next time, modulo wraps
writepos=(writePosition +1)%D; // update write pointer for next time, modulo wraps
}
Code does not check whether pointers cross
  won’t happen when moving at same speed
  pointers moving at different speeds here

## Slide 8: Interpolate sample
float PluginAudioProcessor::interpolateSample(int type,
float delayReadPosition, float* delayData, int delayBufferLength) {
switch (type) {
case 0: { //NearestNeighbour:
int closestSampleIndex = (int)floorf(delayReadPosition + 0.5f);
if (closestSampleIndex == delayBufferLength) closestSampleIndex = 0;
return delayData[closestSampleIndex];
}
…
}
}
Round to nearest integer. If it rounds to end of buffer, roll back to beginning
Notes: must pass MidiKeyboardState object to initialise MidiKeyboardComponent object

## Slide 9: Interpolate sample
float PluginAudioProcessor::interpolateSample(int type,
float delayReadPosition, float* delayData, int delayBufferLength) {
switch (type) {
…
case 1: { // linear
float fraction = delayReadPosition - floorf(delayReadPosition);
int sample0 = (int)floorf(delayReadPosition);
int sample1 = (sample0 + 1) % delayBufferLength;
return fraction * delayData[sample1]
+ (1.0f - fraction) * delayData[sample0];
}
…
}
}
adjust sample weights with fraction by which read pointer between 2 samples
Notes: must pass MidiKeyboardState object to initialise MidiKeyboardComponent object

## Slide 10: Interpolate sample
float PluginAudioProcessor::interpolateSample(int type,
float delayReadPosition, float* delayData, int delayBufferLength) {
switch (type) {
…
case 2: { //quadratic
int sample1 = (int)floorf(delayReadPosition + 0.5) % delayBufferLength;
int sample2 = (sample1 + 1) % delayBufferLength;
int sample0 = (sample1 - 1) % delayBufferLength;
float fraction = delayReadPosition - sample1;
return (fraction * (fraction - 1) * delayData[sample0]
- 2 * (fraction - 1) * (fraction + 1) * delayData[sample1]
+ fraction * (fraction + 1) * delayData[sample2]) / 2.0f;
}
}
}
adjust sample weights with fraction by which read pointer between 3 samples