## Slide 1
Filters and equalisers in JUCE

## Slide 2: Equalisation
Definition
  Boosting or cutting certain frequency components in a signal
Equalisation (EQ) is a form of filtering
  Filters change magnitudes & phases of signal’s frequency content
  Usually linear and time-invariant
Origin
  Trying to obtain flat frequency response
  No colouration
Example
  Transmitting analogue voice signal over long distance
  Transmission line attenuates high frequencies
  Apply EQ to correct loss, resulting in more natural sound on other end
Notes: Equalisation (EQ) is the process of boosting or cutting certain frequency components in a signal. The name originates from the application of trying to obtain a flat frequency response - no coloration. For example, when transmitting (analog) voice signals over long distances of wire, the high frequencies would be attenuated. By applying some equalisation filters, this loss could be 'undone' so that the voice would sound more natural on the receiving end. Equalisation is a very important tool in recording for bringing out an instrument's sound.

## Slide 3: Digital filter can be described many different ways
Difference equation (time domain):
y[n] = a y[n -1] + x[n]
Transfer function (frequency domain):
  Use normalised radial sampling frequency w=2pf/fs
  z= ejw
H(z)=Y(z) /X(z)=(1-az-1)-1
Block diagram
Algorithm (software)
+
a
z-1
y[n]
x[n]
      loop()
      {
      read x
      y = a * y + x
      write y
      }
General difference equation
Transfer function
If bi=0, for all i,
  No feedback
  finite impulse response (FIR) filter
If bi0, for any i,
  Feedback
  infinite impulse response (IIR) filter

## Slide 4: FIR & IIR filters
Weighted sum of last M inputs
Finite impulse response:
  If , for n > M
Always stable
z-1
z-1
z-1
z-1
z-1
z-1
x[n]
...
+
y[n]
b0
b1
b2
b3
b4
b5
b6
Weighted sum of last M inputs & N outputs
Infinite Impulse Response
Stability depends on coefficients ak
Most equalisers use IIR filters

## Slide 5: What do we want in a filter?
Generally two conflicting priorities:
Sharpness of cutoff
  Between passband and stopband
Computational complexity
  Measured in multiplies per sample
Order
N = 1
N = 2
N = 3
N = 6
Butterworth
(IIR) filters
Rolloff:
6N dB/octave
log(f)
log(H)

## Slide 6: What do we want in a filter? (part 2)
For equalisers, sharpest cutoff not necessary
  Small, controlled adjustments to frequency response
Advantages of IIR
  More computationally efficient (lower orders)
  Models analogue filters
Advantages of FIR
  Always stable
  Linear phase (when coefficients are symmetrical)
symmetrical impulse response means...
magnitude change with delay means...
phase is a linear function of frequency

## Slide 7: High order filtering
For equalisation
  Change some frequencies, but leave others unchanged
  Combine multiple 1st and 2nd order filters
Series
  Transfer function as product of 2nd order terms
  Low shelf, high shelf and peaking filters
Parallel
  Transfer function as sum of 2nd order terms
  Low pass, high pass and bandpass filters
H1(z)
X(z)
Y(z)
H2(z)
H3(z)
H1(z)
X(z)
Y(z)
H2(z)
H3(z)
+

## Slide 8: Ideal filters
|H|2
0
p
1
wc
0
p
wc
|H|2
1
Lowpass
Highpass
|H|2
0
p
1
wc
G
0
p
wc
|H|2
1
G
Low Shelving Filter
High Shelving Filter
Compare shelving to lowpass & highpass filters
Most filters remove low or high frequencies
Here, just want to boost or cut portion
Cutoff frequency
  Where response changes between 2 levels

## Slide 9: Ideal filters
|H|2
0
p
wc
1
G
0
p
wc
|H|2
1
G
Peaking Filter (boost)
Peaking Filter (cut)
|H|2
0
p
wc
1
0
p
wc
|H|2
1
B
B
Bandpass
Bandstop
Centre frequency
  Where response reaches maximum or minimum
B
B

## Slide 10: Magnitude response of shelving filters
Boost
Cut
Boost
Cut
low shelving filter (top)
high shelving filter (bottom)
varying gain (left) varying center frequency (right)

## Slide 11: Magnitude responses for peaking filter
Boost
Cut
vary gain
vary center frequency
vary bandwidth
Warping changes where bandwidth occurs
wc=π/2 (half Nyquist rate)  bandwidth symmetrical about centre frequency
wc  0: bandwidth to right of wc  low shelf
wc  π: bandwidth to left of wc  high shelf
Notes: The filter's bandwidth BW is only perfectly centered around the center frequency F0 when such frequency is set to 0.5*pi (half the Nyquist rate). When F0 is closer to 0 or to pi, there is a warping effect that makes a larger portion of the bandwidth to occur at one side of the center frequency. In the edge cases, if the center frequency is set to 0 (pi), the entire bandwidth of the filter occurs to the right (left) of the center frequency. The result is a so-called shelving lowpass (highpass) filter.

## Slide 12: Q factor
log-frequency scale
Quality factor: ratio of centre frequency and bandwidth
  Q=Centre frequency / bandwidth = wc/B
Q = 0.5
Q = 0.71
Q = 1
Q = 1.5
Q = 3
Q = 10
Second order
lowpass resonator filters
Constant Q peak filters
  Tune centre frequency while keeping Q constant
  Bandwidth scales with frequency
Notes: One often used filter is the constant Q peak filter.
Q factor is defined as the bandwidth relative to cut-off frequency.
Q=ωc/B
The cut-off frequency of peak filters is then tuned while keeping Q constant. So the bandwidth is increased when cut-off frequency increased and vice versa.

## Slide 13: Effect of higher order
Sharper transition for 4th-order
Notes: Some Basic Designs
One of the design parameters is the filter bandwidth, BW. You not only specify what the desired bandwidth is, you also specify at what gain this bandwidth is specified, GBW. In this case, we set GBW to be at half the peak magnitude squared gain of the filter, that is, approximately 3.0103 dB below the 6 dB gain. To see this, we can plot the magnitude squared and verify that the point at which the filter's bandwidth is 0.2*pi as specified is half of the peak magnitude squared.

## Slide 14: Filter implementation
Consider this filter:
  What do we need to calculate values in real time?
  Suppose we had a function that took one new value of x[n] and returned one new value of y[n]
float a1, a2, b0, b1, b2; // Assume these are initialised
float calculate(float x) {
float y;
y =
return y;
}
b0*x + b1*xPrev + b2*xPrevPrev + a1*yPrev + a2*yPrevPrev;
[what goes here?]
yPrevPrev = yPrev; // Need to remember old values...
yPrev = y; // Could also use a circular buffer
xPrevPrev = xPrev;
xPrev = x;
float yPrev, yPrevPrev, xPrev, xPrevPrev; // Previous samples
b0*x + b1*xPrev + b2*xPrevPrev + a1*yPrev + a2*yPrevPrev;

## Slide 15
Low pass |  |  | - |  | 
High pass |  | 0 | - |  | 1
Low shelf |  |  | - |  | 
High shelf |  | 1 | - |  | 
Bandpass |  |  |  | 1 | 
Bandstop |  | 1 | 0 |  | 1
Peaking |  |  |  |  | 
Lowshelf2 |  |  | - |  | 
Highshelf2 |  |  | - |  | 
Peaking2 |  |  |  |  | 
Low pass |  |  | - |  | 
High pass |  | 0 | - |  | 1
Low shelf |  |  | - |  | 
High shelf |  | 1 | - |  | 
Bandpass |  |  |  | 1 | 
Bandstop |  | 1 | 0 |  | 1
Peaking |  |  |  |  | 
Lowshelf2 |  |  | - |  | 
Highshelf2 |  |  | - |  | 
Peaking2 |  |  |  |  | 
Notes: Two different formulations. The first is derived in my audio effects book, the second in the All About paper.
sqrt(G) for gain at wc in shelving filters
First uses arithmetic meanSecond, square mag at fc is average of the other square mags, so (1+G^2)/2
Second uses geometric mean, square mag at fc is geo mean of the others, so sqrt(1*G^2)=G
Lowpass and highpass stay as is, probably same for bandpass and bandstop

## Slide 16: Useful resources
https://github.com/TheAudioProgrammer/juceIIRFilter
https://github.com/landonviator/viator-graphic-eq/blob/main/viator-graphic-eq
https://docs.juce.com/master/tutorial_dsp_introduction.html

## Slide 17: juce::dsp::iir
Classes for IIR filter processing
struct ArrayCoefficients
  Set of coefficients for use in an Filter object
struct Coefficients
  Set of coefficients for use in an Filter object
class Filter
  Processing class that can perform IIR filtering on an audio signal

## Slide 18: Useful resources
auto newCoefficients = juce::dsp::IIR::Coefficients<float>::makeNotch(sampleRate, 1000.0, 1.0);
juce::dsp::ProcessorChain<juce::dsp::Gain<double>, juce::dsp::Gain<double> > chain1;
chain1.get<0>().setGainLinear(5.0);
chain1.get<1>().setGainLinear(5.0);
juce::dsp::ProcessorChain<juce::dsp::IIR::Filter<float>, juce::dsp::IIR::Filter<float>> chain;
chain.get<0>().coefficients = juce::dsp::IIR::Coefficients<float>::makePeakFilter(sampleRate, 1000.0f, 1.0f, 2.0f);
// auto filter = new juce::IIRFilter(juce::IIRCoefficients::makeHighPass(sampleRate, 1000, 1.0)); // in prepareToPlay
// filter->processSamples(buffer.getWritePointer(i), buffer.getNumSamples()); // in processBlock

## Slide 19: Three ways to implement filters
Directly
  keep recent inputs and recent outputs
    Do this for every channel
  Keep array of filter coefficients
  Apply filter operation each sample, each channel
Use Juce IIRFilter class
  implements generic 2 pole, 2 zero IIR filter
  setCoefficients saves 6 coefficients to calculate output samples
  processSamples performs filter operation on given samples
Use Juce IIRFilter and makePeakingFilter
  Different programming environments implement filters differently
 Lets use Juce classes

## Slide 20: Direct implementation
for (int i = 0; i < numSamples; ++i) {
float out = coefficients[0] * channelData[i]
+ coefficients[1] * x1 + coefficients[2] * x2
- coefficients[4] * y1 - coefficients[5] * y2;
out = out / coefficients[3];
x2 = x1;
x1 = in;
y2 = y1;
y1 = out;
channelData[i] = out;
}

## Slide 21: Define and initialise
Add private parameters to pluginProcessor.h
juce::AudioParameterFloat* gainParam;
juce::AudioParameterFloat* centreFrequencyParam;
juce::AudioParameterFloat* qParam;
juce::OwnedArray<juce::IIRFilter> filters;
Add audio parameters in constructor in pluginProcessor.cpp
addParameter(centreFrequencyParam = new juce::AudioParameterFloat
("cornerFrequency","Corner frequency",10.0f,20000.0f,1000.0f));
addParameter(gainParam = new juce::AudioParameterFloat
("gain","Gain",-12.0f,12.0f,0.0f));
addParameter(qParam = new juce::AudioParameterFloat("Q","Q",0.1f,20.0f,2.0f));
Add filters to array in prepareToPlay
filters.clear();
for (int i = 0; i < getTotalNumInputChannels(); ++i) {
juce::IIRFilter* filter;
filters.add(filter = new juce::IIRFilter());
}
Notes: MidiKeyboardComponent needs a MidiKeyboardState and the orientation as arguments.

## Slide 22: processBlock 1 - Define variables
Set up the basics in the processBlock method on pluginProcessor.cpp
juce::ScopedNoDenormals noDenormals;
auto numOutputChannels = getTotalNumOutputChannels();
auto numInputChannels = getTotalNumInputChannels();
auto numSamples = buffer.getNumSamples();
float gain = gainParam->get();
float Q = qParam->get();
float centreFrequency = centreFrequencyParam->get();
float sampleRate = (float)juce::AudioProcessor::getSampleRate();
float normalisedFrequency = juce::MathConstants<float>::twoPi
* centreFrequency / sampleRate;
float linearGain = pow(10.0f, gain / 20.0f);
Notes: must pass MidiKeyboardState object to initialise MidiKeyboardComponent object

## Slide 23: processBlock 2, set coefficients
const float bandwidth = normalisedFrequency / Q;
const double two_cos_wc = -2.0*cos(normalisedFrequency);
const double tan_half_bw = tan(bandwidth / 2.0);
const double g_tan_half_bw = linearGain * tan_half_bw;
const double sqrt_g = sqrt(linearGain);
// takes arguments b0, b1, b2, a0, a1, a2. Normalises filter by a0 for time-domain implementations
auto coefficients = juce::IIRCoefficients(
sqrt_g + g_tan_half_bw, /* b0 */
sqrt_g * two_cos_wc, /* b1 */
sqrt_g - g_tan_half_bw, /* b2 */
sqrt_g + tan_half_bw, /* a0 */
sqrt_g * two_cos_wc, /* a1 */
sqrt_g - tan_half_bw /* a2 */
);
for (int i = 0; i < filters.size(); i++)
filters[i]->setCoefficients(coefficients);

## Slide 24: processBlock 3, apply filters
for (int channel = 0; channel < numInputChannels; ++channel) {
float* channelData = buffer.getWritePointer(channel);
filters[channel]->processSamples(channelData, numSamples);
}
Not optimal, not elegant
  Recalculates filters every block
    Should only recalculate when parameters change
  Only does peaking filters
  Doesn’t do chain of filters, yet
filters1[channel]->processSamples(channelData, numSamples);
filters2[channel]->processSamples(channelData, numSamples);