## Slide 1
Wah-wah

## Slide 2: Background
Originally developed by jazz trumpeters using mutes
Guitar effect since Jimi Hendrix popularised Vox Crybaby pedal in late 1960s
Wah-wah pedal
  Resonant (high-Q) filter
  Pedal controls variable centre frequency
  Knob controls dry/wet mix
  Original GCB95 Cry Baby Wah

## Slide 3: Block diagram
Variable Mixing
Bandpass or peaking filter with variable center frequency
x[n]
+
y[n]
1-Mix
Mix

## Slide 4: Wah-wah resembles human vocalisation
Spectral characteristics of phonemes [u],[a]
Vocal folds are harmonic source filtered by formants depending on shape of mouth
  [u] vowel: first formant ~350 Hz
  [a] vowel: first formant ~700 Hz
  [u] to [a] articulation produces modulated sound
  1st formant moves up in frequency
[a] ‘ah’ first formant in range 700-1200Hz
  Matches range of resonant peak in wah-wah circuit
  Pedal range covers frequencies where first 2 formants overlap
Missing second formant
  Only one resonant peak in wah-wah circuit
  Electro-Harmonix “Talking Pedal” uses two peaks

## Slide 5: Varieties of wah-wah effects
Resonant filter
  lowpass, bandpass or peaking filter
  Variable centre frequency
    can vary from near 0 to fs/2
    In practice, varies across midrange only
  Small bandwidth high Q
Standard wah-wah
  Centre frequency manually controlled by pedal
Auto-wah, centre frequency controlled by
  LFO, frequency usually 1-2 Hz OR,
  Envelope of input signal
Tremolo-wah
  also amplitude variations
magnitude 12 dB (Gc ~ 20) at wc=p/2
Magnitude Response of Resonant lowpass filter

## Slide 6: Auto-wah - LFO
One auto-wah effect uses low-frequency oscillator
  LFO controls filter’s centre frequency
  Similar parameters to other LFO effects:
    Sweep rate
    Sweep width
    Minimum frequency
Time
fc
fmin
W

## Slide 7: Auto-wah – envelope follower
Can also refer to envelope follower wah effect
  Centre frequency scales with signal envelope
    Envelope is local average signal level
  Envelope characterised by attack and decay times
    How fast does it respond to increasing and decreasing signal?
    Usually, attack time << decay time
Other parameters:
  Minimum frequency fmin
  Sensitivity S

## Slide 8: M-fold wah-wah
Replace unit delay in resonant bandpass filter by M tap delay
M bandpass filters spread over entire spectrum
Simultaneously change their center frequency
M-fold wah-wah with white noise input
Periodic enhancement of output spectrum