## Slide 1
Expansion / Noise Gating

## Slide 2: Expanders and noise gates are dynamics processors
Function is opposite of compression
  Increase perceived dynamic range of signal
  Attenuate low level signals
  Leave high level signals unchanged
Expander uses variable gain control
  Controlled by level detector
  Gain never greater than 1
  Gain = 1 for loud signals, < 1 for soft signals
    Opposite of compressor
    soft signals get softer
Noise gating is expansion taken to extreme
  Heavily attenuate or eliminate low-level input
  Used to eliminate signals containing only noise
(look familiar?)
X
Level
Detector
Gain
Control
y[n]
x[n]

## Slide 3: (a) Audio from snare drum microphone with spill from cymbals and kick drum (b) same recording with noise gate applied to remove low level bleed
(a)
(b)
Audio from snare drum microphone with spill from cymbals and kick drum
same recording with noise gate applied

## Slide 4: Expander reduces signal level only when it drops below threshold
No expansion
2:1 expansion
3:1 expansion
∞:1 expansion
(noise gate)
Input level (dB)
Output
level (dB)
Threshold
Threshold = input level at which
expander activates
(above this, gain = 1)
Knee = transition between
expanded and
unexpanded
regions
Ratio = amount that decreasing
input level affects output level

## Slide 5: Implementation notes
Level detector calculates signal level over period of time
  Not instantaneous sample value
  Use RMS or envelope calculations
  Example: sine wave is 0 at certain times, but doesn’t mean there’s no signal at these points
Amount of expansion expressed as ratio
  Change in input dB  change in output dB
  Not the same as gain
  xdB=20 log10(x)
  Example: 4:1 expansion ratio
    3dB input drop produces 12dB output drop

## Slide 6: Noise gating
Large ratio = noise gating
  10:1 or higher expansion ratio
  Line approaches vertical below threshold
  Signal may be completely removed
    An on/off switch for audio
Most important parameter?
  Threshold
  Where gate “opens” and “closes”
    High signal  gate open
    Low signal  gate closed

## Slide 7: Attack and release
(not quite) analogous to compressor
  Provides ballistics and smoothing
  Attack time: time required for expander to respond to increasing signal level (gain reaches 1)
  Release time: time required for expander to respond to decreasing signal level (gain drops toward 0)

## Slide 8: Effect of an expander
Attack
Time
Release
Time
Only middle portion of input is above expander's threshold value
Takes time for expander to increase gain when input rises above threshold
When input drops below threshold, expander slowly reduces gain

## Slide 9: Why use expansion / noise gating?
Increase dynamic range of low-quality recordings
  More extremes on cassettes/vinyl which have low dynamic range
  Potentially less of an issue in digital systems
    What sampling parameter affects dynamic range?
Noise reduction
  Reduce feedback, unwanted bleed between tracks
  Eliminate noise or hiss in absence of a signal
  Set the right threshold
    Don’t cut off any of the instrument sound
    Don’t let through any ambient noise
  Noise still there when instrument is playing. Why isn’t this a problem?

## Slide 10: Companding
Compression and expansion are complementary
  Reduce effects of noise when transmitting signal
  Not just for audio systems
Assume transmission channel has limited dynamic range
  Compress before you transmit
    Increase average signal level with respect to channel noise
  Expand after you receive
    Restore signal to its original range (artifacts)
    Noise is attenuated
Used in analogue audio recording
  e.g. Dolby A noise reduction

## Slide 11: Placement in the Effects Chain
Noise gate often near end of effects chain
  other effects can produce noise
  have noise gate after them so noise not heard & amplified when not playing.
If using delay and reverb effects, place them after noise gate
  sound trails off naturally rather than abrupt silence.