## Slide 1: Under the hood of a dynamic range compressor
Audio samples, source code, VST plug in:
www.elec.qmul.ac.uk/digitalmusic/audioengineering/compressors/index.html
Notes: So today I’m going to talk about design of a dynamic range compressor.
Dynamic range compression, despite being one of the most widely used audio effects, is still poorly understood, and there is little formal knowldege and analysis of compressor design techniques.
In this tutorial, we describe several different approaches to digital dynamic range compressor design. Digital implementations of several classic analog approaches are given, as well as designs from recent literature and new approaches that address possible issues. Several design techniques are analysed and compared, including RMS and peak-based approaches, feedforward and feedback designs, linear and log domain ballistics. We explain what makes the designs sound different, and provide distortion-based metrics to analyse their quality. Finally, we provide recommendations for high performance compressor design.
1

## Slide 2: Questions and Challenges
Given how a compressor is used, how can you build one?
How can you emulate an analog design?
What makes compressors sound different?
Why do attack and release times mean different things for different compressors?
How can you measure the performance of a compressor?
“No two compressors sound alike... each one is inaccurate in its own unique way” – Roey Izhaki, Mixing Audio: Concepts, Theory and Practice
Notes: The motivation for this talk comes from a talk I heard at an AES Convention by Alex Case, entitled ‘Compression FX—Use Your Power for Good, Not Evil’
"No two compressors sound alike... each one is inaccurate in its own unique way.” Some differ in topology, others introduce additional stages and some simply differ from the precise digital design since these deviations add character to the compressor. However we can describe the main parameters of a compressor unit and specify a set of standard stages and building blocks that are present in almost any compressor design.
In general, compressors are quite an unexplored field in academia. The authors know of no prior publication that collectively derives and discusses the most common compressor design options in depth. A better understanding of the different design choices would make compressor design considerably easier and less of a trial-and-error process. It would also shed light on how the different design choices affect the perceived sonic characteristics of the compressor. The goal of this paper is to provide such analysis, considering both technical and perceptual aspects.

## Slide 3: What we’re not going to talk about
How to use a dynamic range compressor
  Preferred parameter settings for different tasks
How not to use a dynamic range compressor (Loudness war)
  But will show how better design helps prevent misuse
Hearing aids
  Still applicable, but we’re concerned with compressors for music production, mastering and broadcast
Sidechaining and parallel compression
Multiband compression
Additional parameters
  Look-ahead, hold...
Notes: So this is a big subject, and I’m focusing on design. In order to be clear about what the focus is, let me tell you what I’m not going to talk about.
We’re not really discussing how to use a dynamic range compressor. Of course, by telling you how to design one, I’ll discuss its intended use, but we’re not really focusing on the preferred parameter settings for different tasks.

## Slide 4: Introducing the dynamic range compressor
map dynamic range of audio signal to smaller range
  Reduce signal level of higher peaks while leaving quieter parts untreated
  Then (optionally) boosting whole signal to make it as loud as, or louder than, original uncompressed signal
Unlike gain, delay, EQ, panning...
  Poorly defined
    Not always agreed what compression parameters do
  An adaptive audio effect
    Action of the compressor depends on the input signal
  Nonlinear
    Generally noninvertible
Notes: Analysis of compressors is difficult because they represent nonlinear time-dependent systems.
Dynamic Range Compression (DRC) is the process of mapping the dynamic range of an audio signal to a smaller range, i. e., reducing the signal level of the higher peaks while leaving the quieter parts untreated. DRC is used extensively in audio recording, production work, noise reduction, broadcasting and live performance applications.
Considering the classic audio effects (equalisation, delay, panning, etc.), the dynamic range compressor is perhaps the most complex one. Design choices involve the compressor topology, the static compression characteristic, placement and type of smoothing filters, sidechain filtering, etc. This explains why every compressor in common usage behaves and sounds slightly different and why certain compressor models have become audio engineers' favorites for certain types of signal. Analysis of compressors is difficult because they represent nonlinear time-dependent systems with memory. The gain reduction is applied smoothly and not instantaneously as would be the case with a simple static nonlinearity. Furthermore the large number of design choices makes it nearly impossible to draw a generic compressor block diagram that would be valid for the majority of real world compressors.
In general, compressors are quite an unexplored field in academia. The authors know of no prior publication that collectively derives and discusses the most common compressor design options in depth. A better understanding of the different design choices would make compressor design considerably easier and less of a trial-and-error process. It would also shed light on how the different design choices affect the perceived sonic characteristics of the compressor. The goal of this paper is to provide such analysis, considering both technical and perceptual aspects.

## Slide 5: Compressor Controls
Threshold- T
  level above which compression starts
Ratio- R
  determines the amount of compression applied.
Knee Width- W
  Controls transition in the ratio around the threshold
Make-up Gain- M
  Used to match the output signal’s overall loudness to the original
Attack Time- tA
  Time to decrease gain once signal overshoots threshold
Release Time- tR
  Time to bring gain back to normal once signal falls below threshold
Notes: Threshold defines the level above which compression starts. Any signal overshooting the threshold will be reduced in level.
Ratio controls the input/output ratio for signals overshooting the threshold level. It determines the amount of compression applied.
Attack and release times provide a degree of control over how quickly a compressor acts. They are also known as time constants, although the latter is usually referenced to dB, denoting the gain decrease in dB that the compressor will apply for the given attack time and the opposite for the release time. Instantaneous compressor response, as described in {Lachaise, 2008 #13342}, is not sought because it introduces distortion on the signal.
The attack time defines the The release time defines the
A Make-Up Gain control is usually provided at the compressor output. The compressor reduces the level (gain) of the signal, so that feeding back a make-up gain to the signal allows for matching the input and output loudness level.
The Knee Width option controls whether the bend in the response curve has a sharp angle or has a rounded edge. The Knee is the threshold-determined point where the input-output ratio changes from unity to a set ratio. A sharp transition is called a Hard Knee and provides a more noticeable compression. A softer transition where the ratio gradually grows from 1:1 to a set value in a transition region on both sides of the threshold is called a Soft Knee. It makes the compression effect less perceptible. Depending on the signal one can use hard or soft knee, with the latter being preferred when we want less obvious (transparent) compression.

## Slide 6: Main components
Side-chain
  Level detection
    Estimate the ‘signal level’
  Decibel conversion
  Gain computer
    Apply threshold, ratio, knee
  Timing (Ballistics, Smoothing)
    Apply attack and release
  Gain stage
    Output is input multiplied by control vector produced by side-chain

## Slide 7: Level Detection – the options
Peak vs RMS
  Peak detection - Based on absolute value of the signal
  RMS (Root Mean Square) - Based on square of the signal
    Square of the level is average of square of the input
    Or Square of the level is smoothed estimate of square of the input
Other envelope followers
  Not so common
  Usually based on lowpass filtering absolute value of signal
Notes: For level detection, the choice is usually either peak or RMS. Peak based is quite simple, and it uses just the absolute value of the signal. RMS stands for root mean square, and involves estimation of level using some smoothed or averaged estimation from the square of the input signal.

## Slide 8: Issues with RMS level detection
Introduces significant delay
Introduces additional parameter, M or t
Several studies suggest general behaviour is the same for peak & RMS detection
  F. Floru, "Attack and Release Time Constants in RMS-Based Feedback Compressors," Journal of the Audio Engineering Society, vol. 47, pp. 788-804, October 1999.
  J. S. Abel and D. P. Berners, "On peak-detecting and rms feedback and feedforward compressors," in 115th AES Convention, 2003.
Notes: Well, there are a few reasons not to use the RMS sensing for level detection. First it requires some form of averaging, so it introduces a delay and the compressor becomes less responsive to sudden changes.
Second, its a bit awkward from an implementation point of view since it requires an additional parameter that is not seen by the user. Either there is a window length or a time constant. I should point out by the way, that I’m aware of one popular DAW where the built in compressor does not use averaging in the RMS detection. So its really just root square instead of root mean square.

## Slide 9: The Gain Computer
Static Compression Curve -depicts output signal level as a function of input signal level
Notes: Now lets move on to the gain computer.
Here we show whats at the heart of the compressor, the static compression curve, which depicts output signal level as a function of input signal level. This one plot describes the interaction of four parameters; threshold, ratio, knee width and make-up gain. I should note that although this depicts a static compression curve, it actually combines two stages; the gain computer and the gain stage.

## Slide 10: The Gain Computer
Compression ratio
  Hard knee
  Soft knee
    Linear interpolation (bad)
    Second order interpolation (good)
Notes: Ok, so how does this gain stage work.

## Slide 11: Make-up Gain
make-up gain simply adds to the output decibel level
Intended for loudness matching
Available as user control
Automated as function of threshold and ratio,
  Ignores input signal and actual amount of compression applied
Automated based on amount of gain reduction compressor applies to the signal
  must be smoothed on slow time scale to prevent makeup gain from affecting any dynamics
Notes: It’s easy to see that make-up gain simply adds to the output decibel level. Thus high thresholds (closer to 0dB) give less make-up gain than low thresholds, and similarly, high ratios give more make-up gain than low ratios. This is a common approach, and other designs feature an auto-makeup gain with similar values, e.g., .
However, this ignores the input signal, and ignores the actual amount of compression applied. If the input signal was fairly quiet, so there was very little compression, it would apply the same amount of make-up gain as if the signal was very loud and there was a lot of compression.
An alternative, is to base the make-up gain directly on the amount of gain reduction the compressor applies to the signal: the more average gain reduction, the more makeup-gain is required to compensate. A smoothed average of the control can be used as the make-up gain, where the smoothing is done on a slow enough time scale to prevent the makeup gain from affecting any dynamics. Thus, the time constant used for estimating make-up gain should be significantly larger than the compressor’s maximum release time.
Also, it should be noted also that there are advanced compressor implementations that offer an automated make-up gain which very closely matches the intended goal of matching the loudness of the compressed signal with the loudness of the uncompressed signal.

## Slide 12: That’s the easy part…
What about ballistics?
Attack Time- tA
  Time to decrease gain once signal overshoots threshold
Release Time- tR
  Time to bring gain back to normal once signal falls below threshold

## Slide 13: Exponential Moving Average Filter
Also known as smoothing filter, one pole low pass filter...
Step response
Time constant - time it takes a system to reach 1-1/e= 63% of its final value
Notes: At this point its important to introduce one of the most well known filters, the exponential moving average filter.

## Slide 14: Time constants
From the smoothing filter
Officially, time it takes a system to reach 1-1/e= 63% of its final value
  tA – level starts at 0, goes to 1. Attack time is the time it takes for level to reach 0.63.
  tR – level starts at 1, goes to 0. Release time is the time it takes for level to reach 1-0.63=0.37.
But some compressors,
  Miscalculate it
  Define it as time to go from 90% of initial value to 10% of final value
  Define it as time to change level by so many dBs
  ...

## Slide 15: Analog Peak Detector
  Assuming ideal diode,
    Where tA=RAC and tR=RRC
  Used in
    D. Berners, "Analysis of Dynamic Range Control (DRC) Devices," Universal Audio WebZine, vol. 4, September 2006.
    P. Dutilleux and U. Zölzer, "Nonlinear Processing, Chap. 5," in DAFX - Digital Audio Effects, U. Zoelzer, Ed., 1st ed: Wiley, John & Sons, 2002

## Slide 16: Analog Peak Detector
Step response
correct peak estimate only when release time is considerably longer than attack time
attack time gets slightly scaled by release time
  faster attack time than expected when we use a fast release time
Output of the peak detector circuit for different release time constants. Attack Time = 50ms.
Notes: Although used in many analogue compressors, and some digital designs, this circuit has a few problems. When xL[n] ≥yL [n], the step response is as shown. That is, for an input with amplitude 1, the output does not converge to 1. This implies that we will get a correct peak estimate only when the release time constant is considerably longer than the attack time constant. Another side effect is that the attack time also gets slightly scaled by the release time: there will be a faster attack time than expected when we use a fast release time. Both problems are illustrated in Figure 3.
SSL Stereo Bus and Fairchild 670 use dual release to get around this.

## Slide 17: Decoupled Peak Detector
attack envelope is now impressed upon release envelope
good estimate of actual release time given by adding attack time constant to release time constant
Notes: This shows an alternative peak detector where the subcircuits for attack and release are completely decoupled. The input signal is first fed through a peak detector with instantaneous attack. The result is a maximally fast peak estimation which is then buffered and smoothed by a first-order low-pass filter. The advantage of this is that the detector does not suffer from the level differences caused by different time constants exhibited by the standard peak detector circuit. Using the derivations for the analog peak detector, a digital implementation of the decoupled peak detector is straightforward.
However the attack envelope is now also impressed upon the release envelope. A good estimate of what the actual release time would be is given by simply adding the respective attack time constant to the release time constant.

## Slide 18: Branching Peak Detector
Easily accomplished in digital implementation
  G. W. McNally, "Dynamic Range Control of Digital Audio Signals," Journal of the Audio Engineering Society, vol. 32, pp. 316-327, May 1984.
  U. Zolzer, Digital Audio Signal Processing, 2nd ed.: John Wiley and Sons, Ltd., 2008.
Notes: In a solely digital environment, we can efficiently fix this by adding a branch to the difference equation of the standard peak detector.
The added branch ensures that the state variable is only discharged during the release phase.

## Slide 19: Time constants in decoupled & branching peak detectors
Output of decoupled and branching peak detector circuits for different release time constants
  branching peak detector produces intended release time constant
  decoupled peak detector produces measured time constant ~ tA+tR.
Notes: Branching has intended release, decoupled has release as tA+tR. This depicts the output of the decoupled and branching peak detector circuits for different release time constants. Compare the two red ones against each other, and the two blue ones against each other.
The branching peak detector produces the intended release time constant, whereas the decoupled peak detector produces a measured time constant of approximately tR+tA. Ideally then, the decoupled peak detector should be used with tR replaced by tR+tA. Instead, the attack time is often added to the release time for the branching peak detector. In which case, neither peak detector displays accurate time constants, but the release trajectories are roughly in agreement and it guarantees that the release time can never be shorter than the attack time.
Output of the decoupled and branching peak detector circuits for different release time constants. The branching peak detector produces the intended release time constant, whereas the decoupled peak detector produces a measured time constant of approximately tA+tR.

## Slide 20: Output of the branching peak detector circuits for different release time constants.

## Slide 21: Smooth, level corrected peak detector
Smooth decoupled peak detector
Smooth branching peak detector
  Used in
    P. Dutilleux, et al., "Nonlinear Processing, Chap. 4," in Dafx:Digital Audio Effects, 2nd ed: Wiley, 2011, p. 554.
    U. Zolzer, Digital Audio Signal Processing, 2nd ed.: John Wiley and Sons, Ltd., 2008.
Notes: All the analogue designs only make use of the full release time if the input returns back to zero after a peak. However, when the signal settles on an intermediate plateau instead, the release envelope will simply stop at this point and the release time is much shorter than we would expect. The sudden stop creates a discontinuity in the envelope output. We can adjust the branching peak detector in order to ensure that it will always make use of the full release time.
This peak detector now simply switches coefficients between the attack and the release phase.
The same modification can be introduced to the release mechanism of the decoupled peak detector, if a continuous release mechanism is desired.

## Slide 22: Comparison of Digital Peak Detectors
All envelopes reach maximum peak value and feature similar attack trajectories
Release envelopes too short for decoupled and branching peak detectors
  smoothed versions make full use of release time
Discontinuity for smooth, branching peak detector
  abrupt switch from attack to release
  release envelope is continuous for smoothed, decoupled peak detector
Notes: The attack trajectories are pretty much the same, and feature similar maximum peak values.
All the analogue designs only make use of the full release time if the input returns back to zero after a peak. However, when the signal settles on an intermediate plateau instead, the release envelope will simply stop at this point and the release time is much shorter than we would expect. The sudden stop creates a discontinuity in the envelope output.
That is, the nonsmooth peak detectors have short release times.
If we look at the inset, we see another problem.

## Slide 23: Feedforward or feedback design
Feedforward
Feedback
  Limiter (ratio of ∞: 1) needs infinite negative amplification
  Not designed for look-ahead
Notes: Now, we have two choices for the sidechain; either a feedforward or feedback design.
In both cases, a decibel level control is added to the input level to produce the output level. And in both cases, the same output-input static curve is used. So we can write the control in terms of the input for the feedforward case, or control in terms of the output for the feedback case.

## Slide 24: Static compressor block diagrams with linear/decibel conversion not depicted
Feedforward design
feedback design
alternate feedback design

## Slide 25: Sidechain configuration
  Level detection
  Decibel conversion
  Gain computer
  Timing (Ballistics, Smoothing)
Notes: Ok, so now it comes to putting it all together. At this point all we know is that there are 6 user-defined parameters as input to the side-chain, and quite a few different components. If we can define the ordering of the components, and the choice of how they are implemented, hopefully using the 6 parameters, then we have deifined the compressor design.

## Slide 26: Timing Placement- linear domain
R. J. Cassidy, "Level Detection Tunings and Techniques for the Dynamic Range Compression of Audio Signals," in 117th AES Convention, 2004.
J. S. Abel and D. P. Berners, "On peak-detecting and rms feedback and feedforward compressors," in 115th AES Convention, 2003.
U. Zolzer, Digital Audio Signal Processing, 2nd ed.: John Wiley and Sons, Ltd., 2008.
P. Hämäläinen, "Smoothing of the Control Signal Without Clipped Output in Digital Peak Limiters," in International Conference on Digital Audio Effects (DAFx), Hamburg, Germany, 2002, pp. 195-198.
S. J. Orfanidis, Introduction to Signal Processing Orfanidis (prev. Prentice Hall), 2010.

## Slide 27: Timing Placement- biased linear domain
Attack and release now depend on threshold, not zero
Envelope smoothly fades out once signal falls below threshold

## Slide 28: Timing Placement- linear domain, post-gain
J. Bitzer and D. Schmidt, "Parameter Estimation of Dynamic Range Compressors: Models, Procedures and Test Signals," presented at the 120th AES Convention, 2006
L. Lu, "A digital realization of audio dynamic range control," in Fourth International Conference on Signal Processing Proceedings (IEEE ICSP), 1998, pp. 1424 - 1427.

## Slide 29: Timing Placement- log (dB)omain
S. Wei and W. Xu, "FPGA implementation of gain calculation using a polynomial expression for audio signal level dynamic compression," J. Acoust. Soc. Jpn. (E), vol. 29, pp. 372-377, 2008.
S. Wei and K. Shimizu, "Dynamic Range Compression Characteristics Using an Interpolating Polynomial for Digital Audio Systems," IEICE Trans. Fundamentals, vol. E88-A, pp. 586-589, 2005.

## Slide 30: Block Diagrams of the Compressor Configuration. (a) the return-to-zero detector; (b) the return-to-threshold detector; (c) the log domain detector.

## Slide 31: Performance – sidechain configuration
release discontinuity in linear domain return-to-zero detector
linear domain return-to-threshold (biased) and log domain detector curves look similar
  faster attack, slower release for linear domain return-to-threshold
gain envelope produced by different placement of ballistics in sidechain configurations
Notes: The figure compares the three different detector options in terms of the linear gain envelope they produce. The attack lag and the release discontinuity of the linear domain return-to-zero detector can be clearly seen. The linear domain return-to-threshold and log domain detector curves look similar, though the former features faster attack and slower release behavior than the latter.
Figure 11. Compressor envelope trajectories in the linear domain for the linear domain return-to zero detector (solid), linear domain return-to-threshold detector (dotted) and log domain detector (dashed).

## Slide 32: Performance- Artifacts
How can we measure and characterise performance of a compressor?
Most artifacts associated with parameter settings, not design
  Dropouts
    Long release -> keeps attenuating after transient finished
  Overshoot
    Long attack -> misses attenuation of initial transient
  Lack of clarity
    Short attack -> squash all transients
  Pumping
    Short release -> jump in signal level after transient
  Breathing
    Noticeable movement of noise floor

## Slide 33: Performance- Noise and Distortion
Signal to Noise Ratio
  Not useful
Total Harmonic Distortion
  Measures strength of harmonics (introduced by compression) in relation to original frequency
Notes: Most objective measures of compressor performance have come from hearing aid design research. These often ignore the effects of distortion, which are considered negligible when speech intelligibility is the fundamental concern. Here, the total harmonic distortion (THD) is given for compressors based on the four peak detector designs as a function of the input signal frequency. The effect of smoothing in minimizing harmonic distortion is clearly evident. Furthermore, the decoupled peak detector offers a slight improvement over the branching design, with and without smoothing, since it minimizes the introduction of distortion components at the transition between attack and release phases.
Total harmonic distortion as a function of input signal. The input signal was a pure sinusoid with unity amplitude. Threshold, ratio, attack, release and knee were set to -20dB, 7, 1 ms, 15 ms and 0 dB, respectively.

## Slide 34: Performance – frequency dependence
Effective compression ratio
  used in assessing compressors in cochlear implants and hearing aids
  amplitude modulated sine wave applied at input
  spectrum consists of a carrier and two side bands
  DSi difference between amplitude of side bands and amplitude of carrier of input signal
  DSo difference between amplitude of side bands and amplitude of carrier of compressed signal is found,.
  effective compression ratio is then given by DSi/DSo.
Notes: One of the main metrics used in assessing compressors used in cochlear implants and hearing aids is the effective compression ratio. This is found by measuring the modulation of a signal at the output given a certain modulation at the input. An amplitude modulated sine wave is applied at the input. The spectrum consists of a carrier and two side bands. The difference between the amplitude of the side bands and the amplitude of the carrier is DSi. Compression is applied, and the difference between the amplitude of the side bands and the amplitude of the carrier of the compressed signal is found, DSo. The effective compression ratio is then given by DSi/DSo.

## Slide 35: Performance – effective compression ratio
  Interpretation?
Notes: One of the main metrics used in assessing compressors used in cochlear implants and hearing aids is the effective compression ratio. This is found by measuring the modulation of a signal at the output given a certain modulation at the input. An amplitude modulated sine wave is applied at the input. The spectrum consists of a carrier and two side bands. The difference between the amplitude of the side bands and the amplitude of the carrier is DSi. Compression is applied, and the difference between the amplitude of the side bands and the amplitude of the carrier of the compressed signal is found, DSo. The effective compression ratio is then given by DSi/DSo.
The effective compression ratio as a function of the modulation frequency is given in the figure. The input signal and compressor parameters were set as previously.The decoupled designs generally perform closer to the target compression ratio of 7:1. This is primarily due to the lack of full use of the release time in the branching compressors. However, the nonsmooth decoupled design actually outperforms the smooth decoupled design for high modulation frequencies, since the rapid decay of the compression ratio during release prevents the low amplitude modulator from being overly compressed.

## Slide 36: Performance- Ballistics and sidechain configuration
Detector Placement | Detector Type | Fidelity of Envelope Shape (FES) |  |  | 
 |  | Guitar | Bass | Drums | Vocals
Log domain | Branching | 0.884 | 0.945 | 0.766 | 0.952
 | Decoupled | 0.899 | 0.932 | 0.755 | 0.941
 | Branching Smooth | 0.852 | 0.927 | 0.640 | 0.941
 | Decoupled Smooth | 0.859 | 0.911 | 0.648 | 0.936
Linear domain | Branching | 0.836 | 0.879 | 0.517 | 0.932
 | Decoupled | 0.790 | 0.831 | 0.537 | 0.930
 | Branching Smooth | 0.825 | 0.856 | 0.456 | 0.932
 | Decoupled Smooth | 0.775 | 0.805 | 0.461 | 0.934
Measures correlation between envelopes of compressed and uncompressed signals
Nonsmooth designs do well since they often apply no compression
Placing ballistics (attack and release) in log domain outperforms placing them in linear domain
Fidelity of the envelope shape
Notes: Another metric from prior work on compressors for improved speech intelligibility is the Fidelity of the Envelope Shape (FES). This is intended to measure how well the envelope of the signal is maintained. It is based on a measure of the correlation between the envelopes (in dB) of the compressed and uncompressed signals. Although it is highly dependent on the envelope estimation method, it has the added benefit that it does not require an artificial test signal.
Here, we show, Fidelity of the Envelope Shape for compression applied to four acoustic signals. In each case, a strong, fast acting compressor was applied; threshold -40dB, ratio 10:1, attack time 1ms, release time 40ms, knee 20dB.
Only minor differences can be seen between the FES for the various log domain approaches. The slightly worse performance of the smooth compressors may be due to the fact that the signal is always in attack or release phase, whereas the nonsmooth compressors have times where the envelope is completely unchanged. More noticeable, however, is the difference in FES for different level detector placements.
The log domain detectors clearly outperform linear domain detectors on all signals except vocals (where there is only a minimal difference in FES).

## Slide 37: Dry/Wet mixing
Dynamic range compression is a ‘processor’ as opposed to an ‘effect.’
  produces a modified version of the signal
  intended to replace input with processed version at output.
  amount of compression is controlled by the Threshold and Ratio
But can also be used as an ‘effect’
  Something added to the original sound
  Then they come with a dry/wet mix
  this mixing is performed in the linear domain
  results in strange change of compression curve above Threshold
Notes: Dynamic range compression is generally considered to be a ‘processor’ as opposed to an ‘effect.’ Effects, like flanging, phasing and reverb, are intended to be added to an existing signal, and hence almost always come with a dry/wet mix. Processors, like EQ, gates and panners, produce a modified version of the signal. They are usually intended to replace the input with the processed version at output. Thus, they rarely come with a dry/wet mix. Instead, the amount of compression is controlled by the Threshold and Ratio. So its unusual and counterintuitive for the dynamic range compressor to have dry/wet mixing. Since this mixing is performed in the linear domain, it results in a strange change of the compression curve above the Threshold, but little else. However, as an artistic effect, there is nothing wrong with it.
The Dry/Wet mix may be analysed by assuming a static (attack and release are both zero) compression curve with hard knee, and a peak detector is used for the envelope follower. This simplified situation allows us just to deal with threshold, ratio and mix, and to state that the output, above the threshold is simply expressed as ydB =20log10|y[n]| =T+(20log10|x[n]|-T)/R. We can express the output in the linear domain, assuming positive input;
This is then the input to the mixing stage. So we can see how the input/output curve has been changed by mixing.
Where we’ve written the output several different ways, to show both a compact expression for the output, and to show how the output level as a function of input level has been modified.
Figure 13 shows the effect of the mixing parameter on the static input output curves. It can be seen that the behaviour is no longer linear above the threshold, and that even a small amount of mixing of the dry signal will generally make the dry signal dominate, e.g., 75% wet with ratio of infinity to 1 appears similar to a 100% wet with 2 to 1 compression.

## Slide 38: Dry/Wet mixing
Notes: shows the effect of the mixing parameter on the static input output curves. It can be seen that the behaviour is no longer linear above the threshold, and that even a small amount of mixing of the dry signal will generally make the dry signal dominate, e.g., 75% wet with ratio of infinity to 1 appears similar to a 100% wet with 2 to 1 compression.

## Slide 39: Pseudocode
% Smoothed branching digital dynamic range compressor.
% Parameters
% x: input signal
% fs: sample rate (kHz)
% tauAttack: attack time constant (ms)
% tauRelease: release time constant (ms)
% T: decibel threshold
% R: compression ratio
% W: decibel width of the knee transistion
% M: decibel Make-up Gain
% Returns
% y: output (compressed) signal

## Slide 40: Pseudocode
%LEVEL DETECTION
y_L = max(abs(x), 1e-6);
%DECIBEL CONVERSION
x_dB= y_L;
y_dB = 20*log10(x_dB);

## Slide 41: Pseudocode
%GAIN COMPUTER
x_G=y_dB; %Input to gain computer is (log) level estimation
slope = 1 / Ratio - 1;% Feed-forward topology
overshoot = x_G - T;
if (overshoot <= -W/2)
y_G =x_G;
if ((overshoot > -W/2) & (overshoot < W/2))
y_G =x_G+slope* (overshoot + W / 2) .^ 2/ (2*W) ;
if (overshoot >= -W/2)
y_G =x_G+slope* overshoot ;

## Slide 42: Pseudocode
x_T=y_G-x_G; %Input to ballistics is amount of gain reduction
%BALLISTICS
alphaAtt = exp(-1 / (tauAttack * fs));
alphaRel = exp(-1 / (tauRelease * fs));
if x_T(0) > 0 y_T(0) = (1-alphaAtt)*x_T(0);
else y_T(0) = (1-alphaRel)*x_T(0);
end
for i=2:length(x_T)
if x_T(i) > y_T(i-1)
y_T(i)= alphaAtt * y_T(i-1) + (1-alphaAtt)*x_T(i);
else
y_T(i)= alphaRel * y_T(i-1) + (1-alphaRel)*x_T(i);
end
end

## Slide 43: Pseudocode
c_dB = -y_T; %Control vector, from smoothed gain reduction
c_dB = M+c_dB; %Add make-up gain
gain = 10.^(c_dB./20); %Convert to linear
y = x .* gain; %Gain stage

## Slide 44: The big unknown – psychoacoustics
Compressor designs
  in the literature: >20
  Commercial designs: >40
Studies of parameter settings
  for hearing aids: >10
  for music production and broadcast: 0 ?
    Anecdotal recommendations : 10?
Studies of compressor designs
  for hearing aids: <5?
  for music production and broadcast: 0 !

## Slide 45: Recommendations
Feedforward compressors are preferred
  more stable and predictable than feedback designs
  Benefits of feedback designs are only relevant in analog
Peak level detection suggested over RMS
  RMS introduces additional parameter
    Often not user controlled
  Smoothing done anyway by attack and release
  May introduce unnecessary delay
Soft knee with high order interpolation
  Linear interpolation gives two hard knees

## Slide 46: Recommendations
Ballistics in the log domain after the gain computer
  Maintain envelope shape
  no attack lag
  easy implementation of variable knee width
Smooth, peak detector for attack and release
  Decoupled
    Low harmonic distortion
    Prevent discontinuities
  Branching
    detailed knowledge of the effect of the time constants
    Minor discontinuities in the slope of the gain curve
Make-up gain at end of side-chain
  Agrees with expected use
  Not intended or needed to be smoothed