## Slide 1: Phase vocoder, part 1
What you’ll learn:
Segmenting a real-time signal into windows
Working with overlapping windows (overlap-add)
Multi-threaded audio processing
What you’ll make:
A phase vocoder framework with simple effects

## Slide 2: Block-based processing
Sometimes audio calculations need to run on block of samples
  For example: wait until 512 samples arrive, then do something with all of them at once
Compare this to filters, where we calculate new output every sample
  With block-based processing, we typically run calculation periodically, not every sample
run calculation

## Slide 3: Block-based input
input
buffer
Start with fixed size buffer
  Fill it up sample by sample
  When it’s full, apply window function and pass it to block-based process (like FFT)
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
write
pointer
current
sample
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
x[n]
Block-based
processing
Apply
window
Block-based
processing
Apply
window
Block-based
processing
Apply
window
S12
S13
S14
S15
S16
S17

## Slide 4: Block-based input and output
After dividing signal into windows, often want to reconstruct it
  Process each block
  Stitch processed blocks together into
  new signal
  If we don’t process each block,
  should reconstruct signal exactly
Application: phase vocoder
  FFT on each block
  Do processing in frequency domain
  Use phase of bins for accurate frequency
  estimate
  IFFT on each block

## Slide 5: Block-based input and output
input
buffer
Ideal block-based processing system might work something like this:
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
write
pointer
current
sample
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
x[n]
Block-based
processing
Apply
window
Block-based
processing
Apply
window
Block-based
processing
Apply
window
S12
S13
S14
S15
S16
S17
...
y[n]
output
buffer
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
Y9
Y10
Y11
Y12
Y13
Y14
Y15
Y16
Y17
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
Y9
Y10
Y11
Y12
Y13
Y14
Y15
Y16
Y17
read
pointer
Problem: not causal!

## Slide 6: Block-based output: causality
For causal system, output cannot depend on future inputs
Partial solution: add 1-window latency to output
  As we gather input samples for next FFT, copy samples from last FFT into output
...
Block 0
Block 1
Block 2
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
...
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
...
Block-based
processing
Block-based
processing
Block-based
processing
Block-based
processing
x[n]
y[n]
Problem: y[0] depends on x[5]. System is not causal!

## Slide 7: Overlapping blocks
Previous example performed block calculation at regular intervals
  Once full block of samples assembled, it was processed (e.g. using an FFT)
  Larger window (block) size, less frequent the calculations
  In that example, each input sample was part of exactly one block
It can be useful to have blocks that overlap one another
  For example, use larger FFTs but calculate them more often
  Number samples between start of consecutive blocks is called hop size
  This is often fraction of block size (or window size)
    For example, FFT size 1024, hop size 512
Might apply window function before calculating FFT
  In this example, a triangular window
Window size = M
Hop size = M/2

## Slide 8: Overlap-Add
Standard approach for block-based processing with overlapping blocks is overlap-add:
  Isolate block of length M using windowing function
  Take FFT of length N ≥ M of segment
    If N > M, zero-pad block (add zeros to end of window)
  Do something interesting to frequency-domain data
  Take IFFT to get new time domain segment
  Add the segment to an output buffer which also contains the preceding segments
    As we’ll see, can’t write segment directly to audio output
  Advance by hop size (H) to next frame and repeat
    In real time, count samples until H more have arrived
    Hop size H is less than window size M, hence the overlap
FFT
effect
IFFT

## Slide 9: Review: overlapping blocks (input side)
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
...
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
Goal is to work with overlapping blocks in real time
  This means block k shares some samples with block k-1
  How do we adapt our windowing code to handle this?
Easiest approach: keep a running history of the input samples
  i.e. a buffer which always has the last M samples
  What kind of structure have seen that does this?
  At each hop, pass M samples from circular buffer to FFT
x[n]
y[n]
Circular buffer

## Slide 10: Review: overlap-add with a circular buffer
We use a circular buffer to keep track of the input
Necessary characteristics:
  The buffer always holds (at least) the last M input samples (where M is the window size)
  If using multiple channels, one buffer per channel
Using the circular buffer:
  Each iteration of the for() loop:
    store input in buffer
    increment the write pointer (wrapping as necessary)
    increment the total count of samples stored
  When the count reaches the hop size:
    take one window from buffer, unwrap it, and pass it to FFT
    in other words: copy it to a new buffer such that the oldest sample appears at index 0 of the new buffer
x[24]
x[12]
x[18]
x[6]
x[3]
x[25]
x[26]
x[4]
x[5]
x[7]
x[8]
x[9]
x[10]
x[11]
x[15]
x[14]
x[13]
x[16]
x[17]
x[19]
x[20]
x[21]
x[22]
x[23]
write pointer
(next sample to
be replaced)
latest
window
(M = 8 in this
example)
Important: this
is not the same as
when the write
pointer wraps around!

## Slide 11: Review: unwrapping the circular buffer
x[24]
x[12]
x[18]
x[6]
x[3]
x[25]
x[26]
x[4]
x[5]
x[7]
x[8]
x[9]
x[10]
x[11]
x[15]
x[14]
x[13]
x[16]
x[17]
x[19]
x[20]
x[21]
x[22]
x[23]
write pointer
(next sample to
be replaced)
latest
window
(M = 8 in this
example)
x[24]
x[25]
x[26]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[9]
x[10]
x[11]
x[12]
x[13]
x[14]
x[15]
x[16]
x[17]
x[18]
x[19]
x[20]
x[21]
x[22]
x[23]
How the circular buffer is actually stored in memory:
What we need to calculate the FFT (the latest 8 samples):
x[19]
x[20]
x[21]
x[22]
x[23]
x[24]
x[25]
x[26]
In other words: having assembled the samples into a circular buffer, on each hop it is helpful to copy them into a linear (standard) buffer to pass to the FFT library

## Slide 12: Block-based output: overlap
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
We need an intermediate output buffer (different from the system audio output) to hold the results of our block-based calculation
  Each window, the new output should be added into that buffer
  A sample can be sent from there to the system output as soon as all the blocks it depends on have been calculated (this implies a latency of at least 1 window)
x[n]
Block-based
processing
Block-based
processing
Block-based
processing
Block-based
processing
Block-based
processing
output
buffer
Note: these output
samples are
the sum of parts
of two different
blocks

## Slide 13: Output circular buffer
Circular buffer to get output from overlap-add
  Different from input circular buffer
Keep track of 2 pointers in circular output buffer
  Write pointer: where does next block get written once it’s calculated?
    moves in jumps of hop size
  Read pointer: where to get next sample for system output?
    moves continuously frame by frame
  Write pointer must remain ahead of read pointer
Necessary characteristics of the output buffer:
  Hold at least W+H samples, where W is window size, H hop size
  One buffer per channel of signal
  Needs array, write pointer from FFT & read pointer to system output
Using the output buffer:
  After inverse FFT, add result into output buffer, starting at write pointer
  In processBlock, copy from output buffer to audio output at read pointer
  Then set sample you just copied to 0
  Finally, increment read pointer
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
xxx
read
pointer
write
pointer
Output
circular buffer:

## Slide 14: The full signal chain
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
x[n]
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
...
y[n]
write
pointer
input
buffer
Block-based
processing
Apply
window
output
buffer
add
result
at write
pointer
most
recent W
samples
read pointer
these processes
happen every frame
this happens once per hop (every H samples)
ECS7012P Music and Audio Programming • Week 10a

## Slide 15: Overlap-add task
Task: using fft-overlap-add project, implement the output circular buffer
  Variables are already declared for you at the top of the file
  Write pointer is for keeping track of where the next block is written
  Read pointer keeps track of where to copy samples to the audio output
  Notice that process_fft() takes four arguments:
    input buffer, input pointer, output buffer, output write pointer
  Look at bottom of process_fft() to see how output is copied to the buffer
Add your code in render():
  Copy samples from the output buffer to the audio output (use the variable out)
  After you copy the output, set that sample in the output buffer to 0
  Increment the output circular buffer pointers in the relevant places
    Which one happens every frame? Which one advances once per hop?
Once it works, try uncommenting the robotise code in process_fft()
ECS7012P Music and Audio Programming • Week 10a

## Slide 16: Block-based processing performance
Try changing the block size to 4 samples
What happens to the output? Why?

## Slide 17: The full signal chain: performance
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
x[n]
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
...
y[n]
write
pointer
input
buffer
Block-based
processing
Apply
window
output
buffer
add
result
at write
pointer
most
recent W
samples
read pointer
How long do the FFT and IFFT have to run?
1 sample. Why might this be a problem?
ECS7012P Music and Audio Programming • Week 10a

## Slide 18: Intermittent CPU load
We've been assuming the CPU load is roughly constant over time
  Even if the average load is within limits, the instantaneous load might not be!
Example: say we do an FFT every 10 samples
  Let's assume only the FFT takes any time
  With a buffer size of 8, we're fine:
  Calculation takes less than one buffer length
  But with a buffer size of 4, we're not...
  Calculation takes longer than a call to render()
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
FFT
FFT
...
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
FFT
FFT
ECS7012P Music and Audio Programming • Week 10a

## Slide 19: Handling intermittent load
What can we do about occasional, heavy load?
  Most calls to render() do almost nothing; some calls can't finish on time...
We should add latency so the result doesn’t need to be ready in 1 sample
  But that still doesn’t solve the problem if a calculation spans multiple calls to render()
Solution: move the expensive process to another thread
  Run the FFT on a thread with lower priority than render()
  The FFT thread will use whatever processing is left over when render() is not running
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
FFT
FFT
ECS7012P Music and Audio Programming • Week 10a

## Slide 20: The full signal chain: added latency
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
Block 0
Block 1
Block 2
...
x[n]
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
...
y[n]
write
pointer
input
buffer
Block-based
processing
Apply
window
output
buffer
add
result
at write
pointer
most
recent W
samples
read pointer
Now we have 1 full hop to finish
the FFT calculations
ECS7012P Music and Audio Programming • Week 10a

## Slide 21: Multi-threaded processing
use two threads
  render(): high priority, runs every callback, finishes quickly
  process_fft(): lower priority, runs occasionally, takes longer to finish
    This will run whenever render() is not running
    Still higher priority than the rest of Linux
With 2 threads, render() always runs first
  The rest of the time is spent on the FFT, which could span multiple callbacks
FFT thread should sleep and wait for a signal to run
  render() should send the signal when a new hop has elapsed
  render() also needs to tell FFT thread where to find data (locations of buffers & pointers it needs)
  FFT thread should run calculation, store the output in the buffer, then return
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
render()
FFT
process_fft()

## Slide 22: Multi-threaded processing
With 2 threads, render() always runs first
  The rest of the time is spent on the FFT, which could span multiple callbacks
process_fft() is allowed to be interrupted by render()
  That means we need to be careful not to let render() modify any variables process_fft() was using
  Main concern here is the input buffer pointer, which will keep changing before process_fft() is even allowed to run. Need to cache this value (save a copy that render() won’t change).
  Reverse isn’t true: render() won’t be interrupted because it has higher priority
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
FFT
render()
process_fft()

## Slide 23: Threading task
Task: using the fft-overlap-add-threads project
  Convert the code to run the FFT in a second thread
  Use JUCE
  Also finish implementing process_fft_background()
S0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
S22
S23
FFT
render()
process_fft()