## Slide 1
Phase Vocoder Effects
Mutation, Robotisaton, Whisperisation, Pitch shifting, Time scaling

## Slide 2: Phase Vocoder
Sound analysis-synthesis techniques performed in the spectral domain
  widely recognised ‘standard’ implementation
decompose signal over short windowed frames (STFT) to analyse frequency content over time
  Take into account phase information
Applications
  Time scaling / pitch shifting of audio
  Signal Content Analysis
  Denoising
  Sound synthesis by example
  Pitch detection
  Steady State/Transient Separation
  …

## Slide 3: Introduction: FFT
What is the FFT?
  Fast Fourier Transform
  Algorithm to compute Discrete Fourier Transform (DFT) for evenly-spaced frequency samples
  DFT can be seen as sampling of Discrete-Time Fourier Transform (DTFT)
    DTFT:
    DFT:
    FFT:
(continuous frequency)
(discrete frequency)
Same as DFT: just a specific implementation

## Slide 4: Introduction: FFT
Reconstructing signal from DFT/FFT
  Inverse Discrete Fourier Transform (IDFT/IFFT)
    DFT:
    IDFT:
Notice: N time samples N frequency samples
  Two different perspectives on same signal
  Given a signal of length M, can exactly reconstruct from an FFT of length N ≥ M
    What happens with an FFT of length N < M?
Aliasing

## Slide 5: Windowing
Suppose we look at only short slice of input signal
  Want instantaneous snapshot of frequency content
  Window the signal, then apply the DFT
    Multiply by a function that’s nonzero for a fixed length M
    Might also have a shape within the nonzero section: rectangular, triangular (Bartlett), Hamming, Blackman, etc.
    Can reconstruct windowed signal from DFT length N as long as N ≥ M

## Slide 6: Four popular window functions

## Slide 7: Effect of a rectangular window and a Hann window applied to a signal

## Slide 8: Short-Time Fourier Transform
Short-Time Fourier Transform (STFT) is the DTFT of the windowed signal
  Similarly, can take DFT/FFT for discrete samples of windowed signals
Can break any signal into windowed segments
  ...then (in the right circumstances) put it back together

## Slide 9: Overlap-Add
Can split signal into overlapping segments
  Distance between segments is called hop size
  Here, reconstruction from triangular windows with hop size M/2 (can do same with Hamming windows)
Remember, take DFT of each segment to get frequency content, IDFT to get back...

## Slide 10: Overlap-Add
Overlap-Add processing method:
  Take mth segment (frame) of length M using windowing function
  Take DFT of length N ≥ M of segment
    If N > M, zero-pad the segment (add zeros to end)
  Do something interesting to frequency data
  Take IDFT to get back to time domain segment
  Add result to output buffer containing prior segments
  Advance by hop size to (m+1)th frame and repeat

## Slide 11: Overview of Overlap and Add Process
FFT
IFFT
Frequency Domain
Processing
...
...
+
+
+
+
+
+
x[n]
y[n]
Break input signal into windows
Add results of each IFFT to output
Hop Size
Window Size
for each window:
...
...
Segment audio by applying window function
Apply FFT to each segment
Extract phases and amplitudes
Do stuff!
Apply IFFT to each segment
Overlap segments and append on to output audio

## Slide 12: Relationship between actual phase and target phase.
k-1
k
f
ft
fd
wkh
Frequency bin
Phase
Instantaneous frequency represented by gradient of dashed line
Bin frequency is gradient of solid line.
Ft – target phase
Fd –phase deviation

## Slide 13: constant overlap-add criterion requires that window functions, when overlapped, add to constant value. holds in top plot, but not bottom plot.

## Slide 14: complex baseband filterbank implementation (top) where h[n] is low pass filter, and complex bandpass implementation (bottom). Only filters for first 3 bins shown
h[n]
h[n]
h[n]
x[n]
X[n,w0]
X[n,w1]
X[n,w2]
e-jw n
0
e-jw n
1
e-jw n
2
.
.
.
ejw n
1
ejw n
2
.
.
.
ejw n
0
y[n]
h[n]ejw0n
h[n]ejw1n
h[n]ejw2n
x[n]
X[n,w0]
X[n,w1]
X[n,w2]
.
.
.
ejw n
1
ejw n
2
.
.
.
ejw n
0
y[n]
e-jw n
0
e-jw n
1
e-jw n
2

## Slide 15: Applications
Many possibilities between DFT and IDFT
  Efficient FIR convolution
    FIR filter of length N needs N multiplies per sample
    Convolution in time = multiplication in frequency
  Mutation and cross-synthesis
  Robotisation and whisperisation
  Time-stretching and pitch-shifting
H(z)
X(z)
Y(z)

## Slide 16: Mutation
DFT bins have magnitude and phase
Suppose we have DFTs of two signals
  Combine magnitudes and phases in interesting combinations
  Sometimes known as cross-synthesis or morphing
  For example, magnitude from one, phase from other

## Slide 17: Mutation
Example operations on magnitude only
  Multiplication: r = r1 * r2
    Multiplication in linear terms = addition in dB scale
    Similar to spectral AND operation, keeping zones where energy is located in both signals
    For fixed r2 (and zero phase z2), equivalent to FIR filtering
  Addition: r = r1 + r2
    Similar to spectral OR operation
    Not simple mixing: only operating on magnitudes, not phases
  Masking: r = (r2 > threshold ? r1 : 0)
    Keep magnitude of one sound only if the other is above a threshold
    (A ? B : C) syntax means “if A, then B, otherwise C”

## Slide 18: Mutation
Phase is critical to time-frequency representations
  Explains how signals evolve from frame to frame
  Has an important influence on output quality
Example operations on phase of two inputs
  Keep phase of only one sound, change magnitude
    Phase is a strong cue for pitch of sound (why?)
    Result: pitch influenced by the phase you keep
  Add phases
    Strong alteration: phase moves at double speed on average
    Or double the reconstruction hop size: n2 = 2 * n1
  Arbitrary combination or variation on phases

## Slide 19: Robotisation
Robotisation = applying fixed pitch onto a sound
  Implemented by setting DFT phase values to 0 before reconstruction
  Forces periodicity: erratic and random variations converted into fixed-pitch sound
  Pitch determined by hop size between segments
    Can even be adjusted dynamically to create pitch changes
  “Robot voice” effect
Sound examples: before and after robotisation

## Slide 20: Robotisation VST I
int inwritepos; // Write pointer into the input buffer
int outwritepos; // Write pointer into the output (overlap-add) buffer
int outreadpos; // Read pointer into the output buffer
int inputBufferLength; // Length of the input buffer (in samples)
int outputBufferLength; // Length of the output buffer (in samples)
int sampsincefft; // Counter of how many samples have elapsed since last FFT
float *windowBuffer; // Buffer that holds the (pre-calculated) window function
int windowBufferLength; // Length of the window function
float *fftTimeDomain; // Buffer that holds time-domain samples for the FFT calculation
float *fftFrequencyDomain; // Buffer that holds frequency-domain samples from FFT
float fftScaleFactor; // Scaling factor to normalize output level; depends on window/hop sizes
int fftTransformSize_; // Size of the FFT calculation (in samples); normally equals
// window size but could be longer
int hopSize_; // Hop size parameter (in samples)
// Collect the audio samples in the input buffer. When we've reached the next
// hop interval, calculate the FFT and process the pitch shift.

## Slide 21: Robotisation VST II
for (int i = 0; i < numSamples; ++i)
{
const float in = channelData[i];
// Store the next buffered sample in the output. Do this first before anything
// changes the output buffer-- we will have at least one FFT size worth of data
// stored and ready to go. Set the result to 0 when finished in preparation for the
// next overlap/add procedure.
channelData[i] = outputBufferData[outreadpos];
outputBufferData[outreadpos] = 0.0;
if(++outreadpos >= outputBufferLength) outreadpos = 0;
// Store the current sample in the input buffer, incrementing the write pointer. Also
// increment how many samples we've stored since the last transform. If it reaches
// the hop size, perform an FFT and any frequency-domain processing.
inputBufferData[inwritepos] = in;
if (++inwritepos >= inputBufferLength) inwritepos = 0;

## Slide 22: Robotisation VST III
if (++sampsincefft >= hopSize_)
{
sampsincefft = 0;
// Find the index of the starting sample in the buffer. When the buffer length
// is equal to the transform size, this will be the current write position but
// this code is more general for larger buffers.
int inputBufferStartPosition = (inwritepos + inputBufferLength
- fftTransformSize_) % inputBufferLength;
// Window the buffer and copy it into the FFT input
int inputBufferIndex = inputBufferStartPosition;
for(int fftBufferIndex = 0; fftBufferIndex < fftTransformSize_; fftBufferIndex++)
{
// Set real part to windowed signal; imaginary part to 0.
fftTimeDomain[fftBufferIndex][1] = 0.0;
if(fftBufferIndex >= windowBufferLength) // Safety check, in case window
// isn't ready
fftTimeDomain[fftBufferIndex][0] = 0.0;
else
fftTimeDomain[fftBufferIndex][0] = windowBuffer[fftBufferIndex]
* inputBufferData[inputBufferIndex];
inputBufferIndex++;
if(inputBufferIndex >= inputBufferLength)
inputBufferIndex = 0;
}

## Slide 23: Robotisation VST IV
// Perform the FFT on the windowed data, going into the frequency domain.
// Result will be in fftFrequencyDomain
fftw_execute(fftForwardPlan_);
// ********** PHASE VOCODER PROCESSING GOES HERE **************
// This is the place where frequency-domain calculations are made
// on the transformed signal. Put the result back into fftFrequencyDomain
// before transforming back.
// ************************************************************
for(int bin = 0; bin < fftTransformSize_; bin++)
{
float amplitude = sqrt(fftFrequencyDomain[bin][0]*fftFrequencyDomain[bin][0]
+ fftFrequencyDomain[bin][1]*fftFrequencyDomain[bin][1]);
// Set the phase of each bin to 0. phase = 0 means the signal is entirely
// positive-real, but the overall amplitude is the same as before.
fftFrequencyDomain[bin][0] = amplitude;
fftFrequencyDomain[bin][1] = 0.0;
}
// Perform the inverse FFT to get back to the time domain. Result wll be
// in fftTimeDomain. If we've done it right (kept the frequency domain
// symmetric), the time domain resuld should be strictly real allowing us
// to ignore the imaginary part.
fftw_execute(fftBackwardPlan_);

## Slide 24: Robotisation VST V
// Add result to output buffer, starting at current write position
// (Output buffer will have been zeroed after reading the last time around)
// Output needs to be scaled by the transform size to get back to original
// amplitude: this is a property of how fftw is implemented. Scaling will also
// need to be adjusted based on hop size to get the same output level (smaller
// hop size produces more overlap and hence higher signal level)
int outputBufferIndex = outwritepos;
for(int fftBufferIndex = 0; fftBufferIndex < fftTransformSize_; fftBufferIndex++)
{
outputBufferData[outputBufferIndex] += fftTimeDomain[fftBufferIndex][0] * fftScaleFactor;
if(++outputBufferIndex >= outputBufferLength) outputBufferIndex = 0;
}
// Advance the write position within the buffer by the hop size
outwritepos = (outwritepos + hopSize_) % outputBufferLength;
}
}

## Slide 25: Robotisation
Window size affects performance
  Use short window to capture just one period of waveform per segment
  Left: M = 1024; Right: M = 64

## Slide 26: Whisperisation
Whisperisation = erasing pitch cues
  Implemented by randomising DFT phases before reconstruction
  Short window lengths work best

## Slide 27: Whisperisation VST
adapt previous robotization code example to perform whisperization
  basic overlap-add structure stays
  only need to change lines following FFT calculation
int for(int bin = 0; bin <= fftTransformSize_ / 2; bin++)
{
float amplitude = sqrt(fftFrequencyDomain[bin][0]*fftFrequencyDomain[bin][0] +
fftFrequencyDomain[bin][1]*fftFrequencyDomain[bin][1]);
// This is what we would use to exactly reconstruct the signal:
// float phase = atan2(fftFrequencyDomain[bin][1], fftFrequencyDomain[bin][0]);
// Instead, use this to scramble phase:
float phase = 2.0 * M_PI * (float)rand() / (float)RAND_MAX;
// Set phase of each bin to 0. phase = 0 means signal entirely positive-real,
// but overall amplitude same as before.
fftFrequencyDomain[bin][0] = amplitude * cos(phase);
fftFrequencyDomain[bin][1] = amplitude * sin(phase);
// FFTs of real signals are conjugate-symmetric. We need to maintain that symmetry
// to produce a real output, even as we randomize the phase.
if(bin > 0 && bin < fftTransformSize_ / 2) {
fftFrequencyDomain[fftTransformSize_ - bin][0] = amplitude * cos(phase);
fftFrequencyDomain[fftTransformSize_ - bin][1] = -amplitude * sin(phase);
}
}

## Slide 28: Denoising
Removal of unwanted low level sounds not intended to be in signal
  Reduce unwanted low level sound on musical recording usually 'hiss' or 'hums'
  Remove artefacts produced by nonlinear operations
  Minimize unwanted low level (generally high) frequencies
Noise from any number of sources
  usually appears as high frequency 'hiss', or low level 'hum'
Goals
  achieve clean crisp signal by reducing overall noise
  Don’t disrupt wanted signal
Denoising performed using analysis and synthesis
  extract magnitude and phase information
  Phase unchanged
  Low magnitudes attenuated

## Slide 29: Denoising
Two basic nonlinear algorithms:
  and
  x is input signal, c is noise reduction coefficient
  Another example implementation:
Similar to applying noise gate
  However, operates on each frequency component
  Only magnitude modified; phase remains as it was
function ft = denoise(f,r,coef)
if abs(f) >= 0.001
ft = f.*(r./(r+coef));
else
ft = f.*(r./(r+sqrt(coef)));
end

## Slide 30: Denoising
Example spectra for windowed FFT of flute sound
  Left: input signal
  Right: output according to with c = 0.01

## Slide 31: Denoising example
Denoising reduces amplitudes of each bin
  Need to boost overall signal level to maintain loudness
    Similar to dynamic range compressor
  In this example, gain of 4.75 to restore level

## Slide 32: Denoising variations
Analyse noise content first
  Apply different nonlinear function to each bin
  For example, reducing ventilation noise in a room
Time-varying noise estimation
  Estimate noise threshold as function of spectrum
  Often involves LPC or cepstral techniques
Use noise estimation to decrease pumping effects
Denoising is nonlinear and can produce artefacts
  Small grains (spurious components) that jump out
  Noise can also be a useful component of a sound

## Slide 33: Time scaling and pitch shifting
Analysis identical to any standard phase vocoder
Synthesis hop size varied for time compression/expansion
  Changes time scale without changing pitch
If pitch shifting, interpolate back to original time scale
  Now pitch changed, but time scale is unchanged

## Slide 34: Pitch shifting VST I
int outwritepos; // Temporary write pointer
float *inputBufferData; // Buffered input samples awaiting FFT
int inputBufferLength; // Length of the input buffer (in samples)
float *outputBufferData; // Buffered output samples for overlap-add
int outputBufferLength; // Length of the output buffer (in samples)
int sampsincefft; // Counter of how many samples have elapsed since last FFT
float *windowBuffer; // Buffer that holds the analysis window function
int windowBufferLength; // Length of the analysis window function
float *synthWindowBuffer; // Buffer that holds the synthesis window function
int synthesisWindowLength;// Length of the synthesis window
float *fftTimeDomain; // Buffer that holds time-domain samples for the FFT calculation
float *fftFrequencyDomain; // Buffer that holds frequency-domain samples from FFT
float fftScaleFactor; // Scaling factor to normalize output level; depends on window/hop sizes
float *resampledOutput; // Buffer holding resampled (interpolated) output from FFT
float **lastPhase; // Previous phase values for each bin and channel
float **psi; // Adjusted phase values for each bin and channel
int fftTransformSize_; // Size of the FFT calculation (in samples); normally equals
// window size but could be longer
double pitchRatio_; // Ratio of output to input frequency
int analysisHopSize_; // Hop size parameter for input (in samples)
int synthesisHopSize_; // Hop size parameter for output (in samples)
// synthesis / analysis size should match pitchRatio_

## Slide 35: Pitch shifting VST II
executes the pitch shift for one (overlapped) FFT window
fftw_execute(fftForwardPlan_);
for (int i = 0; i < fftTransformSize_; i++) {
// Convert bin into magnitude-phase representation
double magnitude = sqrt(fftFrequencyDomain[i][0] * fftFrequencyDomain[i][0] +fftFrequencyDomain[i][1] * fftFrequencyDomain[i][1]);
double phase = atan2(fftFrequencyDomain[i][1], fftFrequencyDomain[i][0]);
// Calculate frequency for this bin
double frequency = 2.0 * M_PI * (double)i / fftTransformSize_;
// Increment the phase based on frequency and hop sizes
double deltaPhi = (frequency * analysisHopSize_) +
princArg(phase - lastPhase[i][channel] - (frequency * analysisHopSize_));
lastPhase[i][channel] = phase;
psi[i][channel] = princArg(psi[i][channel] + deltaPhi * synthesisHopSize_);
// Convert back to real-imaginary form
fftFrequencyDomain[i][0] = magnitude * cos(psi[i][channel]);
fftFrequencyDomain[i][1] = magnitude * sin(psi[i][channel]);
}
fftw_execute(fftBackwardPlan_); // Perform inverse FFT

## Slide 36: Pitch Shifting VST III
// Resample output using linear interpolation to stretch it
double outputLength = floor(fftTransformSize_ / pitchRatio_);
for(int i = 0; i < outputLength; i++) {
x = i * fftTransformSize_ / outputLength;
ix = floor(x);
dx = x - (double)ix;
resampleOutput[i] = fftTimeDomain[ix]*(1.0 - dx) + fftTimeDomain[(ix+1)%fftTransformSize_]*dx;
}
// Add the result to the output buffer, starting at the current write position
int outputBufferIndex = outwritepos;
for(int fftBufferIndex = 0; fftBufferIndex < outputLength; fftBufferIndex++) {
if (fftBufferIndex > synthesisWindowLength) outputBufferData[outputBufferIndex] += 0;
else outputBufferData[outputBufferIndex] += resampleOutput[fftBufferIndex] * fftScaleFactor * synthesisWindowBuffer[fftBufferIndex];
if(++outputBufferIndex >= outputBufferLength) outputBufferIndex = 0;
}
// Advance the write position within the buffer by the hop size
// (Use original hop size since we have resampled output back to expected length)
outwritepos = (outwritepos + analysisHopSize_) % outputBufferLength_;