## Slide 1: JUCE and VST

## Slide 2: JUCE - Jules' Utility Class Extensions
Oen source cross-platform C++ codebase for developing desktop and mobile applications, & plug-ins
Used to write software so it runs with same user experience on many platforms & in many formats
contains classes covering many other commonly used features
  UI elements, graphics, audio, XML & JSON parsing, networking, cryptography, multi-threading…
  reduces number of third-party libraries needed
Supports Windows, macOS, Linux, iOS and Android operating systems
Created in 2004 by Jules Storer

## Slide 3: The Projucer
Once files and settings for JUCE project specified, it automatically generates 3rd-party project files to allow project to compile natively on each target platform
  Visual Studio, Xcode, Android Studio, CodeBlocks and Linux Makefiles
Also has code editor, integrated GUI editor, wizards for creating new projects and files
JUCE’s build configuration tool for creating and managing JUCE projects

## Slide 4: JUCE and audio
Most widely used framework for audio application and plug-in development
Large audio functionality
  Support for audio devices (such as CoreAudio, JACK, DirectSound) and MIDI playback, DSP building blocks, polyphonic synthesizers…
  built-in readers for common audio file formats (WAV, AIFF, FLAC, MP3, Vorbis…)
Comes with wrapper classes for building audio plugins
Single binary produced that supports multiple audio plugin formats
  Supports VST, VST3, AU, AUv3, AAX, LV2 … plug-in formats
    Use in DAWs like Logic, Live, Pro Tools, FL Studio or Cubase
  Since all platform and format-specific code is contained in the wrapper, user can build for almost any plug-in format & platform from single codebase

## Slide 5: Basic JUCE audio plug-in components and their relationship to the DAW
PluginProcessor
processBlock()
setValue()
getValue()
prepareToPlay()
releaseResources()
Audio Callback
Init. and Cleanup
Parameter Controls
PluginEditor
sliderValueChanged()
...and other control types
timerCallback()
called periodically by system
GUI Handlers
GUI
DAW
called once before starting
called once after finishing
called continuously while running

## Slide 6: VST – Virtual Studio Technology
Created by Steinberg in 1996
  Steinberg, creators of Cubase, Nuendo, … owned by Yamaha since 2005
audio plug-in software interface
integrates software synthesizers & effects units into digital audio workstations
Often uses digital signal processing to simulate traditional recording studio hardware
Main industry standard for audio plug-ins

## Slide 7: Overview of VST plugins
usually run within digital audio workstation (DAW)
  provide additional functionality
  standalone plugin hosts also exist that support VST
usually have graphical user interface that displays controls similar to physical switches and knobs on audio hardware
Most are either instruments (VSTi) or effects (VSTfx)
  other categories exist, e.g spectrum analyzers and various meters

## Slide 8: VST effects (VSTfx)
VST effects process audio
receive digital audio and process it through to their outputs
perform same functions as hardware audio processors
Chaining
  most hosts can route audio output from one VST to input of another
  For example, output of VST synthesizer can be sent through reverb effect

## Slide 9: VST Instrument (VSTi)
VST Instrument plugins generate audio
Can act as standalone software synthesizers, samplers, or drum machines
  Often emulate look & sound of hardware synthesizers and samplers
  lets musicians and recording engineers use virtual versions of devices that otherwise might be difficult to obtain
MIDI messages control instrument parameters
  Receive musical notes as digital information via MIDI
  Output digital audio
  Some effect plugins also accept MIDI input
    for example, MIDI sync to modulate the effect in sync with tempo

## Slide 10: Other VSTs
VST Monitoring effects
  Special type of VST effect
  Provide feedback about input signal without processing audio
  Audio monitoring devices represent audio characteristics visually
    Spectrum analysers: frequency distribution
    Meters: amplitude
VST MIDI effects
  process MIDI messages (for example, transpose or arpeggiate), and
  route MIDI data to other VST instruments or hardware devices

## Slide 11: VST Host
software application or hardware device in which VST plugins run
presents plugin UIs and routes digital audio & MIDI to and from plugins
Stand-alone hosts provide environment for VST plugins
  Often optimized for live performance use
Hardware VST hosts can load special versions of VST plugins
  portable & usable without computer, though some require computer for editing
  either
    run music applications like Cubase, Live, Pro Tools, Logic etc.
    run their own DAW
    require separate DAW application

## Slide 12: What we will do
Learn audio processing and programming concepts
Learn how to process audio samples and MIDI
Use JUCE to develop VST plugins and standalone applications in C++
Prototype and deploy different audio effects, filters, instruments and generators