## Slide 1: Phase vocoder, part 2
Look more at working in frequency domain
Window functions: why and how
  Constant Overlap-Add (COLA) criterion
  Analysis and synthesis windows
Reconstructing exact frequency from FFT bin phase
Phase vocoder effects:
  FFT-based frequency detector
  Robotisation (phase zeroing)
  Whisperisation (phase randomisation)
  Pitch shifting
[images: wikipedia]

## Slide 2: Sine wave in the frequency domain: task
Task: run the example project fft-sine
  This project takes FFT of a sine wave and displays the spectrum in the GUI
    Block-based processing in render.cpp
  Adjust the frequency of the oscillator in the GUI: what happens to the spectrum?
    By default, the sine is exactly on an FFT bin frequency
    After you adjust it, the frequency will fall between FFT bins
  You can change the FFT size at the top of render.cpp

## Slide 3: Sine wave in the frequency domain
x[n]
What does the FFT of a single sine wave look like?
  Let’s suppose its frequency exactly matches a bin: 2πk/N for some k
  This means that an integer number of oscillations fit in the window
...
Xk
(lower half)
All energy is in one frequency bin
All other bins 0 (except mirror image above Nyquist)
Magnitude is constant no matter where the window starts
Phase may change depending on window location

## Slide 4: Sine wave in the frequency domain
What if frequency doesn’t exactly match any bin? We’ll see two effects:
  Energy smears out across all the other frequency bins (we’ll see why shortly)
  Phase is likely to be different on each successive hop
    If we’re clever, we can reconstruct the exact frequency based on the phase changes!
x[n]
Non-integer number
of periods
Xk
(lower half)
Energy spills over into
other bins, especially close neighbours

## Slide 5: Reconstructing exact frequency
We can estimate the exact frequency of a sine wave from the FFT
  Even though the FFT only has bins at fixed, regularly spaced frequencies!
To do this, we will need two hops
  Two snapshots of the signal taken a known length of time apart
Key point: frequency is the derivative of phase
  or in discrete time:
  We can write out the first-order difference:
  Or generalising over a hop of H samples:
y

## Slide 6: Reconstructing exact frequency
Calculating frequency from phase in discrete time:
  In discrete time, frequency 𝜔 is normalised between 0 and 2π;
  Assumes unwrapped phase (i.e. always increasing, not constrained 0-2π)
We can invert this formula to calculate phase shift based on frequency:
  For a DFT of size N, we know bin k has a frequency of 2πk/N
  For a sine wave of exactly the bin frequency, this is the expected phase shift over 1 hop:
  By subtracting off this expected phase shift, the remainder will tell us whether the actual frequency is higher or lower than the bin frequency

## Slide 7: Reconstructing exact frequency
First we calculate the phase remainder:
Then use remainder to calculate the deviation from the bin centre frequency:
  We should wrap the phase to be between -π and π (i.e. the principal argument)
Finally, we can rearrange to get the exact frequency of our sine wave:
  We could also calculate in terms of (fractional) FFT bins
    Use the fact that bins are spaced 2π/N apart in frequency
measured phase values from bin k on two successive hops
centre frequency of bin k
multiplied by the hop size
centre frequency of bin k (= 2πk/N)
fractional bin number
of the sine wave

## Slide 8: Reconstructing exact frequency: code
Effectively, we are predicting how far the phase ought to advance from one hop to the next, then comparing the actual measured values
  Phase advancing farther means a higher frequency (compared to the bin frequency)
  Phase advancing less far means a lower frequency
What do we need to implement this in code?
  A global (or static) variable to hold the phase of each bin
    Saving each bin implies an array
    This is very similar to saving previous values of x[n] or y[n] for a filter (see Lecture 8)
  A function to wrap the phase to the range -π to π
  Implement the calculations inside of our process_fft() function
    Write a for() loop iterating across each bin
y
prediction
ECS7012P Music and Audio Programming • Week 10b

## Slide 9: Reconstructing exact frequency: task
Task: in fft-sine, write the code to work out the exact frequency of each bin
  Implement these formulas:
  Remember you will need a global or static array to hold the previous phases
  The GUI will display the frequency of the bin with highest magnitude
  However, the same formula can apply to every bin regardless of magnitude
    In practice, we only look at the first half of bins because the DFT is conjugate symmetric
bin phase this hop
bin phase last hop
FFT
size
bin
number
hop size
wrapPhase()
written for you
bin centre frequency
(2πk/N)

## Slide 10: Choosing an FFT size
The previous formulas gave us one frequency component for each bin
  An FFT of size N has (N/2+1) unique bins after accounting for symmetry
  This tells us the maximum number of frequency components we can represent
Hence, the larger the FFT, the greater the frequency resolution
  Bins are spaced more closely together in frequency: 2πk/N
  Easier to resolve two closely-spaced frequency components of a signal
What’s the tradeoff?
N time-domain samples ↔︎ N frequency-domain bins
  Resolving short transient events within a long time window is difficult
  Frequency-domain processing tends to smear transients, distorting their shape
  Another tradeoff to large FFTs: longer latency
  These are fundamental mathematical limitations
Poor time resolution

## Slide 11: Choosing a hop size
How often should we take an FFT?
  Assuming we want to reconstruct signal, hop size H must be no more than FFT size N
Advantages of smaller hop sizes
  We get more frequent time snapshots of the signal
  Phase of each bin advances less from one hop to next,
  improving frequency estimation
  Some types of window need a hop size of N/2, N/3 or even less to reconstruct the signal
  Lower latency for phase vocoder effects
Disadvantages of smaller hop sizes
  More computationally expensive
  Hop sizes that aren’t integer division of FFT size can lead to artefacts on reconstruction
H = N
H = N/2
H = N/4

## Slide 12: Windowing
Overlap-Add process segments signal into finite-length windows
  These segments can have discontinuities at the edges (assuming 0 outside the window)
  We might not notice this if we just reconstruct the signal with no frequency-domain processing
  If we modify the signal, these sharp edges can lead to crackling or buzzing sounds
We can use a window function to taper the edges
  Pre-calculated shape that we multiply the segment by before FFT
H = N/4
sharp edges
Hann window

## Slide 13: Types of window function
Rectangular
Triangular (Bartlett)
Hann
Hamming
for

## Slide 14: Effects of windowing
Hann-windowed
spectrum
(frequency smearing)
Windowing lets us isolate a particular time segment of our signal
The cost is smearing of energy in the frequency domain
  Energy appears at frequencies where it doesn’t exist in the original signal
Each frequency component of the signal appears as a series of lobes
  Main lobe: a broad peak centred around the actual frequency
  Side lobes: secondary peaks at other frequencies
We typically want to minimise:
  Main lobe width
  Side lobe height
ideal signal
(all energy at one
frequency)
Main lobe width
(expressed in
frequency)
Side lobe height
(expressed in dB)
ECS7012P Music and Audio Programming • Week 10b

## Slide 15: Window spectra
Main lobe width: 8π/N
Side lobe height: -26.5dB
Rectangular
Triangular (Bartlett)
Hann
Hamming
Main lobe width: 4π/N
Side lobe height: -13dB
Main lobe width: 8π/N
Side lobe height: -31.5dB
Main lobe width: 8π/N
Side lobe height: -42.8dB
→ When in doubt: use a Hann window
ECS7012P Music and Audio Programming • Week 10b

## Slide 16: Coding a window
It is most efficient to pre-calculate the window when the program starts
  Then recalculate when settings change: window size, window type etc.
Store the window in an array (typically a global variable)
  Length of the array is equal to the window size
To calculate, use a for() loop to iterate over each sample of the window
To apply, multiply the signal by the window buffer frame-by-frame
  Could do this while unwrapping a circular buffer (see Lecture 18)
for(unsigned int n = 0; n < windowSize; n++) {
windowedSignal[n] = originalSignal[n] * windowBuffer[n];
}
const int windowSize = 1024;
float windowBuffer[gWindowSize];
for(unsigned int n = 0; n < windowSize; n++) {
windowBuffer[n] =
}
equation for window
ECS7012P Music and Audio Programming • Week 10b

## Slide 17: Visualising the effects of windowing
Let’s go back to our fft-sine project and see the window in action
Task: in fft-sine, implement a Hann window
  Change the frequency in the GUI so it doesn’t align with any bin
  What happens to the width of the main lobe?
  What happens to the side lobes?
  As a bonus, the Hann window should improve the frequency estimation!
Why didn’t we see the classic comb filter pattern?
  Because the window size is the same as the FFT size
  The FFT is effectively sampling the peaks of each lobe
Task 2: in setup(), change the window size to be a fraction of the FFT length
  Say 1/4 or 1/8 of the FFT length
  Now the lobes should be visible