## Slide 1
Spatial Audio
Part 3 – Binaural sound

## Slide 2: Precedence effect
  Step toward one speaker monophonic source will appear localised to that speaker
  Effect persists despite changes in volume between speakers!
Psychoacoustic phenomenon: precedence effect
  Spatial processing inhibited for tens of milliseconds after localised acoustic event
  Exploit this by inserting delay in an audio channel
Sounds from different locations arrive at ears at different times

## Slide 3: Precedence effect

## Slide 4: Gain and delay
Two primary tools for placing sounds in space
  > 1ms or > 30dB: sound localised to one source
Two simultaneous sounds
with level difference
Two equal amplitude sounds
with time difference

## Slide 5: Gain and delay
Joint control of panorama and precedence effects
  Use variable-length delay lines
gL(q)
DelayL(q)
gR(q)
DelayR(q)
x[n]
yL[n]
yR[n]
q

## Slide 6: Panning & Precedence Implementation
Sources placed in apparent location using
  delay
  amplitude
Sound from just one side
  1 ms delay
  >30dB amplitude difference between 2 equally spaced speakers
Source appear half way between center & speaker
  0.2ms delay between right & left speaker
  Approximately 6dB amplitude difference between right & left channels

## Slide 7: Transparent amplification
How to reinforce live sound?
Example: amplifying acoustic instruments on stage
  Want apparent sound sources to merge nicely, acoustically and visually, with sounds from acoustic instruments on stage
Possible solution: only front loudspeakers
  Sound is not uniform throughout space
Better solution: transparent amplification
  Feed rear speakers with delayed signal
  Ensures localisation to stage as long as live stage sound always arrives first
  Minimum delay depends on distance from stage
Minimum delay for room length L, speed of sound c
TD=L/c (sec)

## Slide 8: Head-related transfer function
Panning and precedence give azimuth cues
  Based on Interaural Time Difference (ITD) and Interaural Level Difference (ILD)
  What about elevation?
  How do we localise sound front-to-back?
Head-Related Transfer Function (HRTF)
  Torso, head and outer-ear perform elevation-dependent filtering of sounds before they reach inner ear
  Filtering effects resolve ambiguity in ITD and ILD
  Filtering can be artificially simulated

## Slide 9: HRTFs
HRTFs are unique
  But patterns emerge
HRTFs for 2 subjects
  Sound 2 meters to left of subject
  moved from ear level (0 degrees) to elevation 30 degrees above
    solid line: 0 degrees
    long dashes: 10 degrees
    short dashes: 20 degrees
    dotted line: 30 degrees

## Slide 10: Head shadowing
Head shadowing = sound travelling through or around head to reach inner ear
  Head can produce significant attenuation
  Also filtering effect, usually lowpass filter
    Model: diffraction of plane wave around rigid sphere
  Head shadowing can cause perception problems with linear distance and direction

## Slide 11: Head Shadowing and ITD
  a – effective radius of head
  q – azimuth
  a – position of the zero
HRTF
ITD – modelled as first order allpass filter

## Slide 12: Sound wave from distant source acts like plane wave, approaches spherical head of radius r from azimuth angle q.
q
rsinq
r
rq
rsinq
plane
wave
Path length difference d=rsinq+rq
Time difference Td=d/c, c is speed of sound
Typical adult head r=0.14/2 m
q=45o, Td=(0.07/343)(π/4+sin(π/4))=301µs
(300µs measured)
q=90o, Td=(0.07/343)(π/2+sin(π/2)) = 524µs
(400µs measured)
If head size changed to 18cm diameter,
q=90o, Td=(0.09/343)(π/2+sin(π/2))=674µs
(541µs measured)

## Slide 13: HRTF modeling ITD and ILD as a filter based on the input signal and azimuth angle.
H(z,q+p/2)
z-d(q+p/2)
H(z,q-p/2)
z-d(q-p/2)
X(z)
YL(z)
YR(z)

## Slide 14: Pinna reflections
Pinna (pl. pinnae) or auricle: outer part of the ear
  Important to sound localisation
  Reflect incoming sound in ways depending on source angle
Distinguishing front and back sources
  Sounds from front reflect off pinnae
  Sounds from back do not cause reflections
  Listening over headphones, sounds without reflections localised to back
    This includes most microphone recordings
Perception of height also depends on pinna reflections

## Slide 15: Pinna parameters
Pinnae provide multiple reflections
  Implemented digitally with tapped delay line
  Short echoes = notches in frequency domain
    Just like case with flanger
  Notch location is elevation-dependent
    Main perceptual cue for elevation
Formula for time delay of echoes:
Parameters for amplitude and time delay
n | rpn | An [samples] | Bn [samples] | Dn (Approx.)
2 | 0.5 | 1 | 2 | 1
3 | -1 | 5 | 4 | 0.5
4 | 0.5 | 5 | 7 | 0.5
5 | -0.25 | 5 | 11 | 0.5
6 | 0.25 | 5 | 13 | 0.5
rpn: amplitude of reflections
Dn adjusts to individual pinna characteristics

## Slide 16: Pinna echoes implemented as an FIR filter.
+
z-d1
c1
z-d2
c2
z-dn
cn
z-d3
c3
…
YL,R(z)
WL,R(z)

## Slide 17: HRTF Implementation
Based on head shadowing, ITD, pinna reflections
Parameters do not work equally well for all people
head shadowing/ITD most useful & important cue
pinna-reflector - linear interpolation for noninteger delay
  important when the delay is small
pinna cues
  reinforce perception of azimuth
  provide elevation cues
shoulder echo often omitted
  not particularly important
  unknown parameters
Filtering applied even when both azimuth & elevation angles =0
elevation harder to notice than azimuth cues
  HRTF parameters often need to be fine-tuned to a particular user’s ears.

## Slide 18: Sweeping
illusion of moving, rotating sound source about listener’s head
perform HRTF processing on small segment
overlap-add with another segment at slightly different azimuth or elevation angle
  does not perform processing on input
  attempts to smooth different output chunks
  360’ clockwise rotation, beginning behind user
  azimuth–10’ to 10’, elevation–60’ to 60

## Slide 19: Areas of research
Spatial system to HRTF mappings
HRTF datasets
Near field HRTFs
Finding individual HRTFs
Approximating typical HRTFs